1999 NEPOOL MARGINAL EMISSION RATE ANALYSIS

for

the nepool ENVIRONMENTAL PLANNING COMMITTEE

| Paula A. Hamel, Chairman | - | PG&E Generating Company |
| --- | --- | --- |
| Mark R. Babula, Secretary | - | ISO New England Inc. |
| Bruce W. Bentley | - | Central Vermont Public Service Corp. |
| Bruce Biewald | - | Synapse Energy Economics, Inc. |
| David B. Damer | - | Wisvest-Connecticut, LLC |
| Michael A. DiMauro | - | Mass. Municipal Wholesale Electric Co. |
| Scott S. Hodgdon, Asst. Secretary | - | ISO New England Inc. |
| Shawn V. Konary, Vice-Chairman | - | Mirant New England, LLC |
| Thomas Murrell | - | NSTAR Electric & Gas |
| William E. Nason | - | FPL Energy, LLC |
| Jacob J. Scheffer | - | Entergy Nuclear Generation Company |
| Kathleen M. Shanley | - | The United Illuminating Company |
| Cynthia Karlic-Smith | - | NRG – Middletown Operations |
| Mary R. Smith | - | All Energy Marketing Company, LLC |

by

ISO New England Inc.

April 2002

TABLE OF CONTENTS

Executive Summary	1

TABLE ES1 - 1999 Marginal Emission Rates (Lbs./MWh)	1

TABLE ES2 - 1999 Marginal Emission Rates (Lbs./MBtu)	1

BACKGROUND	2

METHODOLOGY	2

Models Used	2

Calculating Marginal Emissions	3

ASSUMPTIONS	4

RESULTS	5

1999 Marginal Heat Rate	5

Incremental Generation By State/Load Zones	5

TABLE 1 - 1999 Incremental Generation By State/Load Zones	5

1999 Marginal Emission Rates	6

TABLE 2 - 1999 Marginal Emission Rates (Lbs./MWh)	6

TABLE 3 - 1999 Marginal Emission Rates (Lbs./MBtu)	6

Calculated Historical Marginal Emission Rates	7

TABLE 4 – Calculated SO2 Marginal Emission Rates (Lbs./MWh)	7

TABLE 5 – Calculated NOx Marginal Emission Rates (Lbs./MWh)	7

TABLE 6 – Calculated CO2 Marginal Emission Rates (Lbs./MWh)	8

GRAPH 1 – Calculated SO2 Marginal Emission Rates	9

GRAPH 2 – Calculated NOX Marginal Emission Rates	10

GRAPH 3 – Calculated CO2 Marginal Emission Rates	11

Incremental Emissions by State/Load Zone and by Ozone & Non-Ozone Season	12

TABLE 7 - 1999 Incremental SO2 Emissions	12

TABLE 8 - 1999 Incremental NOX Emissions	13

TABLE 9 - 1999 Incremental CO2 Emissions	13

APPENDIX A	14

TABLE 10: 1999 NEPOOL Capacity by State and Unit Category	14

TABLE 11: New Capacity Added to New England During 1999	14

# Executive Summary

The NEPOOL Environmental Planning Committee (EPC) has conducted a study to analyze the impact that demand side management (DSM) programs have had upon New England Power Pool’s (NEPOOL) aggregate SO2, NOX and CO2 generating unit emissions.  The 1999 Marginal Emission Rate Analysis Report (MEA Report) provides an estimate of marginal SO2, NOX and CO2 emissions for calendar year 1999.  The results of the 1999 marginal emission rate calculations, in Lbs./MWh and Lbs./Mbtu, are shown in Tables ES1 and ES2.  The NEPOOL EPC has published MEA reports for calendar years 1993 through 1998.

### TABLE ES1 - 1999 Marginal Emission Rates (Lbs./MWh)

### TABLE ES2 - 1999 Marginal Emission Rates (Lbs./MBtu)

These values were developed using the PROSYM production simulation model under two scenarios.  The Reference Case scenario was meant to simulate, as closely as possible, the actual operation of the NEPOOL system during the year 1999.   To calculate the amount of additional (marginal) SO2, NOX, and CO2 emissions that would have been emitted if DSM programs were not in place, the second or Marginal Case was created by increasing all hourly loads by 500 MW (incremental load increase).  The difference in total emissions between the two cases was calculated in Lbs./MWh and the resultant values are noted above in Table ES1.  A Marginal Heat Rate was calculated using simulation results and used to convert the Marginal Emission Rate in Lbs./MWh to Lbs./MBtu.  The formula used to calculate the Marginal Heat Rate is:

1999 Marginal Heat Rate = (Marginal Case Fuel Consumption – Reference Case Fuel Consumption)

(Marginal Case Generation – Reference Case Generation)

The 1999 Marginal Heat Rate was calculated to be: 10.013 MBtu/MWh

# BACKGROUND

In early 1994, the NEPOOL Environmental Planning Committee (EPC) conducted a study to analyze the impact that demand side management (DSM) programs had on New England Power Pool’s (NEPOOL) NOX emissions in the calendar year 1992.  The results were presented in a report entitled, 1992 Marginal NOX Emission Rate Analysis, which was used to support applications for obtaining NOX emission reduction credits (ERCs) resulting from those DSM program impacts.  Such applications were filed under the Massachusetts ERC banking and trading program, which became effective on January 1, 1994.  The ERC program allows inventoried sources of NOX, VOCs, and CO2 in Massachusetts to earn bankable and tradable credits by reducing emissions below regulatory requirements.  One of the creditable activities is electric utility DSM programs installed since January 1, 1992.  In 1994, the 1993 Marginal Emission Rate Analysis (MEA Report) was published, which provided analysis on the impact of DSM programs on SO2, NOX and CO2 emissions for the calendar year 1993.  The MEA Report was also published for the years 1994 through 1998 to provide similar analysis.

The 1999 Marginal Emission Rate Analysis Report provides an estimate of the impact of DSM programs on NEPOOL’s SO2, NOX and CO2 emissions for the calendar year 1999.

# METHODOLOGY

## Models Used

For conducting the 1999 Marginal Emissions Analysis, ISO New England used the Henwood Energy Services, Inc. (HESI) standardized database platform called Electric Market Simulation System (EMSS™).  EMSS manages the data for the desired market and creates input files to support the chronological production simulation software, PROSYM™.  The PROSYM production simulation model was used to replicate, as closely as possible, actual 1999 NEPOOL system operations.  However, because PROSYM is a chronological simulation model, there are modeling limitations and it is not possible to exactly replicate the discrete hourly events that occurred historically, such as daily changes in fuel prices, sudden forced outages, and unit deratings.  PROSYM’s simulation of the 1999 NEPOOL system approximates the minimization of costs using the traditional short-run marginal cost based methodology.  The PROSYM production simulation model simulates the NEPOOL power system as a one-bus model and thus the impacts resulting from transmission constraints are not captured.

## Calculating Marginal Emissions

Marginal emissions are calculated by comparing two simulations.  The Reference Case was created to replicate, as closely as possible, the actual 1999 NEPOOL system operation.  To calculate the amount of additional (marginal) emissions that would have been emitted if DSM programs were not in place, a Marginal Case is created by increasing all hourly loads by 500 MW (incremental load increase).  The MEA Report was originally produced to estimate the impacts of DSM programs on the NEPOOL system.

The 1994 Report entitled, NEPOOL Forecast Report of Capacity, Energy, Loads and Transmission 1994-2009 (1994 CELT Report), identified 1994 aggregate summer DSM programs in the amount of 1,034 MW.  The reason why an incremental 500 MW was originally used to estimate the impacts from DSM programs was that that amount was an average or in-between point.  Marginal emission rates could have been calculated for the first (1) MW of incremental load and could also have been calculated for the 1,034 MW of incremental load.  In 1994, the NEPOOL Environmental Planning Committee (EPC) decided to model the average effects of not having DSM programs at the average or in-between point of 500 MW incremental load.  Additionally, the 500 MW incremental load has been used in all MEA Reports since 1994, and thus provides a consistent base line for historical observations.  The 1999 Report entitled, NEPOOL Forecast Report of Capacity, Energy, Loads and Transmission 1999-2008 (1999 CELT Report), identifies 1999 summer DSM programs totaling 1,468 MW and winter DSM programs totaling 1,527 MW.

ISO New England dispatches all the generating units in NEPOOL (New England) economically to meet the hourly load and operating reserve requirements.  This means that multiple units may increase output in response to an increase in load.  Therefore, there is no single marginal unit that can be identified at any given time.  Rather, typically there are multiple marginal units located throughout the six New England states.

This report calculates 1999 NEPOOL marginal SO2, NOX, and CO2 emission rates that are expressed in both Lbs./MWh and Lbs./MBtu.  Also included, by state, is incremental tons of emissions and energy consumption.  This data is calculated by increasing the actual 1999 NEPOOL loads by 500 MW in all hours.  Based on a comparison between the two simulations, Reference Case vs. Marginal Case, monthly differences in energy output and the corresponding SO2, NOX and CO2 emissions are then determined.  These marginal emission rates are based on actual fuel use in 1999 and other discretely modeled system conditions.  Caution should be exercised in using this information for years other than 1999.  It should also be noted that although Reference Case simulations approximately match actual operation, the simulations are run on a single-bus model and are subject to differences from actual hourly dispatch.  The final hourly NEPOOL marginal emissions are divided into the four time-periods described below.

- On-Peak Ozone Season (where the Ozone Season is defined as occurring from May 1 to September 30) consisting of all weekdays between hour beginning 8 A.M. and hour beginning 9 P.M. from May 1 to September 30.

- Off-Peak Ozone Season consisting of all weekdays between hour beginning 10 P.M. and hour beginning 7 A.M. and all weekends from May 1 to September 30.

- On-Peak Non-Ozone Season consisting of all weekdays between hour beginning 8 A.M. and hour beginning 9 P.M. from January 1 to April 30 and October 1 to December 31.

- Off-Peak Non-Ozone Season consisting of all weekdays between hour beginning 10 P.M. and hour beginning 7 A.M. and all weekends from January 1 to April 30 and October 1 to December 31.

# ASSUMPTIONS

The key parameters and assumptions modeled within the 1999 Marginal Emissions Rate Analysis are highlighted below:

- NEPOOL DSM programs for 1999 have been modeled at the average aggregate of 500 MW in all hours.

- Actual historical hourly loads for 1999 were modeled for the NEPOOL system.

- The actual hourly net interchange with external systems, New York, New Brunswick, and Hydro-Quebec, was netted out from the actual historical hourly NEPOOL loads.  This results in the modeling of native NEPOOL load and generation only.  NEPOOL pumped-storage pumping load is included within the hourly NEPOOL loads.

- To explicitly model generating unit annual maintenance outages of three consecutive weekdays or longer (scheduled maintenance), generator maintenance that was recorded in the ISO New England 1999 Annual Maintenance Schedule (AMS) was discretely incorporated into all modeling runs.

- Forced outages were modeled discretely within the maintenance schedule as they occurred in actuality.  This gives the best possible method for modeling the 1999 actual outage occurrences.

- For major dispatchable hydro-electric stations, all pumped storage facilities, and several large non-dispatchable or self-scheduled units, actual 1999 monthly energies were input into all modeling runs and those units were modeled as Limited Energy units.  All of the Limited Energy units were dispatched within PROSYM to meet their target 1999 actual monthly energies.  Dispatchable generators were operated according to system economics.

- For generating units with dual fuel capability, fuel-switching assumptions were based on the Environmental Protection Agency’s (EPA) raw hourly data and analyzed to distinguish between oil and gas-fired energy production.

- Fuel prices for generating units were defaulted to those defined within PROSYM’s Electric Market Simulation System (EMSS) database.  In the EMSS database, the natural gas prices for the year 1999 were taken from the Henry Hub basin, and coal and fuel oil prices were extracted from 1999 FERC Form 423, a monthly report of cost and quality of fuels for electric plants.

- The generating unit emission rates were calculated from the 1999 actual emissions as reported to the US EPA’s Acid Rain Division and published in the EPA Emissions Scorecard 1999.  For those units which were not required to file with the US EPA Acid Rain Division, the assumed emission rates were either the rate noted in EPA’s E-Grid2000 data or provided through HESI’s database version 5.7.0.

# RESULTS

## 1999 Marginal Heat Rate

In past MEA reports, a fixed Marginal Heat Rate of 10.0 MBtu/MWh was used to convert from Lbs./MWh to Lbs./MBtu.  The 1999 Marginal Heat Rate was calculated from the results of the modeling runs.  Since heat rate is equal to fuel consumption divided by generation, the 1999 Marginal Heat Rate is defined as follows:

1999 Marginal Heat Rate = (Marginal Case Fuel Consumption – Reference Case Fuel Consumption)

(Marginal Case Generation – Reference Case Generation)

The 1999 Marginal Heat Rate was calculated to be:	10.013MBtu/MWh

To convert from Lbs./MWh to Lbs./MBtu, the 1999 Marginal Heat Rate is used as the global conversion factor for all calculations within this report.

## Incremental Generation By State/Load Zones

Table 1 shows the incremental generation, by state/load zones, for the Ozone Season and Non-Ozone Season time-periods.  Also shown is the percent of total NEPOOL generation increase, by state/load zones, resulting from a 500 MW increase in all NEPOOL hourly loads.

### TABLE 1 - 1999 Incremental Generation By State/Load Zones

## 1999 Marginal Emission Rates

Table 2 shows SO2, NOX and CO2 marginal emission rates in Lbs./MWh for the NEPOOL system for each of the four time-periods.  Table 3 shows the same information expressed in Lbs./MBtu.  As noted earlier, the 1999 Marginal Heat Rate of 10.013 MBtu/MWh was used as the global conversion factor.

The overall NEPOOL emissions and operating reserve for each state are very dependent on the specific units that are seasonally available to serve NEPOOL load.  Therefore, there could be wide variations in the seasonal emissions, primarily due to changes in unit availability, fuel consumption, and load level.

### TABLE 2 - 1999 Marginal Emission Rates (Lbs./MWh)

### TABLE 3 - 1999 Marginal Emission Rates (Lbs./MBtu)

## Calculated Historical Marginal Emission Rates

Tables 4, 5 and 6 show the calculated marginal emission rates for SO2, NOx, and CO2 in Lbs./MWh for the years 1993 through 1999. Graphs 1, 2 and 3 are graphical representations of Tables 4, 5 and 6, respectively.  There is a decrease in the marginal emission rates for NOx in 1995 primarily due to the implementation of NOx RACT regulations as required under Title I of the 1990 Clean Air Act Amendments.  There is an increase in the marginal emission rates for CO2 from 1997 to 1998, primarily due to the lower availability in nuclear generation, and the subsequent increase in fossil-fired generation to compensate for that loss.  For the most part, the NOx marginal emissions rate trend decreases into the year 1999, due to NEPOOL Participants’ commitment to lower NOx emissions.

### TABLE 4 – Calculated SO2 Marginal Emission Rates (Lbs./MWh)

### TABLE 5 – Calculated NOx Marginal Emission Rates (Lbs./MWh)

### TABLE 6 – Calculated CO2 Marginal Emission Rates (Lbs./MWh)

### GRAPH 1 – Calculated SO2 Marginal Emission Rates

### GRAPH 2 – Calculated NOX Marginal Emission Rates

### GRAPH 3 – Calculated CO2 Marginal Emission Rates

## Incremental Emissions by State/Load Zone and by Ozone & Non-Ozone Season

Tables 7, 8, and 9 show the calculated incremental SO2, NOX, and CO2 emissions, by state, for the ozone and non-ozone season time-periods, that would have been produced if the total NEPOOL load in all hours was increased by 500 MW.  Also shown is the percent of the total increase in emissions that would have correspondingly been produced within each state.

### TABLE 7 - 1999 Incremental SO2 Emissions

Notes:

1)	The Incremental Emissions are calculated by increasing the actual 1999 NEPOOL loads by 500 MW in all hours.

2)	Annual totals may not equal sum due to rounding.

### TABLE 8 - 1999 Incremental NOX Emissions

### TABLE 9 - 1999 Incremental CO2 Emissions

Notes:

1)	The Incremental Emissions are calculated by increasing the actual 1999 NEPOOL loads by 500 MW in all hours.

2)	Annual totals may not equal sum due to rounding.

# APPENDIX A

Table 10 shows the total NEPOOL capacity claimed for capability during the 1999 calendar year.  NEPOOL capacity listed in Table 10 was taken from ISO New England’s December 1999 Seasonal Claimed Capability (SCC) Report.  Table 11 identifies new units that went into commercial during the 1999 calendar year.

### TABLE 10: 1999 NEPOOL Capacity by State and Unit Category

### TABLE 11: New Capacity Added to New England During 1999

Prepared for

NEPOOL

by

ISO New England Inc.

Customer Service:  (413) 540-4220

Website: http://www.iso-ne.com

# Footnotes

Henwood Energy Services, Inc.- EMSS version 4.3.20.

Henwood Energy Services, Inc.- PROSYM version 3.4.29.