## Slide 1
October 8, 2015 | nepool markets committee
Jon Lowell
Market development
Improving price formation and efficient dispatch
Resource Dispatchability Requirements

## Slide 2: Improving Price Formation and Efficient Dispatch
A number of recent market design efforts have focused on improving price formation, operational flexibility, and efficient dispatch outcomes. A partial list includes:
  Coordinated Transaction Scheduling
  Energy Market Offer Flexibility
  Fast Start Pricing
  DNE Dispatch
  DARD Pump Intertemporal Parameters
Several common threads tie these efforts together:
  Improved ISO ability to dispatch resources in accordance with economic offers specified by the Participant
  Prices more consistent with Participants’ economic preferences and with operational requirements
  Improved performance incentives resulting from those prices
One significant group of resources remains outside these improvements – “non-dispatchable” generators

## Slide 3: Current Non-Dispatchable Generation
Category | SCC MW | WCC MW | Nameplate MW
Intermittent – DNE Dispatchable | 378 | 527 | 1475
Intermittent – Other | 451 | 454 | 953
Non-Intermittent | 4,455 | 4,513 | 5,181
Settlement Only Resources | 264 | 202 | 887
Total | 5,548 | 5,696 | 8,497
Total (excluding DNE) | 5,171 | 5,169 | 7,021

## Slide 4: Non-dispatchable resources present three particular challenges and concerns
Non-dispatchable generation can adversely impact price formation and efficient dispatch
Current Intermittent Power Resource definition includes resources that are not inherently intermittent
Fixed (unpriced) transactions in the Day-Ahead Market can produce unintended outcomes

## Slide 5: ❶ Non-dispatchable generation adversely impacts price formation and efficient dispatch
Resources not under dispatch control can contribute to real-time congestion and prices that don’t reflect the congestion
In some cases, this requires System Operators to issue manual curtailment instructions to ensure reliable operation
  Manual curtailments are not reflected in real-time prices
  Real-time prices become inconsistent with operational requirements
When low loads combine with large amounts of non-dispatchable generation, Minimum Generation Emergencies become more likely and last longer

## Slide 6: ❶ Non-dispatchable generation adversely impacts price formation and efficient dispatch (cont.)
Today, many types of resources are non-dispatchable in real-time:
  Settlement Only Resources
  Intermittent Power Resources
  Nuclear
  External Transactions
  Demand Response
It is not uncommon to have more than 50% of online resources participating in the Real-Time Energy Market in a non-dispatchable status (see next slide)

## Slide 8: ❶ Non-dispatchable generation adversely impacts price formation and efficient dispatch (cont.)
When dispatchable and non-dispatchable resources are located in an export-limited local area, the burden of relieving real-time congestion falls first on the dispatchable resources
This leads to economically inefficient outcomes that can be inconsistent with state regulatory and energy policy goals, even when the value of Renewable Energy Credits are reflected in offer prices

## Slide 9: ❷ Current Intermittent Power Resource definition includes resources that are not inherently intermittent
The original Intermittent Power Resource definition reflected
  Differences in FCM qualification requirements and qualified capability determination based on technology
  Use of a renewable energy source
  Contractual status as a Qualified Facility
  Contractual requirements that restricted operational flexibility
FERC Order 764 defines “Variable Energy Resources” as:
    ”a device for the production of electricity that is characterized by an energy source that: (1) is renewable; (2) cannot be stored by the facility owner or operator; and (3) has variability that is beyond the control of the facility owner or operator.”
Resources historically registered as Intermittent Power Resources include technologies that do not fit the FERC definition:
  Biomass
  Coal
  Internal combustion

## Slide 10: ❷ Current Intermittent Power Resource definition includes resources that are not inherently intermittent (cont.)
Intermittent Power Resources are non-dispatchable today
  Note that wind and hydro will be DNE Dispatchable in April 2016
Intermittents other than wind, hydro and solar use thermal generating technologies that are capable of being controlled and dispatched
When located in export constrained local areas, they contribute to congestion
  Burden of relieving real-time congestion falls first on the dispatchable resources and may never impact non-dispatchable resources that contribute equally or more to the congestion
When congestion can’t be resolved through economic dispatch, manual curtailments are required to maintain reliability, leading to:
  Inefficient prices (congestion pricing likely goes away)
  Inefficient dispatch outcomes

## Slide 11: ❸ Fixed (unpriced) transactions in the Day-Ahead Market can produce unintended outcomes
Fixed load bids and exports can clear at prices well above the Participant’s actual willingness-to-pay
Self-scheduled generation and imports can clear at prices below the offer floor
These outcomes:
  Rely on administrative pricing rules to clear the Day-Ahead Market
  Are seldom anticipated or desired by the Participant
  Produce “scary”1 Day-Ahead prices that are not transparent and do not reflect true preferences
  Increase the divergence between Day-Ahead commitment schedules and the resources actually needed to meet real-time load
1“Scary” is an imprecise term referring to Day-Ahead prices much higher than buyers’ true
willingness to pay or much lower than sellers true willingness to accept.

## Slide 12: Anticipated Schedule
ISO plans to come back to the Markets Committee in November and December depending upon the extent of comments and feedback from stakeholders
Timing of when proposal will be finalized for a vote and implemented will be determined based upon the discussion over the next several months