## Slide 1
NEPOOL Markets COMMITTEE | sep13, 2016
Hanhan Hammer
Market Development
Dispatch Lost Opportunity Cost Calculation Clarifications and Updates
NCPC Modifications for Subhourly Settlement

## Slide 2
NCPC Modifications for Subhourly Settlement: Summary | WMPP ID: 106
Proposed Effective Date: March 2017 | 
Three NCPC related issues have been identified during the Subhourly Settlement implementation
  Calculate Dispatch Lost Opportunity Cost NCPC credit to provide financial incentives for resources to follow the dispatch instruction
  Conform DARD pump NCPC calculations to be subhourly
  Clarify the tariff language to better describe Rapid Response Pricing Opportunity Cost NCPC calculation for DARD
NCPC modifications will be implemented concurrently with Subhourly Settlement changes in March 2017

## Slide 3: Dispatch Lost Opportunity Cost Proposal
Calculate Dispatch LOC NCPC credit to provide the financial incentives for resources to follow the dispatch instruction when the DDP is lower than the EDP
All online dispatchable resources will be eligible, except:
  Resources providing regulation during the interval
    Regulation compensation already includes opportunity costs
  Resources that are postured
    Postured resources are paid Posturing NCPC credits
Subhourly settlement simulation from 6/1/2015 to 5/31/2016 shows the Dispatch LOC credit is about
  $1.77 M without the reserve revenue
  $1.81 M with the reserve revenue

## Slide 4: Dispatch LOC will be calculated subhourly to provide financial incentives to follow dispatch
Dispatch LOC is calculated for every 5-minute interval, using 5-minute energy quantity and 5-minute RT LMPs
Dispatch LOC = Max Profit – Actual Profit
  Max Profit = energy profit at EDP + reserve profit at EDP
    EDP is restricted by the physical capability, such as ramp rate and EcoMax
  Actual Profit = max (actual energy profit, energy profit at the DDP) + reserve payments
Dispatch LOC credit is adjusted down by the amount of the Rapid Response Pricing Opportunity Cost NCPC credit for the same interval
Dispatch LOC credit will be included in other NCPC credit calculations as a form of additional revenue

## Slide 5: Stakeholder Schedule
NCPC modifications will be implemented concurrently with Subhourly Settlement project which targets March 2017
  Calculate Dispatch Lost Opportunity Cost NCPC credit to provide financial incentives for resources to follow the dispatch instruction
  Conform DARD pump NCPC calculations to be subhourly
  Clarify the tariff language to better describe Rapid Response Pricing Opportunity Cost NCPC calculation for DARD
Committee and Date | Focus
Markets Committee: October-2016 | Review tariff language
Markets Committee: November-2016 | Request vote on proposal
Participants Committee: December-2016 | Request vote on proposal

## Slide 6
Hanhan Hammer
(413) 535-4049 | hhammer@iso-ne.com

## Slide 7: Appendix
Example of Dispatch LOC Calculation

## Slide 8: Example: Dispatch LOC for resources ramping down to respond to DDP
Actual Profit = $94 = Actual Revenue – Actual Cost
= {87.5 MW1 x $30/MWh – [25 MW x $10/MWh +(87.5 MW – 25 MW) x $20/MWh] }/12
Dispatch LOC = $10 = Max Profit – Actual Profit = $104 – $94
187.5 MW is the 5-minute integrated quantity for the interval, calculated as [100 MW + (100 MW – 5 MW/min x 5 minute)]/2
For interval beginning t = 0, EDP = 100 MW
Max Profit = $104 = Revenue at EDP – Cost at EDP
= {100 MW x $30/MWh – [25 MW x $10/MWh + (100 MW – 25 MW) x $20/MWh]}/12