## Slide 1
May 8-9, 2018
REVISION 1
Deborah Cooke
(413) 540-4488 | dcooke@iso-ne.com
Increasing the transparency of Forward Capacity Market charges
Design Changes to the Allocation of
Forward Capacity Costs

## Slide 2
Project Title: Allocation of Forward Capacity Costs | WMPP ID: 112
Proposed Effective Date: June 1, 2020 (Capacity Commitment Period 11) | 
The allocation of costs to Capacity Zones were reviewed in light of the Marginal-Reliability Impact (MRI) based demand curves
The current method to allocate Forward Capacity Market costs is opaque
  Current method is not transparent: all FCM costs are reflected in a zonal blended (average) price, which can result in non-intuitive charges
  For example, charge rates in an export-constrained zone can exceed the charge rates in import-constrained zones and/or Rest-of-Pool

## Slide 3: Today’s Agenda
Additional discussion on the marginal value approach for allocating FCA and ARA costs
Follow-up to requests for additional examples
  Multi-year rate election
  FCA 11 and 12 estimated charge rates using the marginal value and NRCP methods
Overview of allocation proposals for the various capacity market components
Review Tariff language revisions

## Slide 4: Marginal Value approach to Cost Allocation
Further discussion on the proposed approach

## Slide 5: Some background on differences between zonal MRI demand curves and fixed limits in the FCA
There are no fixed limits (Local Sourcing Requirements, Maximum Capacity Limit) in the auction clearing
  With fixed limits capacity could “flow” until the constraint bound at which point no additional transfers were permitted
With MRI curves, capacity can “flow” across constrained boundaries as they never bind (i.e., restrict “flow”)
But the transfer is not always a MW-for-MW rate and not always at a constant ratio
  Capacity Clearing Prices reflect the value of capacity in each zone

## Slide 6: Zonal Capacity Obligation and allocation of costs
“Capacity Requirement” is not the same as ICR, LSR, or MCL
  This confusion is the primary reason for the name change to Zonal Capacity Obligation (new term used in today’s materials)
Zonal Capacity Obligation (ZCO) is an allocation mechanism
To balance settlements:
  Total CSO payments must equal Total ZCO charges
  But CSO x Clearing Price does not equal ZCO x Clearing Price; the difference must be accounted for in some manner
  NRCP approach uses CTRs
  Marginal value uses the clearing prices

## Slide 7: What is the interaction between CSO and ZCO? Example: Zonal CSO equals Zonal Capacity Obligation
ICCZ
ICCZ
ROP
ROP
ECCZ
ECCZ
Capacity purchased in each zone is set by the FCA
The ZCO in each zone is determined by
  1) Peak Load Contribution values; and
  2) Total pool CSO – not zonal CSO
  The following must remain true:
  Total CSO = Total ZCO
  Total payments = Total charges
Total Payments = Capacity Clearing Price x CSO
Total Charges = Charge Rate x ZCO
$
MW
In this example:
  Zonal CSO = ZCO
Zonal Charge Rate = Zonal Clearing Price
  Total Payments = Total Charges
CSO
ZCO

## Slide 8: How does the NRCP method account for differences in the zonal CSO and ZCO amounts?
ICCZ
ROP
  Charges are over- or under-collected in comparison to payments
  The difference (excess in this example) is re-allocated to certain zones through CTRs
ICCZ
ROP
ECCZ
Residual CTRs
Total Payments = Capacity Clearing Price x CSO
$
MW
In this example:
  Total Payments ≠ Total Charges
  Residual CTRs reduce payments in some zones, so that:
Total Payments = Total Charges – Residual CTR Allocations
Total Charges = Charge Rate x ZCO
CSO
ZCO

## Slide 9: How does the marginal value method account for differences in the zonal CSO and ZCO amounts?
ROP
In this example:
Charge rate reduced proportionately in all zones so that: Total Payments = Sum(ZCO x Charge Rate)
Total payments must still equal total charges
  Marginal value allocation accounts for this by
    Adjusting the charge rate in all zones proportional to the Capacity Clearing Price(s)
ICCZ
ROP
ECCZ
Total Payments = Capacity Clearing Price x CSO
ICCZ
$
MW
Total Charges = Charge Rate x ZCO
Marginal Value Charge Rates
CSO
ZCO

## Slide 10: An example can demonstrate these concepts
Table below summarizes the auction and load data used
  More realistic than previous examples
  Multiple zones with price separation
Inputs to the example:
Capacity Zones | CSO | Clearing Price | Total Payments | Peak Contribution Value | ZCO
 | MW | $/kW-mo. | $M/mo. | MW | MW
ICCZ | 10,000 | $8.692 | $87 | 9,700 | 14,242
ECCZ | 8,950 | $7.585 | $68 | 4,600 | 6,754
ROP | 15,555 | $8.185 | $127 | 9,200 | 13,508
Totals | 34,505 |  | $282 | 23,500 | 34,505
Calculated values reflect rounding

## Slide 11: Issue – total payments won’t equal total charges if the same rates are used
CZ | Total Payments | ZCO (A) | Clearing Price (B) | Zonal Peak Load Allocator (A x B)
 | $M/mo. | MW | $/kW-mo. | $M/mo.
ICCZ | $87 | 14,242 | $8.692 | $124
ECCZ | $68 | 6,754 | $7.585 | $51
ROP | $127 | 13,508 | $8.185 | $111
Totals | $282 | 34,505 |  | $286
CZ | Total Payments (A) | ZCO (B) | NRCP (C = A ÷ CSO) | Gross ZCO Charge (B x C)
 | $M/mo. | MW | $/kW-mo. | $M/mo.
ICCZ | $87 | 14,242 | $8.692 | $124
ECCZ | $68 | 6,754 | $7.585 | $51
ROP | $127 | 13,508 | $8.185 | $111
Totals | $282 | 34,505 |  | $286
Marginal Value
NRCP
The Zonal Peak Load Allocator (marginal value) is the same as the Gross ZCO charge (NRCP)
  Both are Capacity Clearing Price x ZCO
  Results in an over collection of costs (in this example)
How to address the difference?
  Reduce charges allocated to each Capacity Zones, based on clearing price (marginal value) or
  Allocate the difference to select Capacity Zones, using Capacity Transfer Rights (NRCP)
Calculated values reflect rounding

## Slide 12: Comparison of methods for allocating credit/charge differences to Capacity Zones
Capacity Zone | Zonal Peak Load Allocator | Zonal Peak Load Share (A = RPLACZ ÷ RPLAPool ) | Zonal Charges (B = A x Pool Pmts) | Share of Charges | Charge Rate (B ÷ ZCO) | Charge Rate vs. Price
 | $M/mo. | % | $M/mo. | % | $/kW-mo. | Ratio
ICCZ | $124 | 43.3% | $122 | 43.3% | $8.586 | 98.8%
ECCZ | $51 | 17.9% | $51 | 17.9% | $7.493 | 98.8%
ROP | $111 | 38.7% | $109 | 38.7% | $8.086 | 98.8%
Totals | $286 |  | $282 |  |  | 
Capacity Zone | Gross ZCO Charge (A) | Residual CTR Allocation (B) | Adj. ZCO Charge (C = A – B) | Share of Charges | Charge Rate (C ÷ ZCO) | Charge Rate vs. Price
 | $M/mo. | $M/mo. | $M/mo. | % | $/kW-mo. | Ratio
ICCZ | $124 | ($2.83) | $121 | 42.9% | $8.494 | 97.7%
ECCZ | $51 |  | $51 | 18.2% | $7.585 | 100%
ROP | $111 | ($0.64) | $110 | 39% | $8.138 | 99.4%
Totals | $286 | ($3.47) | $282 |  |  | 
Marginal Value
NRCP
Calculated values reflect rounding

## Slide 13: Also note the relationship of the Capacity Zone rates compared to the Rest of Pool
What does this mean?
  1 MW of capacity in ICCZ is worth 6% more than capacity in ROP; therefore
  1 MW of additional load in ICCZ will be charged a rate that is 6% more than 1 MW of load in ROP
Capacity Zone | Capacity Clearing Price | % of Rest of Pool Price | FCA Charge Rate | % of Rest of Pool Charge Rate
 | $kW-mo. | % | $kW-mo. | %
ICCZ | $8.692 | 106% | $8.586 | 106%
ECCZ | $7.585 | 93% | $7.493 | 93%
ROP | $8.185 | 100% | $8.086 | 100%

## Slide 14: Marginal value approach produces appropriate results with the new demand curves
Both the NRCP and marginal value methods adjust charges to account for variances between payments and charges
Marginal value method recognizes that there are no fixed transfer limits by reducing zonal charge rates proportionately
  Pro rata share of capacity charges (the “allocator”)
  As the zonal clearing prices are used in the calculation, it reflects the marginal benefit provided by capacity in each zone
Net Regional Clearing Price method assumes fixed requirements, binding constraints, and specific flows of capacity from one zone to another in the auction clearing by using Residual CTRs
  Allocated to certain zones based on zonal supply, estimated load, and differences in clearing prices

## Slide 15: Multi-Year Rate election
Further discussion of allocation of costs associated with multi-year rate elections
Additional examples requested:
  Allocation shares from the current FCA used to allocate the multi-year rate election variance
  Rate election in an import constrained zone that is modeled as part of the system in later commitment periods

## Slide 16: Requests from the April meeting
Further discuss the proposal to allocate variances associated with the multi-year rate election in future commitment periods, using the zonal allocators from the original year commitment period
Assess if the allocation of multi-year rate election variances should reflect updated peak load contribution values
Provide an example demonstrating the allocation of variances associated with the multi-year rate election when a resource electing the rate lock originally clears in an import-constrained zone, but the zone is not separately modeled in a later commitment period
1
2
3

## Slide 17: Using initial period values to allocate multi-year rate lock election variances reflects the original procurement
  Capacity costs up to the current period clearing prices are allocated using current commitment period values; this reflects the benefit the existing capacity provides in the current period
  In later commitment periods, the variance between the locked-in rate and the current commitment period clearing price must be allocated to Capacity Zones
Variance does not reflect any additional (or lesser) benefit provided in the current period
Using the initial commitment period clearing allocates this variance consistent with the original purchase of the capacity
1

## Slide 18
Year 1: 2,000 MW of new capacity located in ICCZ elects the multi-year rate lock and clears in the auction
Year 2: Variance to be allocated monthly is $10MM * ($13 /kW-mo. - $8 /kW-mo.) x 2,000
Year 2 allocator is updated using the Year 2 peak load
  Clearing price is from original auction
  * Assumes no Handy-Whitman adjustment
Assessment comparing costs using initial commitment period allocator updated with current period peak load
 | Year 1 |  |  | Year 2 |  |  | 
Capacity Zone | Clearing Price | Peak Load | Zonal Peak Load Share | Clearing Price | Peak Load | Zonal Peak Load Share | ZCO
 | $/kW-mo. | MW | % | $/kW-mo. | MW | % | MW
ICCZ | $13.000 | 11,118 | 52.74% | $8.000 | 9,708 | 52.72% | 14,040
ECCZ | $8.000 | 5,223 | 15.25% | $6.000 | 4,563 | 15.25% | 6,600
ROP | $8.300 | 10,570 | 32.01% | $7.000 | 9,237 | 32.03% | 13,360
Totals |  | 26,911 |  |  | 23,508 |  | 
2

## Slide 19: Using updated peak load values results in minor differences in the zonal allocations and charge rates
Multi-year rates are calculated using:
  Year 1 clearing prices and peak load amounts (5th column)
  Year 1 clearing prices and Year 2 peak load amounts (last column)
There differences in the zonal allocations and charge rates between the two approaches is very small
Calculated values reflect rounding
Inputs |  | Initial Period Peak Load Used |  |  | Current Period Peak Load Used |  | 
Capacity Zone | Multi-Year Rate Election Variance | Zonal Peak Load Allocator | Zonal Allocation | Multi-Year Rate Election Adjust. Rate | Zonal Peak Load Allocator | Zonal Allocation | Multi-Year Rate Election Adjust. Rate
 | $M/mo. | % | $M/mo. | $/kW-mo. | % | $M/mo. | $/kW-mo.
ICCZ | $10 | 52.74% | $5.351 | $0.381 | 52.72% | $5.349 | $0.381
ECCZ |  | 15.25% | $1.257 | $0.191 | 15.25% | $1.257 | $0.191
ROP |  | 32.01% | $3.392 | $0.254 | 32.03% | $3.394 | $0.254
Totals | $10 |  | $10 |  |  | $10 | 
2

## Slide 20: The use of initial period values to allocate multi-year rate election variances is appropriate
The variance was incurred in the initial auction clearing; using the initial period share continues to allocate the variance consistent with that procurement
The use of updated peak load values to allocate variances to each Capacity Zone has minimal impact on the resulting charge rate
  Adds additional complexity

## Slide 21: Multi-Year Rate Election: Additional Requested Example
  Multi-year rate elected in an import constrained zone that is not separately modeled in later commitment periods

## Slide 22
Example: Three Capacity Zones in Year 1 (ICCZ, ECCZ, and ROP); One Capacity Zone (ROP) in Year 2
Year 1: 2,000 MW of new capacity located in ICCZ elects the multi-year rate lock and clears in the auction
Year 2: Variance to be allocated monthly is $12MM * ($13 /kW-mo. - $7 /kW-mo.) x 2,000
  * Assumes no Handy-Whitman adjustment
Allocation of multi-year rate variance when zone is not modeled in later commitment periods
Capacity Zone Year 1 | Clearing Price Year 1 | Zonal Peak Load Share | Capacity Zone Year 2 | Clearing Price Year 2
 | $/kW-mo. | % |  | $/kW-mo.
ICCZ | $13.000 | 53% |  | 
ECCZ | $8.000 | 15% |  | 
ROP | $8.300 | 32% | ROP | $7.000
3

## Slide 23
Allocation to zones pro-rata using Peak Contribution MW from the previous calendar year
  Load zone values summed based on Capacity Zone modeling in the initial rate lock election year
The variance is allocated based on Capacity Zones
modeled in the original FCA
Year 1 |  | Year 2 |  |  |  |  | 
Capacity Zone | Zonal Peak Load Share | Capacity Zone | Multi-Year Rate Election Variance | Peak Load | Imputed ZCO | Imputed Zonal Allocation | Multi-Year Rate Election Adjust. Rate
 | % |  | $M/mo. | $K-mo. | MW | $M/mo. | $/kW-mo.
ICCZ | 53% |  |  | 9,708 | 14,040 | $6.3 | $0.451
ECCZ | 15% |  |  | 4,563 | 6,600 | $1.9 | $0.282
ROP | 32% | ROP | $12 | 9,237 | 13,360 | $3.8 | $0.285
Totals |  |  | $12 | 23,508 | 34,000 | $12 | 
Imputed ZCO (MW) = Peak Load Contribution MWZone ÷ Peak Load Contribution MWPool x Total CSOYear2 (MW)
Calculated values reflect rounding
3

## Slide 24: Estimated charge rates for Capacity Commitment Periods 11 and 12
Comparison of NRCP and Marginal Value Rates for each Capacity Commitment Period
Delineation of individual rate components where possible

## Slide 25: Some individual charge and adjustment rates can be compared using the marginal value vs. NRCP allocation methods
Individual charge/adjustment rates for Capacity Commitment Periods (CCP) 11 and 12 are shown on the following slides
Based on winter month (October) to demonstrate IPR rate
Could not include all rates
  ARA and MRA not available for these commitment periods
  Proposed allocation for the multi-year rate election only appears in CCP 12 (based on multi-year rate elections in CCP 11 onwards)
  Self-supply is embedded in the NRCP calculation
    Reduction to payments and CSO MW in the NRCP calculation
    CLO total is reduced in charge allocation (also impacts residual CTR fund)
  HQICC is embedded in the ZCO calculation
    Included in pool-wide ZCO value, then reduction to CLO of Interconnection Rights Holders (also impacts residual CTR fund)

## Slide 26: Estimated cost allocation rates for CCP 11
Capacity Zone | Capacity Load Obligation | FCA Charge Rate | Multi-Year Rate Election Adj. Rate | IPR Seasonal Capacity Adj. Rate | HQICC Charge Rate | Self-Supply Adj. Rate | Sum of Charge Rates
 | MW | $/kW-mo. | $/kW-mo. | $/kW-mo. | $/kW-mo. | $/kW-mo. | $/kW-mo.
SENE | 14,470 | $5.148 | $0.770 | $0.036 | $0.154 | $0.014 | $6.123
NNE | 6,618 | $5.148 | $0.017 | $0.036 | $0.154 | $0.014 | $5.370
ROP | 13,205 | $5.148 | $0.321 | $0.036 | $0.154 | $0.014 | $5.674
Values shown are approximations and do not reflect the final charges for the Capacity Commitment Period
The most recently published Peak Load Contribution values were used.
Capacity Zone | Capacity Load Obligation | FCA Charge Rate | Multi-Year Rate Election Adj. Rate | IPR Seasonal Capacity Adj. Rate | Net Regional Clearing Price | Residual CTRs Rate | Effective Charge Rate
 | MW | $/kW-mo. | $/kW-mo. | $/kW-mo. | $/kW-mo. | $/kW-mo. | $/kW-mo.
SENE | 14,574 | $5.304 | $1.028 | ($0.007) | $6.325 | $0.174 | $6.151
NNE | 6,667 | $5.085 | $0.015 | $0.164 | $5.264 | $0.000 | $5.264
ROP | 13,305 | $5.289 | $0.305 | $0.008 | $5.602 | $0.015 | $5.586
Marginal Value
NRCP
REVISED

## Slide 27: Estimated cost allocation rates for CCP 12
Values shown are approximations and do not reflect the final charges for the Capacity Commitment Period
The most recently published Peak Load Contribution values were used.
Marginal Value
NRCP
Capacity Zone | Capacity Load Obligation | FCA Charge Rate | Multi-Year Rate Election Adj. |  | IPR Seasonal Capacity Adj. Rate | HQICC Charge Rate | Self-Supply Adj. Rate | Sum of Charge Rates
 |  |  | Pre-FCA 11 | Post-FCA10 |  |  |  | 
 | MW | $/kW-mo. | $/kW-mo. | $/kW-mo. | $/kW-mo. | $/kW-mo. | $/kW-mo. | $/kW-mo.
SENE | 14,104 | $4.484 | $0.863 | $0.004 | $0.031 | $0.142 | $0.016 | $5.541
NNE | 6,296 | $4.484 | $0.019 | $0.004 | $0.031 | $0.142 | $0.016 | $4.695
ROP | 12,799 | $4.484 | $0.397 | $0.004 | $0.031 | $0.142 | $0.016 | $5.074
Capacity Zone | Capacity Load Obligation | FCA Charge Rate | Multi-Year Rate Election Adj. Rate | IPR Seasonal Capacity Adj. Rate | Net Regional Clearing Price | Residual CTRs Rate | Effective Charge Rate
 | MW | $/kW-mo. | $/kW-mo. | $/kW-mo. | $/kW-mo. | $/kW-mo. | $/kW-mo.
SENE | 14,202 | $4.636 | $1.188 | ($0.011) | $5.813 | $0.212 | $5.601
NNE | 6,342 | $4.449 | $0.018 | $0.149 | $4.616 | 0 | $4.616
ROP | 12,892 | $4.590 | $0.381 | $0.007 | $4.997 | $0.016 | $4.962
REVISED

## Slide 28: Overview of Capacity Market Cost Allocation
Summary of component charge rates and allocation methods

## Slide 29: Three main categories of capacity costs
Market Activity
Annual Reconfiguration Auction
(Three)
Monthly Reconfiguration Auction
Special Compensation Rules
CTR Pool-Planned Unit
Forward Capacity Auction
Multi-Year Rate Election
Capacity Transfer Rights
HQICC Capacity
Self-Supply
Intermittent Power Resource Seasonal Capacity
CTR Transmission Upgrade

## Slide 30: Overview of allocation methods for FCM costs
Current allocation method – using NRCP (an average of zonal capacity charges) and Capacity Transfer Rights will be replaced
New allocation methods fall into one of two main categories
  Marginal Value: Allocation of costs to Capacity Zones using weighting based on zonal load and Capacity Clearing Prices
    Modified Marginal Value: Marginal value method that uses the Capacity Clearing Price from the FCA in which resource’s new capacity originally cleared in the weighting
  Pro-rata allocation to Capacity Load Obligation:
    Pool-wide CLO: Equal allocation of costs to total pool Capacity Load Obligation
    Capacity Zone CLO: Equal allocation of costs to Capacity Load Obligation in a Capacity Zone

## Slide 31: Summary of FCM cost allocations
Component | Old Allocation | New Allocation | Explanation
Forward Capacity Auction | NRCP | Marginal Value | Reflects the marginal reliability benefit of capacity procured in the zone
FCA – Multi-Year Rate Election variance | NRCP | Modified Marginal Value | Reflects the marginal reliability benefit of capacity when it was originally procured
Annual Reconfiguration Auction | NRCP | Marginal Value | Reflects the marginal reliability benefit of capacity procured in the zone
Monthly Reconfiguration Auction | NRCP | Pro-rata to Pool CLO | No additional reliability benefit provided to the pool or a specific Capacity Zone
IPR Seasonal Clearing | NRCP | Pro-rata to Pool CLO | No additional reliability benefit provided to the pool or a specific Capacity Zone

## Slide 32: Summary of FCM cost allocations (cont.)
Component | Old Allocation | New Allocation | Explanation
Specifically Allocated Capacity Transfer Rights – Transmission Upgrades | CTRs | Pro-rata to Capacity Zone CLO | Transmission Upgrades increase the transfer capability to specific zones
Specifically Allocated Capacity Transfer Rights – Pool-planned units | CTRs | Pro-rata to Pool CLO | Reflects the full deliverability of capacity from these units throughout the pool
Self-Supply Obligations | NRCP | Pro-rata to Pool CLO | No additional reliability benefit provided to the pool or a specific Capacity Zone
HQICC | NRCP | Pro-rata to Pool CLO | No additional reliability benefit provided to the pool or a specific Capacity Zone

## Slide 33: Summary of Tariff Revisions

## Slide 34: Summary of Proposed Tariff Changes Definitions
Tariff Reference | Defined Term | Summary of Change
I.2.2 | Capacity Load Obligation | Streamlined definition, updated cross-reference
I.2.2 | Capacity Requirement * | Definition removed (replaced with “Zonal Capacity Obligation”)
I.2.2 | Capacity Transfer Rights | Streamlined definition, added cross-reference to Tariff language
I.2.2 | Coincident Peak Contribution | Replaced “power year” with “Capacity Commitment Period”, removed superfluous reference to Load Zones
I.2.2 | Estimated Capacity Load Obligation * | Replaced “Capacity Requirement” with “a Market Participant’s share of Zonal Capacity Obligation” to reflect the new defined term
I.2.2 | Zonal Capacity Obligation * | New defined term replacing “Capacity Requirement”
* Also to be presented to the Budget & Finance Committee as the term is used in Section VII.C of the Financial Assurance Policy

## Slide 35: Summary of Proposed Tariff Changes Capacity Charges
Tariff Reference | Section Name | Summary of Change
Table of Contents, III.13.7.5 | Charges to Market Participants with Capacity Load Obligations | Updated to reflect new sections and revised section numbers
III.13.7.1.3 | Export Capacity | Updated cross-reference
III.13.7.5.1 | Calculation of Capacity Charges Prior to June 1, 2020 | New section number. Indicated this section applies to Capacity Commitment Periods beginning prior to June 1, 2020
III.13.7.5.1.1 | Calculation of Capacity Charges On and After June 1, 2020 | New section describing the FCM charge calculations for Capacity Commitment Periods beginning on or after June 1, 2020
III.13.7.5.1.1.1 | Forward Capacity Auction Charge | New sub-section describing the calculation for Forward Capacity Auction Charges
III.13.7.5.1.1.2 | Annual Reconfiguration Auction Charge | New sub-section describing the calculation for Annual Reconfiguration Auction Charges

## Slide 36: Summary of Proposed Tariff Changes Capacity Charges
Tariff Reference | Section Name | Summary of Change
III.13.7.5.1.1.3 | Monthly Reconfiguration Auction Charge | New sub-section describing the calculation for Monthly Reconfiguration Auction Charges
III.13.7.5.1.1.4 | HQICC Capacity Charge | New sub-section describing the calculation for charges associated with HQICCs
III.13.7.5.1.1.5 | Self-Supply Adjustment | New sub-section describing the calculation for adjustments associated with self-supplied resources
III.13.7.5.1.1.6 | Intermittent Power Resource Capacity Adjustment | New sub-section describing the calculation for adjustments associated with the seasonal capacity award to Intermittent Power Resources
III.13.7.5.1.1.7 | Multi-Year Rate Election Adjustment | New sub-section describing the calculation for adjustments associated with the multi-year rate election of new capacity resources

## Slide 37: Summary of Proposed Tariff Changes Capacity Charges
Tariff Reference | Section Name | Summary of Change
III.13.7.5.1.1.8 | CTR Transmission Upgrade Charge | New sub-section describing the calculation for charges associated with Specifically Allocated Capacity Transfer Rights for Transmission Upgrades
III.13.7.5.1.1.9 | CTR Pool-Planned Unit Charge | New sub-section describing the calculation for charges associated with Specifically Allocated Capacity Transfer Rights for Pool-Planned Units
III.13.7.5.2 | Calculation of Capacity Load Obligation and Zonal Capacity Obligation | Revised section number (previous: III.13.7.5.1) Replaced Capacity Requirement with Market Participant share of Zonal Capacity Obligation. Updated peak contribution values used to calculate ZCO for periods on or after June 1, 2020 Changed references from “load serving entity” to “Market Participant” Removed superfluous language

## Slide 38: Summary of Proposed Tariff Changes Capacity Charges
Tariff Reference | Section Name | Summary of Change
III.13.7.5.1.1 | HQICC Used in the Calculation of Capacity Requirements | Removal of section; adjustment to Zonal Capacity Obligation for HQICCs is described in III.13.7.5.2
III.13.7.5.1.2 | Charges Associated with Self-Supplied FCA Resources | Removal of section; adjustment to Zonal Capacity Obligation for Self-Supply FCA Resources is described in III.13.7.5.2
III.13.7.5.2.1 | Charges Associated with Dispatchable Asset Related Demands | Revised section number (previous: III.13.7.5.1.3)
III.13.7.5.3 | Excess Revenues | Revised section number (previous: III.13.7.5.2)

## Slide 39: Summary of Proposed Tariff Changes Capacity Transfer Rights
Tariff Reference | Section Name | Summary of Change
III.13.7.5.3(a) | Excess Revenues | Added versioning to indicate the section applies to Capacity Commitment Periods beginning prior to June 1, 2020
III.13.7.5.4 | Capacity Transfer Rights | Revised section number (previous: III.13.7.5.3)
III.13.7.5.4.1 | Definition and Payments to Holders of Capacity Transfer Rights | Revised section number (previous: III.13.7.5.3.1) Added versioning to indicate the section applies to Capacity Commitment Periods beginning prior to June 1, 2020 Minor clarifying edits to first paragraph Deleted final paragraph with calculations for the value of specifically allocated CTRs; calculations were moved to the applicable specifically allocated CTR sections (III.13.7.5.4.4(f) and III.13.7.5.4.5(b))

## Slide 40: Summary of Proposed Tariff Changes Capacity Transfer Rights
Tariff Reference | Section Name | Summary of Change
III.13.7.5.4.2 | Allocation of Capacity Transfer Rights | Revised section number (previous: III.13.7.5.3.2) Added versioning to indicate the section applies to Capacity Commitment Periods beginning prior to June 1, 2020
III.13.7.5.4.2(c) | Allocation of Capacity Transfer Rights | Moved section for Maine Export Interface to III.13.7.5.4.4(e)
III.13.7.5.4.3 | Allocations of CTRs Resulting From Revised Capacity Zones | Revised section number (previous: III.13.7.5.3.3) Added versioning to indicate the section applies to Capacity Commitment Periods beginning prior to June 1, 2020
III.13.7.5.4.4 | Specifically Allocated CTRs Associated with Transmission Upgrades | Revised section number (previous: III.13.7.5.3.4)

## Slide 41: Summary of Proposed Tariff Changes Capacity Transfer Rights
Tariff Reference | Section Name | Summary of Change
III.13.7.5.4.4(b) | Specifically Allocated CTRs Associated with Transmission Upgrades | Updated cross-reference
III.13.7.5.4.4(d) | Specifically Allocated CTRs Associated with Transmission Upgrades | Updated cross-reference
III.13.7.5.4.4(e) | Specifically Allocated CTRs Associated with Transmission Upgrades | New sub-bullet (e), moved from III.13.7.5.4.2(c). Deleted reference to the residual CTR fund.
III.13.7.5.4.4(f) | Specifically Allocated CTRs Associated with Transmission Upgrades | New sub-bullet for the calculation of payments for CTRs associated with Transmission Upgrades (moved from III.13.7.5.4.1) Deleted references in the calculation to administrative pricing

## Slide 42: Summary of Proposed Tariff Changes Capacity Transfer Rights
Tariff Reference | Section Name | Summary of Change
III.13.7.5.3.5 | Reserved | Removed reserved section
III.13.7.5.4.5 | Specifically Allocated CTRs for Pool-Planned Units | Revised section number (previous: III.13.7.5.3.6)
III.13.7.5.4.5(a) | Specifically Allocated CTRs for Pool-Planned Units | Added sub-bullet format Clarified calculation of CTRs to reflect current practice (use of most recent seasonal claimed capability amount, and adjustment for self-supply)
III.13.7.5.4.5(b) | Specifically Allocated CTRs for Pool-Planned Units | New sub-bullet for the calculation of payments for CTRs associated with Pool-Planned Units (moved from III.13.7.5.4.1)
III.13.7.5.5 | Forward Capacity Market Net Charge Amount | Revised section number (previous: III.13.7.5.4) Modified calculation to reflect the multiple CLO charges; added versioning for residual CTR funds

## Slide 43: Proposed changes align FCM Cost Allocation with MRI-based demand curves
Modifications to the FCM cost allocation will better reflect the value of capacity purchased using the MRI-based demand curves and enhance transparency
Three main areas for improvement
  Marginal value allocation of FCA and ARA costs
  Allocation of costs to individual Capacity Zones
  Introduction of individual charge rates for each component
Changes effective for the 2020/2021 Capacity Commitment Period (FCA 11)

## Slide 44: Proposed Stakeholder Schedule
Stakeholder Committee and Date | Scheduled Project Milestone
Markets Committee March 6, 2018 | Initial meeting: Overview of current allocation; discussion of issues and proposed solutions for allocating costs to Capacity Zones
Markets Committee April 10, 2018 | Second meeting: Allocation of certain charges to Capacity Zones; improvements to the transparency of Forward Capacity Market charges
Markets Committee May 2018 | Third meeting: Discuss feedback on proposal Review proposed Tariff language
Budget & Finance Committee May 2018 | Conforming change to Section VII.C. of the Financial Assurance Policy
Markets Committee June 2018 | Vote
Participants Committee June 2018 | Vote

## Slide 45
Deborah Cooke
(413) 540-4488 | dcooke@iso-ne.com

## Slide 46: Acronyms Used in this Presentation
ARA = Annual Reconfiguration Auction
CCP = Capacity Commitment Period
CLO = Capacity Load Obligation
CSO = Capacity Supply Obligation
CTRs = Capacity Transfer Rights
CZ = Capacity Zone
ECCZ = Export Constrained Capacity Zone
FCA = Forward Capacity Auction
FCM = Forward Capacity Market
HQICC = HQ Interconnection Capability Credit
ICCZ = Import Constrained Capacity Zone
IPR = Intermittent Power Resource
MRA = Monthly Reconfiguration Auction
MRI = Marginal Reliability Impact
NRCP = Net Regional Clearing Price
PPU = Pool-Planned Unit
ROP = Rest of Pool
TU = Transmission Upgrade
ZCO = Zonal Capacity Obligation

## Slide 47: Appendix – Additional Supporting Information
Additional example comparing marginal value and Net Regional Clearing Price cost allocation methods
Supporting data for base example in April 2018 materials
Monthly reconfiguration auction clearing with zonal price separation
Overview of current method for allocating costs associated with resources retained for reliability
1
2
3
4

## Slide 48: Additional example comparing marginal value and NRCP allocation methods
Change from main example (slides 10-12): zonal Peak Contribution Values
  ICCZ peak load increases by 1,500 MW (and now exceeds the CSO purchased in the zone)
  ECCZ peak load decreases by 500 MW
  ROP peak load decreases by 1,000 MW
The FCA clearing remains the same
Capacity Zones | CSO | Clearing Price | Total Payments | Peak Contribution Value | Zonal Cr
 | MW | $/kW-mo. | $M/mo. | MW | MW
ICCZ | 10,000 | $8.692 | $87 | 11,200 | 16,445
ECCZ | 8,950 | $7.585 | $68 | 4,100 | 6,020
ROP | 15,555 | $8.185 | $127 | 8,200 | 12,040
Totals | 34,505 |  | $282 | 23,500 | 34,505
1

## Slide 49: Additional example comparing marginal value and NRCP allocation methods (cont.)
Capacity Zone | Total Payments | ZCO | Zonal Peak Load Allocator | Zonal Peak Load Share | Zonal Charges | Share of Charges | Charge Rate | Charge Rate vs. Price
 | $M/mo. | MW | $M/mo. | % | $M/mo. | % | $/kW-mo. | Ratio
ICCZ | $87 | 16,445 | $143 | 49.8% | $146 | 49.8% | $8.540 | 98.2 %
ECCZ | $68 | 6,020 | $46 | 15.9% | $39 | 15.9% | $7.452 | 98.2 %
ROP | $127 | 12,040 | $98 | 34.3% | $97 | 34.3% | $8.042 | 98.2 %
Totals | $282 | 34,505 |  |  | $282 |  |  | 
CZ | Total Payments | ZCO | NRCP | Gross ZCO Charge | Residual CTR Allocation | Adj. ZCO Charge | Share of Charges | Charge Rate | Charge Rate vs. Price
 | $M/mo. | MW | $/kW-mo. | $M/mo. | $M/mo. | $M/mo. | % | $/kW-mo. | Ratio
ICCZ | $87 | 16,445 | $8.692 | $143 | ($4.28) | $139 | 49.1% | $8.432 | 97%
ECCZ | $68 | 6,020 | $7.585 | $46 |  | $46 | 16.2% | $7.585 | 100%
ROP | $127 | 12,040 | $8.185 | $99 | ($0.74) | $98 | 34.7% | $8.123 | 99.2%
Totals | $282 | 34,505 |  | $287 | ($5.03) | $282 |  |  | 
Marginal Value
NRCP
1

## Slide 50: Marginal value approach allocates costs to all Capacity Zones consistent with the marginal benefit provided
Marginal value
  Marginal reliability benefit of capacity reflected in the clearing price is also reflected in the charge rate
  Charge rate as a percentage of clearing price is the same in each zone
  Another way to look at this: the potential “over collection” is avoided by reducing the charges in each zone in proportion to the marginal cost of capacity in each zone
NRCP
ICCZ has a higher clearing price and higher capacity requirements (load) but lower share of overall charges – why?
  Residual CTR fund allocates most of the “over collection” back to this zone
Charge rates as a percentage of clearing price vary among zones
1

## Slide 51: Details supporting the base example presented at the April meeting *
Calculated values reflect rounding
* See: Slide 9, https://www.iso-ne.com/static-assets/documents/2018/04/a4_presentation_design_changes_allocation_forward_capacity_costs.pptx
Capacity Zone | CR | ARA CSO Transactions | ARA Clearing Price | ARA Credits / Charges | Reliability Peak Load Allocator | Reliability Peak Load Share | ARA Capacity Zone Costs | ARA Charge Rate
 | MW | MW | $kW-mo. | $K-mo. | $K/mo. | % | $K-mo. | $kW-mo.
Inputs |  |  |  |  | Calculations |  |  | 
ICCZ | 2,785 | (500) | $13 | ($6,500) | 36,202 | 57.2% | ($1,430) | ($0.513)
ECCZ | 726 | 0 | $8 |  | 5,812 | 9.2% | ($230) | ($0.316)
ROP | 2,664 | 500 | $8 | $4,000 | 21,310 | 33.7% | ($843) | ($0.316)
Total | 6,175 | 0 |  | ($2,500) | 61,529 | 100% | ($2,500) | 
Capacity Zone | CR | FCA CSO Credits | Capacity Clearing Price | Reliability Peak Load Allocator | Reliability Peak Load Share | FCA Capacity Zone Costs | FCA Charge Rate
 | MW | $K/mo. | $/kW-mo. | $K/mo. | % | $K/mo. | $kW-mo.
Inputs |  |  |  | Calculations |  |  | 
ICCZ | 2,785 | $24,000 | $12 | 32,471 | 56.6% | $30,541 | $10.967
ECCZ | 726 | $6,000 | $6 | 4,235 | 7.4% | $3,984 | $5.484
ROP | 2,664 | $24,000 | $8 | 20,706 | 36.0% | $19,475 | $7.311
Total | 6,175 | $54,000 |  | 57,412 | 100% | $54,000 | 
2

## Slide 52: Monthly reconfiguration auction clearing with zonal binding
Source: FCM 101 Capacity Supply Obligation Bilaterals and Reconfiguration Auctions, slide 39 https://www.iso-ne.com/static-assets/documents/2017/11/20171023-12-fcm101-cso-bilaterals-and-reconfiguration.pdf
3

## Slide 53: Allocation of costs associated with resources retained for reliability
Resource de-list bids may be rejected if the resource capacity is deemed necessary to maintain local reliability (“retained for reliability”)
These resources are paid at a Commission-approved Permanent or Retirement De-List Bid rate or based upon a cost-of-service agreement
Costs in excess of what the resource would have been paid based upon the FCA market clearing price are allocated separately to Regional Network Load within the affected Reliability Region
  Reliability Regions reflect major transmission constraints on the New England transmission system
No changes to the current allocation are proposed
4