## Slide 1
July 17-19, 2018| NEPOOL Markets Committee
Catherine McDonough
413.535.4027| cmcdonough@iso-ne.com
Enhance the ability of electric storage facilities to participate in the New England wholesale electricity markets
Enhanced Storage Participation

## Slide 2
Enhanced Storage Participation
WMPP ID: 122
Proposed Effective Date: Q1 2019
Resource Dispatchability changes (ER17-68-000) enhanced the participation rules for dispatchable storage facilities to better enable battery storage to fully participate
Additional changes are required to support the implementation of these changes to:
  Allow participants to manage their state of charge in the Energy Market
  Reduce the need to manually re-declare dispatch limits
  Enable full dispatch of facility (+/-) in sequential energy market dispatches
  Allow the proper accounting of spinning reserves
  Enable simultaneous Regulation and Energy Market participation
  Receive a single electronic dispatch instruction for the facility
  Extend NCPC credit rules to all Storage DARDs
Proposal also extends the current DARD and DARD Pump cost allocation rules to Storage DARDs

## Slide 3: Overview of Today’s Presentation
Proposed rule changes improve the ability of directly metered Continuous Storage Facilities to participate in New England’s wholesale electricity markets by acknowledging their physical capability
Additional changes are required to comply with FERC Order 841; we will introduce this subject today and begin a full discussion in August to meet the December filing date
ISO will continue to evaluate how storage (and other technologies) participate in the markets to determine whether additional enhancements may be required

## Slide 4: Summary of Tariff Changes
Additional Clean-Up Changes to June Tariff Redlines
Changes to redlines presented at the June Market’s Committee meeting are highlighted in yellow in the posted tariff documents
Changes were made to the following definitions
  Asset Related Demand, Controllable Behind the Meter Generation, Load Asset, Maximum Consumption Limit, Minimum Consumption Limit, Rapid Response Pricing Asset
Changes were also made to:
  Electric Storage Section: III.10.6 (a)-(h)
  Other Sections: III.1.7.19.2, III.1.7.19.2.1.2(b &c), III.1.7.19.2.3.2(b &c), III.1.10.1A (c, d & e), III.1.10.2, III.1.10.3, III.1.10.9 (e), III.2.4, III.3.2.2 (d), III.3.2.6 (a & b), III.9.5.2, III.10.3, III.14.2(a & b)

## Slide 5: Electric Storage Section
Additional Changes Shown in Blue

## Slide 6: Summary of Tariff Changes
Electric Storage (Section III.1.10.6)
A storage facility is a facility that is capable of receiving electricity from the grid and storing the energy for later injection of electricity back to the grid. A storage facility may participate in the New England Markets as described below.
(a) A storage facility that satisfies the requirements of this subsection (a) may participate in the New England Markets as an Electric Storage Facility. An Electric Storage Facility shall:
  (i) be registered as, and subject to all rules applicable to, a dispatchable Generator Asset (other than a Settlement Only Resource);
  (ii) be registered as, and subject to all rules applicable to, a DARD that represents the same equipment as the Generator Asset;
  (iii) settle its injection of electricity to the grid as a Generator Asset and its receipt of electricity from the grid as a DARD; and
  (iv) meet the requirements of either a Binary Storage Facility or a Continuous Storage Facility, as described in subsections (b) and (c) below.
More specific language

## Slide 7: Summary of Tariff Changes
Binary Storage Facility (Section III.1.10.6)
(b) A storage facility that satisfies the requirements of this subsection (b) may participate in the New England Markets as a Binary Storage Facility. A Binary Storage Facility shall:
  (i) satisfy the requirements applicable to an Electric Storage Facility;
  (ii) offer its Generator Asset and a DARD into the Energy Market as Rapid Response Pricing Assets specify in Supply Offers and Demand Bids a Minimum Run Time and a Minimum Down Time that may be changed through redeclaration requests and that shall be of no more than one hour each; and
  (iii) comprise one or more reversible hydraulic turbines.
Using existing defined term to simply provision

## Slide 8: Summary of Tariff Changes
Continuous Storage Facility (Section III.1.10.6)
(c) A storage facility that satisfies the requirements of this subsection (c) may participate in the New England Markets as a Continuous Storage Facility. A Continuous Storage Facility shall:
  (i) satisfy the requirements applicable to an Electric Storage Facility;
  (ii) be registered as, may provide Regulation as, and is subject to all rules applicable to, an ATRR that represents the same equipment as the Generator Asset and DARD;
  (iii) be capable of transitioning between the facility’s maximum output and maximum consumption (and vice versa) in ten 10 minutes or less;
  (iv) not utilize storage capability that is shared with another Generator Asset, DARD or ATRR;
  (v) specify in Supply Offers a zero MW value for Economic Minimum Limit and Emergency Minimum Limit (except for Generator Assets undergoing Facility and Equipment Testing or auditing); a zero time value for Minimum Run Time, Minimum Down Time, Notification Time, and Start-Up Time; and a zero cost value for Start-Up Fee and No-Load Fee;
Conform to Section III.1 usage
Clarifies that CFS can provide regulation as an ATRR

## Slide 9: Summary of Tariff Changes
Continuous Storage Facility (Section III.1.10.6)
(c) Continuous Storage Facility Requirements (continued)
  (vi) specify in Demand Bids a zero MW value for Minimum Consumption Limit (except for DARDs undergoing Facility and Equipment Testing or auditing) and a zero time value for Minimum Run Time and Minimum Down Time;
  (vii) be Self-Scheduled in the Day-Ahead Energy Market and Real-Time Energy Market, and operate in an on-line state, (that is, with all available electrical supply and consumption equipment continuously connected to the New England Control Area), by Self-Scheduling the facility’s Generator Asset and DARD in the Day-Ahead Energy Market and Real time Energy Market unless the facility is declared unavailable by the Market Participant; and
  (viii) be issued a combined dispatch control signal equal to the Desired Dispatch Point (of the Generator Asset) minus the Desired Dispatch Point (of the DARD) plus the AGC SetPoint (of the ATRR).
    Clarifies that self-scheduled is the default state unless the facility is declared unavailable and that “unavailable status” applies to entire facility

## Slide 10: Summary of Tariff Changes
Other Storage Participation Options (Section III.1.10.6)
(d) A facility registered as a dispatchable Generator Asset, an ATRR, and a DARD that each represent the same equipment must participate as a Continuous Storage Facility.
(e) A storage facility not participating as an Electric Storage Facility may, if it satisfies the associated requirements, be registered as a Generator Asset (including a Settlement Only Resource) for settlement of its injection of electricity to the grid and as a non-dispatchable Load Asset (including an Asset Related Demand) for settlement of its wholesale load.
  New provision to clarify that CSF rules apply to any storage resource that registers as a Generator Asset, DARD and ATRR
  Simplifies language regarding other option available as a load

## Slide 11: Summary of Tariff Changes
Other Storage Participation Options (Section III.1.10.6)
(f) A storage facility that is not registered as a Generator Asset (including a Settlement Only Resource) may, if it satisfies the associated requirements, be registered as a Demand Response Asset. (As described in Section III.8.1.1, a Demand Response Asset and a Generator Asset may not be registered at the same end-use customer facility unless the Generator Asset is separately metered and reported and its output does not reduce the load reported at the Retail Delivery Point of the Demand Response Asset.)
  Deleted because some found it confusing
  Added parenthetical phrase because a storage facility located behind a retail delivery point and registered as a (separately metered and reported) Generator Asset, can participate as a Demand Response Asset

## Slide 12: Summary of Tariff Changes
Other Storage Participation Options (Section III.1.10.6)
(g) A storage device facility may, if it satisfies the associated requirements, be registered as a component of either an On-Peak Demand Resource or a Seasonal Peak Demand Resource.
(h) An Electric Storage Facility or any other storage facility may, if it satisfies the associated requirements, provide Regulation pursuant to Section III.14.
  Change to indicate that a On-Peak or Seasonal Peak DR may consist of measures not entire facilities
  Simplifies this provision for clarity since a storage facility includes an Electric Storage Facility

## Slide 13: Other Tariff Changes

## Slide 14: Summary of Tariff Changes
Definitions
Asset Related Demand
  Change to clarify that while the term “one or more” applies to storage facilities, the term “end-use” does not
Controllable Behind the Meter Generation
  Deletes term ”Retail Delivery Point” because the definition is relevant for DARDs (non-storage), not just demand response assets
  Adds separately metered exception
  Clarifies the meaning of “emergency”
  The updated definition reads:
    Generation whose output can be controlled located at the same facility as a DARD or Demand Response Asset, excluding (1) generators whose output is separately metered and reported and (2)generators that cannot operate electrically synchronized to, and that are operated only when the facility loses its supply of power from, the New England Transmission System, or when undergoing related testing

## Slide 15: Summary of Tariff Changes
Definitions
Load Asset
  Adds “A Load Asset can be an Asset Related Demand, including a Dispatchable Asset Related Demand” to help readers connect these market constructs
Maximum Consumption Limit
  Uses acronym “DARD” in place of Dispatchable Asset Related Demand and in place of “Resource” in reference to “Offer Data”
  Changes parallel edits to Minimum Consumption Limit
Minimum Consumption Limit
  Wording changes to reduce confusion
Rapid Response Pricing Asset
  Change to clarify that the Minimum Down Time of a DARD must be one hour or less to qualify as a Rapid Response Pricing Asset (corrects oversight when the definition was created in 2015); eliminates reference to Notification Time and Start-Up Time because DARDs don’t submit
Notes: Adding Supply Offers to acknowledge the fact that the current Pump Storage Model is really a Fast Start Model on both the Supply and Demand Side

## Slide 16: Summary of Tariff Changes
Summary of Tariff Changes
III.1.7.19.2 Calculation of Real Time Designation
  Intro section deleted because now redundant
III.1.7.19.2.1.2 (b) & (c)
  Replaces word “lesser” with “minimum” because the comparison is now between three not two parameter values
  Corrects the term “CLAIM10” with what should have been “Ten-Minute Non-Spinning Reserve,” and CLAIM30 with what should have been “Thirty-Minute Operating Reserve.”
III.1.7.19.2.3.2 (b) & (c)
  Replaces word “lesser” with “minimum” because the comparison is now between three not two parameter values

## Slide 17: Summary of Tariff Changes
Changes to Section III.1 Market Operations
III.1.10.1A Energy Market Scheduling
  Deletes phrase “Operating Reserve or other services as applicable” in provisions that describe (c) Generator Asset’s Supply Offers, (d) DARD Demand Bids, and (e) Demand Response Resource Demand Reduction Offers because an energy market offer is an offer to provide energy (not reserves) or a bid to consume energy (not reserves)
  Consolidates items (i) and (ii) in provision (c) and re-numbers items
  Changes to (c)(v) and (d) (ii) to clarify that requirement is to keep all physical limits up to date
III.1.10.2 Pool Scheduled Resources
  Words deleted because they are unnecessary and made sentence difficult to read

## Slide 18: Summary of Tariff Changes
Changes to Section III.1 Market Operations
III.1.10.3 Self-Scheduled Resources
  Moves “Demand Response Resources shall not be Self-Scheduled” from introduction to the end of the first paragraph
  Deletes subsection (b) This language is unnecessary and confusing because many read it to mean that the offer price of a self-scheduled resource dispatched above its Economic Min based on economics is not considered in forming the LMP, which is incorrect.
    No replacement is necessary as Section III.2.5 makes it clear that only prices from resources that have offered to supply or consume an additional increment (or decrement) of energy are considered in LMP formation
III.1.10.9 Hourly Scheduling
  (e) Wording changes to improve clarity
    Now reads: “A Market Participant may cancel a Self-Schedule of a Continuous Storage Generator Asset or a Continuous Storage DARD only by declaring the facility unavailable“

## Slide 19: Summary of Tariff Changes
Changes to Section III.2 to Section III.3
III.2.4 Adjustment for Rapid Response Pricing Assets
  Deletes the term “minimum consumption time” because Minimum Run Time is the defined term used to convey the concept of minimum consumption time for DARDs
III.3.2.2(d)
  Updates internal reference
III.3.2.6 Emergency Energy
  (a) & (b) Adds language to indicate that Continuous Storage Generator Assets will be treated as Pooled-Scheduled (rather than as Self-Scheduled) for the purpose of allocating Emergency Energy Credits and Charges mirroring the same language used for NCPC cost allocation
  Removes reference to Storage DARDs which had been mistakenly included in previous tariff redlines

## Slide 20: Summary of Tariff Changes
Changes to Section III.9 to Section III.10.4
III.9.5.2 Forward Reserve Eligibility Requirements
  Corrects reference in provision (vii)
III.10.3(a) Real-Time Reserve Charges
  Corrects typos in formulas

## Slide 21: Summary of Tariff Changes
Changes to Section III.1.14 Regulation Market
III.14.2. (a) (ii) Regulation Capacity Physical Parameters
  Deletes “not a Settlement Only Resource” since the provision refers to Generator Assets that can provide regulation, which must have a Regulation Capacity of at least 5 MW, and because it may erroneously suggest that a Settlement Only Resource can provide regulation under (ii) 2.
  Deletes “facility” because it is not necessary and potentially confusing
III.14.2. (b) Regulation Registration and Technical Parameters
  Adds a facility “capable” of providing Regulation because the requirements apply even if a facility is not providing regulation
  Tightens up language in (iii); now reads: a facility that provides regulation
    “shall not be registered as both an ATRR and a dispatchable Generator Asset, nor as both an ATRR and a DARD, unless it is a Continuous Storage Facility (however, an ATRR may be located at the same facility as either or both a Generator Asset and DARD if the Generator Asset and DARD are separately metered and reported)”
  Numbering corrections in items (v) & (vi)
  Moves final sentence of III.14.3 to III.14.2 (b) (vi) (1)

## Slide 22: Summary of Tariff Changes
Additional Commentary on Changes Reviewed at June MC
Asset (Slide 25)
  Adds Tie-Line Asset as an asset type that was also inadvertently excluded
Asset Registration Process (Slide 25)
  The sentence “The Asset Registration process is posted on the ISO’s website” was removed from the definition of “Asset Registration Process.” While the statement is true, because posting to the web site has become standard practice, references to the ISO website are no longer necessary and such references are gradually being removed from the tariff.
Section III.1.10.1A (Slide 39)
  In sub-sections ( c) and (e), “shall“ was changed to “may” to indicate that Market Participants may (but are not required) to submit DA supply offers
  This change aligns with the current practice whereby only resources with Capacity Supply Obligations are required to offer day-ahead. (See, e.g., III.13.6.2.1.1, III.13.6.2.5.1)

## Slide 23: Stakeholder Schedule

## Slide 24: Expected Stakeholder Schedule
Enhanced Storage Participation
Stakeholder Committee and Date | Scheduled Project Milestone
Market Committee Discussion April 2018 | Discuss Proposal
Markets Committee Discussion May 2018 | Review Tariff Changes
Markets Committee June 2018 | Review Tariff Changes
Markets Committee July 2018 | Vote
Participants Committee August 2018 | Vote
Planned Effective Date: Q1 2019