## Slide 1
September 26, 2018| Westborough, MA
Stephen George
(860) 683-3299 | SGEORGE@iso-ne.com
Energy Emergency Forecasting and Reporting
REVISIONS TO OP-21 & OP-21A –
Energy Inventory Accounting and Actions During An Energy Emergency &
Generator Survey

## Slide 2
Emergency Energy Forecasting and Reporting
The proposal to revise OP-21 and OP-21A was initially presented at the July 12, 2018 Reliability Committee meeting and focused on:
Developing an energy forecasting and reporting framework to establish energy alert thresholds based on an energy assessment over the next 21 days of operation that includes fuel and emissions availability as well as anticipated fuel infrastructure availability and supplies
Establishing Forecast Alert Thresholds issued by the ISO based on its energy assessment
Using the forecasting and reporting process to inform the declaration of Energy Alerts and Energy Emergencies, which would allow for proactive responses in advance of an Energy Emergency declaration
OP-21 & OP-21A Revisions Overview
Proposed Effective Dates: October 2018

## Slide 3: Proposed Revisions
The proposed revisions to OP-21 reviewed with the committee fall into the following general categories:
Incorporation of Energy Emergency Forecasting and Reporting Process, including Forecast Alert Thresholds
Incorporation of criteria for declaration of Energy Alert and Energy Emergency
Modified data collection frequencies
Other revisions and clarifications
Additionally, revisions to OP-21A (Generator Survey) are being proposed to support the Energy Emergency Forecasting and Reporting Process

## Slide 4: Overview of Changes
A review of OP-21 and OP-21A redline changes made in addition to those initially presented at the August 1, 2018 RC meeting will be performed today.
The following slides highlight the most significant changes.
Gray text indicates language that was included in the initial OP-21 revision presented to the RC on 8/1 and red text indicates a subsequent revision.

## Slide 5: OP-21 Revisions Section I: Introduction
Location | Proposed Revision
Introduction | Inserted additional language: This OP also documents the responsibilities of Lead MPs of applicable resources for completion of OP-21, Appendix A - Generator Survey (OP-21A), related communications and reporting requirements, and expectations for response related to an ISO declaration of an Energy Alert or an Energy Emergency. Nothing in this OP shall relieve Lead MPs from their obligations under the Tariff.
Introduction (List of possible initiating conditions) | Added to list: Prolonged, significant reductions of capability to import power into the New England region

## Slide 6: OP-21 Revisions Section II: Process Overview
Location | Proposed Revision
II.A Data Collection Process Description | Inserted effective date for changes to data collection (generator survey) process: Effective October 29, 2018, at the periodicity specified in Sections III.A, III.B, and III.C below, ISO shall distribute a blank survey form, OP-21A, to the Lead MP of each applicable resource.
II.B Energy Emergency Forecasting and Reporting Process and Forecast Alert Thresholds | Inserted effective date for ISO’s Energy Emergency Forecasting and Reporting process: Effective November 26, 2018, or earlier if possible, ISO shall perform Energy Emergency forecasting and reporting…

## Slide 7: OP-21 Revisions Section II: Process Overview, cont.
Location | Proposed Revision
II.B Energy Emergency Forecasting and Reporting Process and Forecast Alert Thresholds | Inserted additional language: The Energy Emergency forecasts are non-binding as forecasted or expected conditions utilized in the development of the forecasts can change. It is the responsibility of the Lead MPs to take all actions to ensure that resources are able to meet applicable obligations under the Tariff.
II.B Energy Alert and Energy Emergency Declaration Criteria | Modified Energy Alert criteria (previously proposed criteria shown in redline format): ISO shall declare an Energy Alert, and take actions as described in Section III.B of this OP, when either of the following conditions exist: FEEA2 or FEEA3 is forecasted to occur in at least 1 hour on 1 or more consecutive days in days 6 through 21 of the 21-day energy assessment, or Any other reason(s) for which the ISO Chief Operating Officer (COO), or designee, determines that the actions described in Section III.B of this OP may mitigate the impact of an actual or forecasted energy deficiency. FEEA3 is forecasted for at least 1 hour on 1 or more consecutive days in days 6 through 21 of the 21-day energy assessment. *note that duplicate language has been added in Section III.B.

## Slide 8: OP-21 Revisions Section II: Process Overview, cont.
Location | Proposed Revision
II.B Energy Alert and Energy Emergency Declaration Criteria | Modified Energy Emergency criteria (previously proposed criteria shown in redline format): ISO shall declare an Energy Emergency, and take actions as described in Section III.C of this OP, when either of the following conditions exist: FEEA2 or FEEA3 is forecasted to occur in at least 1 hour on 1 or more consecutive days in days 1 through 5 of the 21-day energy assessment, or Shedding of firm load under OP-7 is occurring or is anticipated to occur due to an actual energy deficiency resulting from a sustained shortage of fuel availability or deliverability to, or sustained environmental limitations on some or several of New England’s resources, or Any other reason(s) for which the ISO COO, or designee, determines that the actions described in Section III.C of this OP may mitigate the impact of an actual or forecasted energy deficiency. *note that duplicate language has been added in Section III.C.
II.B Energy Alert and Energy Emergency Declaration Criteria | Inserted additional language: To the extent possible, ISO shall declare Energy Alerts and Energy Emergencies on a daily boundary. *note that similar language has been added in multiple locations in the OP

## Slide 9: OP-21 Revisions Section II: Process Overview, cont.
Location | Proposed Revision
II.E Data Retention Requirements | Modified existing/inserted additional language (previous language shown in redline format): ISO shall retain all data submitted on OP-21A for not less than 36 months. In recognition of the sensitive nature of the information provided on OP-21 A, and the unique nature of ISO’s request, ISO shall: Use the information provided on OP-21A submittals solely for the purposes of identifying and addressing prospective energy deficiencies or related concerns that may exist. ISO shall treat submitted data as Confidential Information in accordance with the ISO New England Inc. Transmission, Markets, and Services Tariff, Attachment D - ISO New England Information Policy.

## Slide 10: OP-21 Revisions Section III: Conditions
Location | Proposed Revision
III.A Normal Conditions - Energy Emergency Forecasting and Reporting | Inserted additional language: To the extent possible, for each instance where an Energy Emergency forecast alert threshold was met, the results shall include the reason(s) why the threshold was met. *note that similar language has been added in multiple locations in the OP

## Slide 11: OP-21 Revisions Section III: Conditions, cont.
Location | Proposed Revision
III.B Energy Alert Conditions – Energy Alert Actions | Inserted additional language: When an Energy Alert has been declared, ISO shall: Alert each LCC and surrounding Reliability Coordinator/Balancing Authority (RC/BA) of the Energy Alert. Alert each Lead MP of the Energy Alert via a posting to the ISO’s website. Alert New England state regulators and officials of the Energy Alert. Initiate daily data collection using OP-21A forms, and daily Energy Emergency forecasting and reporting. When an Energy Alert has been declared, each Lead MP shall evaluate actual and anticipated fuel supplies and environmental limitations and should consider taking action, as necessary, to replenish fuel supplies and/or mitigate environmental limitations. When an Energy Alert has been declared, each Lead MP and LCC shall evaluate scheduled maintenance or repair to transmission facilities or resources in the region that reduces the capability of a facility or resource to supply energy to the region and should consider taking action, if possible, to maximize availability of those facilities or resources.

## Slide 12: OP-21 Revisions Section III: Conditions, cont.
Location | Proposed Revision
III.B Energy Emergency Conditions – Energy Emergency Actions | Inserted additional language: When an Energy Emergency has been declared, ISO shall: Alert each LCC and surrounding Reliability Coordinator/Balancing Authority (RC/BA) of the Energy Emergency. Alert each Lead MP of the Energy Emergency via a posting to the ISO’s website. Alert New England State regulators and officials of the Energy Emergency. Report the Energy Emergency to the U.S. DOE, using Form OE-417. Initiate daily data collection using OP-21A forms, and daily Energy Emergency forecasting and reporting. Request that each dual-fuel generator scheduled to operate voluntarily switch to operation on the fuel source that is not in short supply. Implement specific capacity and load relief measures available through actions of OP-4, excluding requesting New England State Governors reinforce appeals for voluntary load curtailment. If actions 1-7 above do not result in the necessary relief from the forecasted Energy Emergency, or if there is insufficient time for those measures to provide relief, the following actions may be taken: Implement a New England State Governors appeal in accordance with OP-4: Request New England State Governors to reinforce appeals for voluntary electrical load curtailment and the Power Warning Implementation. Under extreme conditions, ISO shall seek reliability relief through load shedding actions available through implementation of OP-7. When an Energy Emergency has been declared, each Lead MP shall evaluate actual and anticipated fuel supplies and environmental limitations and should consider taking action, as necessary, to replenish fuel supplies and/or mitigate environmental limitations. When an Energy Emergency has been declared, each Lead MP and LCC shall evaluate scheduled maintenance or repair to transmission facilities or resources in the region that reduces the capability of a facility or resource to supply energy to the region and should consider taking action, if possible, to maximize availability of those facilities or resources.

## Slide 13: OP-21 Revisions Section III: Conditions, cont.
Location | Proposed Revision
III. Cancellation | Inserted additional language: To the extent possible, ISO will cancel Energy Alerts and Energy Emergencies on a daily boundary.

## Slide 14: OP-21A Revisions Generator Survey
Location | Proposed Revision
Notes between questions 2004 and 2005 | This survey is being sent to generators that ISO New England is aware of having the ability to burn oil or coal. If this generator is not capable of burning oil or coal, please explain what changes have been made at the bottom of this survey.

## Slide 15: Conclusion
The ISO is proposing revisions to the current OP-21 and OP-21A to support the Energy Emergency forecasting and reporting process which will trigger defined Energy Alerts and Energy Emergencies in order to proactively communicate potential energy deficiencies to regional stakeholders.

## Slide 16: Stakeholder Schedule
Stakeholder Committee and Date | Scheduled Project Milestone
July 12, 2018 Reliability Committee | Initial presentation
August 1, 2018 Reliability Committee | Review of proposed OP-21 and OP-21A Revisions
September 26, 2018 Reliability Committee | VOTE
October 4, 2018 Participants Committee | VOTE