## Slide 1
October 9-10,2018| NEPOOL Markets Committee
Catherine McDonough
413.535.4027| cmcdonough@iso-ne.com
Electric Storage Participation in Markets
FERC Order No. 841 Compliance

## Slide 2
FERC Order No. 841 Compliance
WMPP ID: 129
Filing Deadline: December 3, 2018
FERC Order No. 841 requires ISOs to establish a “participation model”(i.e., market rules) that facilitates the participation of Electric Storage Resources (ESRs) in RTO/ISO markets
  Effective date for the Order: December 3, 2019
Enhanced Storage Participation changes (WMPP ID: 122), approved by the Participants Committee on August 24, largely (but not completely) meet the requirements of the Order
Additional tariff changes are required to:
  Lower the minimum size requirement for the participation model
  Make the participation model available to all storage technologies

## Slide 3: Today: Summary of FERC Order No. 841 Compliance Filing
Definition of Electric Storage Resource
Creation of a Participation Model for Electric Storage Resources
Eligibility of Electric Storage Resources to Participate in the RTO/ISO Markets
Participation in the RTO/ISO Markets as Supply and Demand
Physical and Operational Characteristics of Electric Storage Resources
State of Charge Management
Minimum Size Requirement
Energy Used to Charge Electric Storage Resources
Proposed changes for compliance

## Slide 4: FERC Order No. 841 Compliance Filing Summary
  A. Definition of Electric Storage Resource
  Order: Defines electric storage resource as “a resource capable of receiving electric energy from the grid and storing it for later injection of electric energy back to the grid”
  ISO Compliance: Market Rule 1, Section III.1.10.6 (added as part of the Enhanced Storage Participation changes) defines a storage facility as follows:
    “A storage facility is a facility that is capable of receiving electricity from the grid and storing the energy for later injection of electricity back to the grid”

## Slide 5: FERC Order No. 841 Compliance Filing Summary
  B. Creation of a Participation Model for Electric Storage Resources
  Order: Requires ISOs to establish a “participation model consisting of market rules that, recognizing the physical and operational characteristics of electric storage resources, facilitates their participation in the RTO/ISO markets”; market rules should clearly specify qualification criteria, be available for all types of electric storage technologies, not preclude the use of existing models, and specify any required change to participation agreements
  ISO Compliance: Electric Storage Facility rules contained in Market Rule 1, Section III.1.10.6 describe the eligibility rules for (a)Electric Storage Facilities (ESFs), (b)Binary Storage Facilities (BSFs), and (c)Continuous Storage Facilities (CSFs)
  Will remove provision(b)(iii) so that any technology can qualify for Binary Storage Facility rules
  Provisions (e) to (h) describe participation options available to storage facilities not participating as Electric Storage Facilities
  No required change to existing participation agreements

## Slide 6: FERC Order No. 841 Compliance Filing Summary
  C. Eligibility of ESRs to Participate in the RTO/ISO Markets
  Order: Requires that electric storage resources using the participation model be eligible to provide capacity, energy and ancillary services that they are technically able to provide; electric storage resources must also be able to de-rate their capacity to meet the minimum duration requirement
  ISO Compliance: ESFs can provide all wholesale market products (capacity, energy, reserves, and forward reserves) and services purchased by ISO (e.g., black start and reactive power) as a Generator Asset if they can meet the technical requirements; ESFs can also provide spinning reserves and forward reserves as a Dispatchable Asset Related Demand (DARD); Binary Storage Facilities can provide regulation service as a Generator Asset and Continuous Storage Facilities can provide regulation service as an Alternative Technology Regulation Resource (ATRR)
  An ESF can de-rate its capability to qualify for the capacity market; a 10 MW/10 MWh ESF can be qualified at 5 MW

## Slide 7: FERC Order No. 841 Compliance Filing Summary
  D. Participation in the RTO/ISO Markets as Supply and Demand
  Order: Electric storage resources using the participation model must be able to set the market clearing price as a wholesale market seller or buyer; ISO must prevent conflicting dispatch signals and make electric storage resources eligible to receive make-whole payments
  ISO Compliance: ESFs can set the market clearing price when charging as a DARD and when discharging as a Generator Asset
  Binary Storage Facilities will receive a desired dispatch point (DDP) to charge as a DARD or to discharge as a Generator Asset, but not both at the same time; Continuous Storage Facilities receive one dispatch signal that combines the energy market DDPs with the regulation market SetPoint (any of which can be zero)
  ESFs will be eligible to receive day-ahead and real-time Net Commitment Compensation Credits (NCPC) as a DARD and Generator Asset

## Slide 8: FERC Order No. 841 Compliance Filing Summary
  E. Physical and Operational Characteristics of Electric Storage Resources
  Order: Participation model must account for 13 physical and operational characteristics (see Appendix A and B) through bidding parameters or other means; bid parameters used to account for these characteristics should be available in both the day-ahead and real time markets; participants should be able to update information (consistent with other participants’ ability to do so) to ensure that ISO can efficiently dispatch the system
  ISO Compliance: ISO will account for eight of the requisite characteristics through bidding parameters in the day-ahead energy market (DAEM)and real-time energy market (RTEM). See Appendix A, p. 31
  ISO will account for the other five characteristics (SOC, maximum SOC, minimum SOC, maximum charge time and maximum discharge time) using the telemetered values of Available Energy and Available Storage during the operating day
  Available Energy: MWhs of energy available for dispatch; accounts for the minimum SOC; caps discharge time during the operating day
  Available Storage: MWhs of unused storage available to be filled from a dispatch to charge; accounts for the maximum SOC; caps charge time during the operating day

## Slide 9: FERC Order No. 841 Compliance Filing Summary
  E. Physical and Operational Characteristics of ESRs (continued)
ISO Compliance: The day-ahead energy market is economically optimized over a 24-hour period based on the bids of market participants (14 hours ahead of the operating day) so the telemetered values of available storage and available energy during the operating day cannot be used to optimize the day-ahead energy market
ESFs have two bid parameters to account for the expected level of available energy and available storage in the day-ahead energy market
Maximum Daily Energy Limit: Maximum amount of MWhs that a Limited Energy Resource expects to be able to generate in the next operating day
Maximum Daily Consumption Limit: Maximum number of MWhs that the Storage DARD is expects to be able to consume in the next operating day
ESFs can use these parameters (along with other parameters in their Demand Bids and Supply Offers) to manage how they clear in the DAEM

## Slide 10: FERC Order No. 841 Compliance Filing Summary
F. State of Charge Management
  Order: Must allow electric storage resources that use the participation model to self-manage their state of charge (SOC)
  ISO Compliance: ESFs will self manage their state of charge using their Demand Bids and Supply Offers in the real-time energy market and in the day-ahead energy market
  Telemetering Available Energy and Available Storage during the operating day will make it easier for ESFs to manage their state of charge in the RTEM and help to ensure that dispatch limits are set to ensure a feasible dispatch
  ESFs can also use a “limited-energy limit” and “self-dispatch” to help manage their state of charge in the RTEM
  Maximum Daily Energy Limit and Maximum Daily Consumption Limit will help ESFs to manage how they clear in the DAEM

## Slide 11: FERC Order No. 841 Compliance Filing Summary
G. Minimum Size Requirement
Order: Must allow electric storage resources 100 kW or larger to use the participation model; minimum size requirement applies to all minimum capacity requirements, minimum offer to sell requirements, and minimum bid to buy requirement
ISO Compliance: ISO will lower the minimum size threshold for Generator Assets, DARDs and ATRRs associated with Electric Storage Facilities from 1 MW to 100 kW
Because the Forward Reserve Market (FRM) is portfolio (not resource ) based, the ISO will also lower the minimum bid threshold for the FRM from 1 MW to 100 kW
See Appendix C (p 43-46) for more details

## Slide 12: FERC Order No. 841 Compliance Filing Summary
H. Energy Used to Charge Electric Storage Resources
  Order: The sale of electric energy from RTO/ISO markets to an electric storage resource that the electric storage resource then resells back to those markets must be at the wholesale locational marginal price (LMP)
  ISO Compliance: ESFs will pay the wholesale Locational Marginal Price (LMP) for MWh consumed and get paid wholesale LMP for the MWh supplied
  Storage facilities that do not use the ESF rules can participate in other manners (e.g., Generator Asset, Demand Response Assets) and be paid for energy (or demand reductions) based on the wholesale LMP; storage facilities that register as an Asset-Related Demand will pay the wholesale LMP for energy purchased from the ISO

## Slide 13: FERC Order No. 841 Compliance Filing Summary
H. Energy Used to Charge Electric Storage Resources (continued)
  Order: Electric storage resources should be exempt from transmission charges (normally allocated to loads) when they are dispatched by the RTO/ISO to provide ancillary services
PTO Compliance: Participating Transmission Owners (PTOs) will exempt Storage DARDs (that is, DARDs associated with ESFs) from Regional Network Service (Schedule 9) and Local Transmission Service (Schedule 21) charges because as dispatchable loads, Storage DARDs provide spinning reserves when they consume

## Slide 14: FERC Order No. 841 Compliance Filing Summary
H. Energy Used to Charge Electric Storage Resources (continued)
  Order: Requires ISO to directly meter electric storage resources so all energy entering and exiting can be measured by that meter. However, the Commission will consider alternate proposals
  ISO Compliance: The ISO will require resources that use the ESF rules to be directly metered. Storage facilities that do not use the ESF rules will have the same participation and metering options as other load or generators in New England

## Slide 15: Expected Stakeholder Schedule
FERC Order No. 841 Compliance
Stakeholder Committee and Date | Scheduled Project Milestone
Market Committee Discussion July 2018 | FERC Order 841 Requirements
Markets Committee Discussion August 2018 | Discuss Proposed Compliance Changes
Markets Committee September 2018 | Review Compliance Tariff Changes
Markets Committee October 2018 | Summary of Compliance Filing and Vote
Participants Committee November 2018 | Vote
Planned Effective Date: Q4 2019

## Slide 17: Appendix A
Tariff Changes Required for Compliance Filing and How ISO Rules Comply with Section IV.E of FERC Order 841
(September Markets Committee Meeting)

## Slide 18: Overview of Today’s Presentation
Review tariff changes for the compliance filing to:
  Add new definitions
  Lower the minimum size requirement for the participation model
  Make the participation model available to all storage technologies
  Effective date for DARDs to participate in the Regulation Market
  Additional Clean-up
Begin overview of ISO compliance approach with review of how Electric Storage Facility (ESF) rules account for specific physical and operational characteristics described in FERC’s Order No. 841 (Section IV.E)
Respond to participant question
Respond to Participant Question
Review Compliance Tariff Changes
How ESF Rules Account for Physical and Operational Characteristics

## Slide 19: Tariff Changes
To Comply with FERC Order No. 841

## Slide 20: FERC Order No. 841 Compliance Changes
Overview of Changes to Market Rule 1
New definitions
  Available Energy and Available Storage
  Maximum Daily Energy Limit
Lower the minimum size requirement for ESFs
  Definition of Asset Related Demand (ARD)
  Electric Storage Facilities Section III.1.10.6 (a)
  Regulation Market Section III.1.14 (a)
Enable all technologies to participate under ESF rules
  Electric Storage Facilities Section III.1.10.6
Effective date for DARDs to participate in Regulation Market
  Modify definition of Regulation Resources
  Sections III.14 .2,III.14 .3, III.14.6, and III.14.8
Clean-up changes
  III.1.7.19.2.3.2 (c), III.1.10.1A (c)(v) and (vii),
  III.9.7.1 through III.9.7.2 , III.9.7.2 (a)(i) and (ii)

## Slide 21: FERC Order No. 841 Compliance Changes
New Definitions
Available Energy
  is a value that reflects the MWhs of energy available from an Electric Storage Facility for economic dispatch”
Available Storage
  is a value that reflects the MWhs of unused storage available from an Electric Storage Facility for economic dispatch of consumption
Maximum Daily Energy Limit
  is the maximum amount of megawatt-hours that a Limited Energy Resource expects to be able to generate in the next operating day

## Slide 22: FERC Order No. 841 Compliance Changes
Lower the Minimum Size Requirement
Asset Related Demand
  Lowering the size requirement for Storage DARDs to 0.1 MW
Section III.1.10.6 (a)
  New subsection (i) that says ESF “should have the ability to inject 0.1 MW and consume 0.1 MW”
  Sections re-numbered to accommodate addition of a new sub-section
Section III.1.14.2 (a)(ii) 1
  Replace Continuous Storage Facility with Electric Storage Facility because Order No. 841 requires 0.1 MW minimum size requirement for all resources using electric storage participation model (not just Continuous Storage Facilities).
    This change makes it clear that the minimum size requirement for Generator Assets not associated with the ESF model has not changed

## Slide 23: FERC Order No. 841 Compliance Changes
Lower the Minimum Size Requirement (continued)
III.1.14.2 (a)(iii) 2
  Add new subsection to drop minimum Regulation Capacity of Continuous Storage ATRRs and of Generator Assets associated with Binary Storage Facilities to 0.1 MW
III.1.14.2 (a)(ii) 3
  Delete “as a Generator Asset” because it is unnecessary and confusing
  Add reference to new subsection 2 so that the 1 MW minimum to provide Regulation Capacity does not apply to ESFs
  Delete phrase “no less than” because it is unnecessary

## Slide 24: FERC Order No. 841 Compliance Changes
Make ESF Rules Available to all Storage Technologies
III.1.10.6 (b)
  Delete (iii) requirement that Binary Storage Facility must “comprise one or more reversible hydraulic turbines” because the Order requires the storage participation model to be applicable to any storage technology
  Delete “and” from subsection (ii) and add “and” to subsection (i) to account for the deletion of subsection (iii)

## Slide 25: FERC Order No. 841 Compliance Changes
Effective Date for DARDs to Participate in Regulation Market
As part of the ISO’s review of the storage changes and FERC Order No. 841, it was identified that the ISO does not have the systems in place to support the ability for a DARD to provide regulation
The ISO is proposing to delay the effective date of the implementation of this functionality because of the significant effort to implement and lack of any requests or interest for a participant to regulate as a DARD
The proposed tariff language for December 2019 removes DARDs from the list of Regulation Resources and deletes tariff provisions that relate to a DARD’s ability to provide regulation (III.14.3 (a)(ii), III.14.3(a)(iii) and III.14.8(d))
The removed provisions, as well as additional provisions (II.14.2(a) (ii)(2), III.14.6(b) related to the BSF changes, will be filed with a future effective date; the ISO is evaluating the effective date for when these changes could be implemented

## Slide 26: FERC Order No. 841 Compliance Changes
Clean-up Changes
III.1.7.19.2.3.2 (c)
  Delete the term “Fast Start” following “shall be calculated” and before the term “Demand Response Resource” to make language consistent with subsection (b) and (c)(ii) of this provision
III.1.10.1A (c)(v)
  Removes term “available energy” from language describing Limited Energy Resources since Available Energy is now a defined term that is not relevant to this provision
III.1.10.1A (c)(vii)
  Change to clarify that a Supply Offer for all Generator Assets associated with ESFs (not just Continuous Storage Facilities) shall also meet the requirements specified in Section III.1.10.6

## Slide 27: FERC Order No. 841 Compliance Changes
Clean-up Changes (continued)
III.9.7.1 through III.9.7.2
  Revised numbering to reduce confusion
III.9.7.2 (a)(i) and (ii)
  Adds reference to “Demand Response Resources that have been dispatched” to language describing Target Activation MW for TMNSR and TMOR because the references to Demand Response Resources were inadvertently deleted in the Enhanced Storage Participation changes

## Slide 28: Electric Storage Facility Rules
How They Comply with FERC Order 841’s Requirement to Account for Physical and Operational Characteristics
(Section IV.E of Order)

## Slide 29: FERC Order No. 841
How ISO Market Rules Comply
Definition of Electric Storage Resource
Creation of a Participation Model for Electric Storage Resources
Eligibility of Electric Storage Resources to Participate in the RTO/ISO Markets
Participation in the RTO/ISO Markets as Supply and Demand
Physical and Operational Characteristics of Electric Storage Resources
State of Charge Management
Minimum Size Requirement
Energy Used to Charge Electric Storage Resources
Today: Review Compliance with Section IV.E
Next Time: Additional Compliance Discussion

## Slide 30: FERC Order No. 841- Requirement (Section IV.E)
General
ISO/RTO must demonstrate how its Storage Participation Model accounts for thirteen physical and operating characteristics of electric storage resources (ESRs) through bidding parameters or other means (Appendix B describes each characteristic)
ISO/RTO can determine whether submission of information by the ESR is mandatory or discretionary; submission of information must be consistent with how ISO/RTO accepts information from other resources
If ISO/RTO adopts bidding parameters to account for the physical and operational characteristics, ISO/RTO must permit the resource to submit the parameters in the day-ahead and real-time markets
Allowing storage model users to provide updated information through any applicable bidding parameters (consistent with other participants’ ability to do so) will help ensure that the RTO/ISO has necessary information to efficiently dispatch the system

## Slide 31: Electric Storage Facility Rules
Account for the Requisite Characteristics in the Real-time Energy Market (RTEM)
Physical Characteristic | Bidding Parameter or Telemetered Value*
State of Charge (%) | Available Energy & Available Storage (MWh)*
Maximum State of Charge (%) | Available Storage (MWh)*
Minimum State of Charge(%) | Available Energy (MWh) *
Minimum Charge Limit (MW) | Minimum Consumption Limit (MW)
Maximum Charge Limit (MW) | Maximum Consumption Limit (MW)
Minimum Discharge Limit (MW) | Economic Minimum (MW)
Maximum Discharge Limit (MW) | Economic Maximum (MW)
Minimum Charge Time | Minimum Run Time for Storage DARD
Maximum Charge Time | Available Storage*
Minimum Run Time | Minimum Run Time for Generator Asset
Maximum Run Time | Available Energy *
Charge Ramp Rate | Manual Response Rate for Storage DARD
Discharge Ramp Rate | Manual Response Rate for Generator Asset
* State variables telemetered to ISO but not included in Supply Offers or Demand Bids

## Slide 32: Electric Storage Facility Rules
Account for State of Charge via Telemetered Values in RTEM
ESFs are required to telemeter their Available Energy and Available Storage to the ISO every 4 seconds
Available Energy is a value that reflects the MWhs of energy available from an Electric Storage Facility for economic dispatch
Available Storage is a value that reflects the MWhs of unused storage available from an Electric Storage Facility for economic dispatch of consumption

## Slide 33: Electric Storage Facility Rules
Telemetered Values Ensure a Feasible Dispatch in the RTEM
  The ISO generally runs its dispatch software every 10 to 15 minutes
  To ensure that the dispatch is feasible, the Maximum Consumption Limit must be re-declared in real time to ensure that an ESF can consume at this limit for 15 minutes based on its Available Storage MWh
The Economic Maximum parameter must be re-declared in real time to ensure that the ESF has enough Available Energy to sustain operation for one hour. Doing so, enables the ISO to co-optimize the supply of energy and reserves and to comply with the NPCC’s one hour duration requirement for reserves

## Slide 34: Electric Storage Facility Rules
Telemetered Values Ensure a Feasible Dispatch in the RTEM (cont.)
If an ESF opts to self-dispatch, the Economic Maximum must be re-declared to ensure that the ESF can discharge at this rate for 15 minutes
  If the self-dispatch MW is greater than the MW discharge rate that can be sustained for one hour based on Available Energy, no reserves will be counted on the ESF
Resources (including Limited Energy Resources) do not submit a maximum run time or maximum charge time in the RTEM
  The maximum run time for an ESF is determined by its Available Energy
  The maximum charge time for an ESF is determined by its Available Storage

## Slide 35: Electric Storage Facility Rules
Account for all Requisite Characteristics in Day-ahead Energy Market
The day ahead energy market is economically optimized over a 24-hour period based on the bids of market participants
ESFs can bid the same parameters into the day-ahead energy market (DAEM) as they can bid into the RTEM
ESFs have two bid parameters that can be used to account for available energy and available storage in the DAEM:
  Maximum Daily Energy Limit (MWh)
    Maximum amount of energy the participant wants to sell for the entire operating day
  Maximum Daily Consumption Limit (MWh)
    Maximum number of MWhs that the participant wants to buy for the entire operating day

## Slide 36: Response to Participant Question
Question: Can you confirm that a 1 MW/2 MWh storage resource, interconnected in front of the meter, would be able to qualify for 1 MW of Capacity, given the two hour audit, even though under the ISO’s automatic re-declaration of energy limits design, the resource would not be dispatched for 1 MW of energy for two hours?
ISO Response: If the storage device had 2 MWh of Available Energy at the beginning of the audit, the automatic re-declaration process would not hinder its ability to generate 1 MW for 2 hours. The Generator Asset would be placed into unit control mode (UCM) 3 (on line, non-dispatchable) at the beginning of the audit and would not be counted for reserves. This would enable the Generator Asset to discharge at 1 MW for two hours without regard to its re-declared Economic Maximum to meet the FCM audit requirement.

## Slide 37: Appendix B
Physical and Operational Characteristics to be Accounted for in Storage Participation Model (Section IV.E of FERC Order)

## Slide 38: Storage Participation Model
Must Account for the State of Charge (SOC)
Characteristic | Definition
State of Charge | The amount of energy stored in proportion to the limit on the amount of energy that can be stored, typically expressed as a percentage. It represents the forecasted starting State of Charge for the market interval being offered into.
Maximum State of Charge | A State of Charge value that should not be exceeded (i.e., gone above) when a resource using the participation model for electric storage resources is receiving electric energy from the grid (e.g., 95% State of Charge). *
Minimum State of Charge | A State of Charge value that should not be exceeded (i.e., gone below) when a resource using the participation model for electric storage resources is injecting electric energy to the grid (e.g., 5% State of Charge).*
*Note: These values may either static values based on manufacturer specification or dynamic values depending on the operational
characteristics of the resource (e.g. if it is providing multiple services and needs to reserve part of its state of charge for another service)

## Slide 39: Storage Participation Model
Must Account for the Dispatch Limits
Characteristic | Definition
Minimum Charge Limit | The minimum MW level that a resource using the participation model for electric storage resources can receive from the grid.
Maximum Charge Limit | The maximum MW quantity of electric energy that a resource using the participation model for electric storage resources can receive from the grid.
Minimum Discharge Limit | The minimum MW output level that a resource using the participation model for electric storage resources can inject onto the grid.
Maximum Discharge Limit | The maximum MW quantity that a resource using the participation model for electric storage resources can inject to the grid.

## Slide 40: Storage Participation Model
Must Account for Intertemporal Constraints
Characteristic | Definition
Minimum Charge Time | The shortest duration that a resource using the participation model for electric storage resources is able to be dispatched by the RTO/ISO to receive electric energy from the grid (e.g., one hour).
Maximum Charge Time* | The maximum duration that a resource using the participation model for electric storage resources is able to be dispatched by the RTO/ISO to receive electric energy from the grid (e.g., four hours).
Minimum Run Time | The minimum amount of time that a resource using the participation model for electric storage resources is able to inject electric energy to the grid (e.g., one hour).
Maximum Run Time* | The maximum amount of time that a resource using the participation model for electric storage resources is able to inject electric energy to the grid (e.g., four hours).
*May be required to ensure that the duration of the dispatch is feasible

## Slide 41: Storage Participation Model
Must Account for Ramp Rates
Characteristic | Definition
Discharge Ramp Rate | The speed at which a resource using the participation model for electric storage resources can move from zero output to its Maximum Discharge Limit.
Charge Ramp Rate | The speed at which a resource using the participation model for electric storage resources can move from zero output to its Maximum Charge Limit.

## Slide 42: Appendix C
Changes Required for Compliance Filing
(August Markets Committee Meeting)

## Slide 43: FERC Order No. 841
Participation Model Must Be Available to All Storage Technologies
The Electric Storage Facility (ESF) rules described in the recently proposed “Electric Storage” section of the tariff (Market Rule 1, Section III.1.10.6 (a through c) is a “storage participation model” that meets most of Order’s requirements
Under the ESF rules, a storage facility can participate as either a Binary Storage Facility (BSF) or a Continuous Storage Facility (CSF) depending on the facility’s physical characteristics
Any storage technology that meets the requirements can participate under the CSF rules, but the BSF rules are currently limited to only the pumped-storage hydro technology
As part of its compliance filing, the ISO will make the BSF rules available to all storage technologies
Other than the reduction in the minimum size requirement discussed below, no other changes to the BSF rules have been identified

## Slide 44: FERC Order No. 841
Minimum Size Requirement for Participation Model Must Be 100 kW
The Order states that its 100 kW minimum size requirement “applies to all minimum capacity requirements, minimum offer to sell requirements, and minimum bid to buy requirements” for electric storage resources that use the “participation model”
Order has no minimum size requirement with regard to MWhs of storage capacity
To comply with the Order, the ISO will lower the minimum size threshold for Generator Assets, DARDs and ATRRs associated with Electric Storage Facilities from 1 MW to 100 kW
Because the Forward Reserve Market (FRM) is portfolio (not resource ) based, the ISO will lower the minimum bid threshold for the FRM from 1 MW to 100 kW

## Slide 45: FERC Order No. 841
Implication of Lower Minimum Size Requirement for ESFs
Electric Storage Facilities (ESFs) can bid/offer a minimum of 100 kW as Generator Asset and/or DARD into the Day-Ahead Energy Market Real Time Energy Market
All Participants (including ESFs) can take on a 100 kW FRM obligation; Participants can already assign a DARD or Generator Asset in 100 kW increments to meet a FRM obligation
ESF Generator Assets can offer 100 kW of qualified capacity into the Forward Capacity Market (FCM)
ESFs can offer 100 kW of capacity into the Regulation Market
No change in ESFs ability to provide Black Start Service or VAR since there is no minimum size requirement to offer these services

## Slide 46: FERC Order No. 841
No Change to Bid/Offer Granularity in any Market
Resources can currently offer in:
  100 kW increments over the minimum size threshold in the energy and regulation markets
  1 kW increments over the minimum bid threshold in the FRM and FCM
The Order does not require and the ISO is not proposing any change to bid/offer granularity in any market

## Slide 47: Acronyms used
AGC – Automatic Generation Control
ATRR – Alternative Technology Regulation Resource
BSF – Binary Storage Facility
CSF – Continuous Storage Facility
ESF – Electric Storage Facility (BSF or CSF)
DAEM – Day-ahead Energy Market
DARD – Dispatchable Asset Related Demand
DDP – Desired Dispatch Point
ESR – electric storage resource
FERC – Federal Energy Regulatory Commission

## Slide 48: Acronyms used (continued)
FCM – Forward Capacity Market
FRM – Forward Reserve Market
LMP – Locational Marginal Price
NPCC – Northeast Power Coordinating Council
PC – Participants Committee
RC – Reliability Committee
RTEM – Real-time Energy Market
RTO – Regional Transmission Organization
SOC –state of charge
TC – Transmission Committee