## Slide 1
February 5, 2019| Markets committee
Chris Geissler
413.535.4367 | Cgeissler@iso-ne.com
Details of ISO’s Interim Winter Energy Security Proposal
INTERIM COMPENSATION TREATMENT

## Slide 2
Winter Energy Security: Interim Treatment
WMPP ID:
133
Proposed Effective Date: CCP 14
Industry and policy trends are changing the makeup of New England’s power system
ISO is developing a market-based approach to address energy security as part of its response to FERC’s July 2nd Order, but that design will not be filed before retirement bids are due for FCA 14 (March 2019)
ISO committed to addressing the impacts of retaining resources for fuel security and, therefore, the ISO is proposing an interim compensation treatment to provide similar compensation to similarly situated resources and to reduce the likelihood of uneconomic retirement bids from resources that provide winter energy security
This interim compensation treatment will be in place for CCPs 14 and 15
Today, the ISO will discuss its final proposal and Tariff language

## Slide 3: Background: Design objectives
Objective A: Provide similar compensation for similar service
Objective B: Reduce the likelihood that an (otherwise economic) resource seeks to retire because it is not fully compensated for its winter energy security attributes in the wholesale markets
Objective C: Simple, transparent, and can be implemented in time for CCP 14 (2023-2024)
Objective D: Satisfies standard market design principles
Objectives introduced at November MC

## Slide 4: Background: Five core design components
Trigger conditions: Indicate when gas availability may be low, and system conditions tight
Maximum duration: Caps the total inventoried energy that is compensated
Forward settlement rate: Per MWh payment rate for inventoried energy sold forward for entire winter season
Spot settlement rate: Per MWh payment rate for inventoried energy maintained during each trigger condition
Two settlement structure: Standard settlement pays/charges participants for deviations between their forward and spot positions at the spot settlement rate

## Slide 5: Additional posted materials
Analysis Group: Updated memorandum that discusses model assumptions and includes additional sensitivity analyses (discussed later in presentation)
IMM: Memorandum explaining how the IMM expects this program would impact FCA bids and energy market offer prices (via opportunity costs)

## Slide 6: Summary: Changes to ISO proposal previously presented at the January MC
Change to proposal | Slide #’s
Expanded inventory eligibility for hydro resources | 11-13
Added clarity to criteria that gas contracts must satisfy to sell inventoried energy | 14-23
Clarify eligibility of retained resources | 24-25
Cap on MWh from LNG-based supply contracts and applicability of cap to Mystic units | 26-28

## Slide 7: Summary: ISO proposal does not include changes to the following elements
Proposal element | Slide #’s
Estimated forward rate | 8-10
Broader changes to contract and reporting requirements for gas contracts | 18, 21-23
Trigger condition criteria | 32-41

## Slide 8: Questions and updates related to the forward settlement rate calculation

## Slide 9: Response to stakeholder questions about model assumptions, forward rate calculations under alternate contract terms
At the January MC, stakeholders asked the ISO and its consultant (Analysis Group) about model assumptions and how the forward rate would differ under alternate contract terms, assumptions, and program parameters
  Ex: representative unit heat rate, firm transport, price volatility
  Alternate contract terms include modifications to the number of calls in the contract, a different strike price, and changes to the maximum duration
After further evaluation, ISO continues to propose a forward rate of $82.49/MWh, and a maximum duration of 72 hours
Next: Analysis Group discusses these model assumptions and additional specifications in more detail

## Slide 10: Discussion of forward settlement rate from analysis group
See Revised Analysis Group memorandum, “Calculation of Rate for Interim Compensation Program”, January 30, 2019

## Slide 11: Update to inventoried energy eligibility for hydro resources

## Slide 12: What types of resources are eligible for inventoried energy revenues?
Technology Type | Proposed Program Eligibility
Batteries | Yes
Biomass/Refuse | Yes
Coal | Yes
Demand response | If distributed generation with eligible technology type
Hydro | If on-site or upstream reservoir/pondage controlled by participant
Natural gas | If has a supply contract for firm delivery of gas (into New England)
Nuclear | Yes
Oil | Yes
Passive demand response | No
Solar | No
Wind | No
Eligibility changes from January shown in red

## Slide 13: Inventory eligibility for hydro resources has been expanded
Both on-site pond amounts and amounts available from upstream reservoirs/ponds can be included in inventory for hydro resources if each of the following conditions is satisfied:
  Inventory from upstream reservoirs/ponds must be deliverable within 12 hours to be eligible
  Upstream amounts must be controllable by/available to the generating facility on demand
Inventory reported for a trigger condition day will be the sum of on-site pond storage and amounts from eligible upstream reservoirs/ponds (capped at available output over 72 hours, if applicable)
Generally consistent with how Operating Procedure 23 treats daily-cycle hydro resources for purposes of establishing their winter SCC value

## Slide 14: Clarifications and Proposed updates to Gas contract eligibility

## Slide 15: Summary: Eligibility of resources with gas supply contracts for inventoried energy payments
Generally, if a market participant has (i) a supply contract for gas, and (ii) firm transportation of this gas into New England, the contracted gas is eligible for inventoried energy payments
  This is true for contracts with gas storage facilities west of New England, LNG terminals, etc.
When these conditions are met, the market participant can schedule this gas if the resource is requested by the ISO
Market participants that sign such contracts help the region meet its winter energy security needs
Next: Further discussion of how ISO interprets (i) and (ii) above

## Slide 16: Contract terms to be eligible for inventoried energy revenues
Recall: At the January MC, stakeholders asked whether certain conditions must be satisfied for contracted gas to qualify as inventoried energy
These questions included:
  Whether the contract allows the gas to be scheduled intraday
  If the gas must be inventoried on-site by the contract counterparty and reported during trigger conditions
  Whether an LNG contract should require that the generator schedule the gas during tight winter conditions (if it is generating)
The Tariff language presented in January required that the gas must be available to be scheduled by the asset, but did not specifically address these questions
Next: ISO discusses how its proposal addresses these questions

## Slide 17: Additional Tariff requirements for gas contracts to be eligible for inventoried energy revenues
Introduce language that specifies that the contract must allow the buyer to schedule the gas intraday
Clarify that inventory reported for the trigger condition day must account for any supply limitations
  E.g., if the contract is with a terminal that is unable to vaporize and deliver gas to the asset on the trigger condition day, the participant would not be credited with inventoried energy
  Similarly, if the contract is with a buoy that does not have a tanker stationed at it on the trigger condition day, the participant would not be credited with inventoried energy
These more specific requirements are broadly consistent with the requirement that the participant must be able to convert its inventoried energy into electric energy at the ISO’s direction

## Slide 18: ISO’s proposal does not require the contracted gas in inventory to be reported by the contract counterparty
Such a provision would add significant complexity to the interim program, as it would require:
  Inclusion of non-standard gas contract terms
  New program reporting and auditing requirements for third parties that do not directly participate in the region’s wholesale electricity markets
  Assignment of inventoried gas to specific market participants
The counterparties to these contracts have expertise in managing inventories to ensure they have gas available when it is scheduled

## Slide 19: Program includes other provisions to exclude contracts that are unlikely to be deliverable
Program caps the total quantity of inventoried energy from LNG-based gas supply contracts
  Reduces possibility that the program provides compensation to more LNG-based inventory than can be delivered within the maximum duration period
Excludes contracts that are unlikely to be exercised because the incremental cost of the gas may be very high
  Contracts where the incremental cost of the gas may exceed 250 percent of the average seasonal forward price at Algonquin Citygate are excluded
  Modified Tariff language from January MC to clarify that this exclusion also applies to contracts with incremental costs that are not fixed (i.e. indexed to a daily gas price), and may result in incremental gas costs that exceed this average seasonal forward price

## Slide 20: Calculation of average seasonal forward price
Table below gives hypothetical forward prices for Henry Hub and Algonquin Basis across the winter months
Monthly prices produce average total price of $10/MMBtu
Gas contracts that have incremental costs less than or equal to $25/MMBtu and meet the other program requirements would be eligible to participate in the program
  E.g., fixed strike price less than $25, variable strike with a price cap less than $25
 | Henry Hub Price ($/MMBtu) | Algonquin Basis Price ($/MMBtu) | Total Price ($/MMBtu)
December | $4.00 | $3.00 | $7.00
January | $8.00 | $4.00 | $12.00
February | $7.50 | $3.50 | $11.00
Average | $6.50 | $3.50 | $10.00

## Slide 21: Are gas units required to exercise LNG contracts under certain conditions to participate?
Stakeholders asked if the program should require gas generators that sell inventoried energy via an LNG-based gas contract to exercise this contract on days where both of the following conditions hold:
  It is a trigger condition day
  The contract is ‘in the money’
Stated rationale behind such a requirement: On these tight winter days, requiring such resources to call gas from the LNG terminals may ‘free up’ more pipeline capacity for other gas resources to meet electricity demand

## Slide 22: ISO’s proposal does not include such a requirement
Such a requirement would substitute administrative rules for the market participant’s business judgement, and would indicate that when these two conditions are met, it is appropriate for the region to deplete its inventoried energy
  Prices are a more appropriate indicator of when participants should deplete their inventoried energy (next slide)
Furthermore, this requirement would raise other practical questions, including:
  How is this provision applied to other types of contract structures that may not have a clear strike price, such as ‘take or pay’ gas contracts?
  Why would it be limited to LNG contracts, given that generation from an oil unit, hydro unit, coal unit, etc., would also reduce the quantity of pipeline gas needed to meet load?

## Slide 23: Energy and gas prices should incent resources to exercise the contract appropriately
If “freeing up” pipeline capacity would materially improve winter energy security, gas prices are likely to be high, and the participant would therefore find it profitable to exercise its LNG contract at lower incremental cost
If “freeing up” pipeline capacity would not materially improve winter energy security, gas prices are less likely to be high, and the participant may wish to buy gas elsewhere to preserve its ability to exercise the contract at a later date when:
  Gas prices are higher, and the revenues associated with exercising the contract are therefore greater
  Freeing up pipeline capacity for another generator contributes more to winter energy security

## Slide 24: Eligibility of retained resources

## Slide 25: Proposal allows retained resources to sell inventoried energy
At earlier MC meetings, stakeholders asked if resources that have been retained for reliability are eligible to sell inventoried energy
After further consideration, the ISO proposes to allow retained resources to participate in the program
  Applies to resources retained for transmission security or fuel security
Such resources will therefore have a strong incentive to maintain inventoried energy, thereby contributing to the region’s winter energy security
  Comparable incentive to other resources

## Slide 26: Cap on LNG-based gas supply contracts

## Slide 27: Updated LNG-based gas contract cap quantity
Recall: At the January MC, the ISO proposed to cap the quantity of inventoried energy from LNG-based gas contracts to 500,000 MWh
  Based on the daily maximum observed LNG sendout in recent history
Rationale: The delivery of this gas to New England is limited by the storage and pipeline capability of the LNG facilities that serve the region
Since January MC, the maximum observed LNG sendout increased by approximately 12 percent
Using this new maximum quantity yields an updated cap of 560,000 MWh

## Slide 28: Cap excludes inventoried energy associated with the Mystic units
Stakeholders asked if any inventoried energy credited to generators at the Mystic station would be counted towards this cap
This cap will not include inventoried energy credited to the generators at the Mystic station
  The gas burned by these generators was not included in the maximum LNG sendout calculation
  Gas delivered to the Mystic station generally does not impact the Everett terminal’s ability to send gas into the interstate pipelines

## Slide 29: Updated program cost estimates

## Slide 30: Updated program cost estimate
Recall: At the January MC, the ISO estimated direct program costs of $142 million/year, under a number of assumptions
Numerous design elements have been modified since this estimate was calculated, including
  The treatment of upstream pondage
  The cap quantity on inventoried energy associated with LNG contracts
  The exclusion of the Mystic units from the LNG cap determination
Based on these program modifications, the ISO now estimates direct program costs in the range of $112 million to $158 million per year
  Lower bound assumes no inventoried energy is sold via contracts for LNG-based gas supply
  Upper bound assumes inventoried energy is sold up to the cap quantity on contracts for LNG-based gas supply
  Cost estimates include program participation from Mystic units

## Slide 31: How often is oil the marginal fuel?
At the January MC, there was also a question about the percent of winter hours in which oil was the marginal fuel
  This frequency may impact the percent of hours where an opportunity cost adder affects the energy market price
In the winter of 2017/2018, oil was the marginal fuel in approximately 9 percent of hours
There may be instances where an oil unit is marginal, and would not include an opportunity cost of using its stored fuel
  Say, because it has a very large tank and does not expect to reach a point where it has less than 72 hours of fuel during the delivery period
Additionally, there may be instances where another resource type is marginal and would include an opportunity cost
  E.g., a gas-fired resource that is exercising a call option under its contract with an LNG terminal

## Slide 32: Trigger condition criteria

## Slide 33: Trigger condition criteria
As discussed at earlier meetings, the ISO proposes that a day will be a trigger condition if it meets the following conditions
Condition 1: Occurs in December, January, or February
Condition 2: The average of the high and low temperatures measured on that day at Bradley Airport (Windsor Locks/Hartford) is less than or equal to 17 degrees
  This corresponds to a heating degree day (base-65) of 48 degrees
At the January MC, stakeholders asked the ISO for more information on gas conditions during trigger conditions, the merits of a multi-day trigger condition criteria, and how opportunity costs would be affected by measuring inventory during the trigger condition day (next)

## Slide 34: Additional information on historic trigger conditions
As first noted at January MC, historic gas prices are 82 percent higher than their seasonal average during trigger condition days over the past five winters
In January, stakeholders asked for additional information about the extent to which system conditions are stressed during trigger conditions
In the 17 winters between December 2001 and February 2018, there were 70 days where the day-ahead gas price was at least $5/MMBtu more than oil
The ISO’s trigger condition criteria would have produced trigger condition days on 46 of these days (66 percent)
This includes each of the 5 days where gas was at least $25/MMBtu more than oil

## Slide 35: ISO consideration of a multi-day trigger criteria
At the January MC, stakeholders asked the ISO to consider modifying the trigger condition criteria so that trigger conditions would only occur if cold winter conditions lasted for several days
  E.g., average temperature is less than or equal to 17 degrees on 3 out of 4 days
After evaluating this criteria, the ISO does not propose such a change for two reasons
  A multi-day trigger condition criteria is more difficult to forecast
  A multi-day trigger condition criteria may fail to produce trigger conditions on cold days when inventoried energy would contribute to the region’s winter energy security
Next: Further discussion of these reasons

## Slide 36: A multi-day trigger condition would be more difficult to forecast
Resources include opportunity costs and take actions (e.g. pursue replenishments) based on their expectations of future trigger conditions
Under a multi-day approach, even if today (Tuesday) is very cold, participants may not know if it is a trigger condition until three days from now (Friday)
Furthermore, whether the temperature today is above or below 17 degrees could determine whether up to five days are trigger conditions
This uncertainty would make forecasting future trigger conditions more challenging for participants as the determination of each trigger condition depends on the temperature across several (past and future) days

## Slide 37: Any trigger condition criteria must balance between including ‘mild’ days and excluding ‘severe’ days
Participants have noted (correctly) that the ISO’s proposed criteria would treat some ‘mild’ days from past winters as trigger conditions
The ISO’s trigger condition criteria was not developed solely to prevent all ‘mild’ days from being trigger condition days
Rather, it aims to satisfy the following two conditions:
  Produce trigger conditions on ‘severe’ days where inventoried energy is more likely to improve winter energy security
  Not produce trigger conditions on ‘mild’ days where inventoried energy is less likely to improve winter energy security
Criteria that are more likely to satisfy A are less likely to satisfy B, and vice versa
  For example, under this multi-day criteria, January 28th 2014 would not have been a trigger condition day, even though it was cold and gas prices exceeded the oil price by more than $50/MMBtu

## Slide 38: Change in trigger condition criteria would not materially impact expected program costs
A multi-day criteria may reduce the number of trigger conditions
  Historic data indicates 6 expected trigger conditions per winter
This change would not impact the forward settlement rate of $82.49, but the spot rate would increase to $13.75/MWh ( = $82.49/MWh / 6 trigger conditions)
For each MWh of inventoried energy maintained through winter and sold spot, expect the following revenues (per MWh):
ISO’s proposal: $82.50 ( = 10 trigger conditions × $8.25/trigger condition)
Multi-day criteria: $82.50 ( = 6 trigger conditions × $13.75/trigger condition)
Inventoried energy would therefore yield same expected payment under either set of trigger conditions, whether sold forward or spot

## Slide 39: Change in trigger condition criteria would not materially impact expected opportunity costs
Recall: The opportunity cost for a resource with inventoried energy is dependent on each of the following factors:
  The spot settlement rate
  The expected number of inventoried energy measurements (associated with trigger conditions) before the end of the delivery period (or it replenishes)
Consider the opportunity cost for a resource with less than 72 hours of inventoried energy at the winter’s midpoint (half of expected trigger conditions remain) if it will not replenish
ISO’s proposal: $41.25 ( = 5 remaining trigger conditions × $8.25/trigger condition)
Multiday criteria: $41.25 ( = 3 remaining trigger conditions × $13.75/trigger condition)

## Slide 40: Multi-day trigger condition criteria likely to have similar impact on energy market prices as ISO criteria
If ISO’s proposed trigger conditions and multi-day criteria have a similar impact on opportunity costs, they are also likely to have similar impacts on energy market prices
The logic behind why this effect would be similar holds not just for the discussed multi-day trigger condition, but for any trigger condition criteria that differs from that proposed by the ISO

## Slide 41: How would opportunity costs change if inventoried energy is measured during the trigger condition day?
At the January MC, stakeholders asked how the opportunity costs included in energy market offers would differ if the design measured inventoried energy during the trigger condition day
For resources with less than 72 hours of inventoried energy, moving the deadline from 8am after the trigger condition day to 8am on the trigger condition day would decrease the opportunity cost by $8.25/MWh between 8am on the trigger day and 8am the following day
Measuring inventoried energy on the trigger day would therefore tend to produce lower energy market prices on trigger condition days than under the ISO’s proposal, where this measurement occurs after the trigger condition day concludes

## Slide 42: Tariff Language

## Slide 43: Introduction of new Tariff section MR1 Appendix K
Section | Change | Description
III.K.1 | New section | Submission of Election Information
III.K.2 | New section | Inventoried Energy Base Payments
III.K.3 | New section | Inventoried Energy Spot Payments
III.K.4 | New section | Cost Allocation
Incremental changes from those included at the January MC are included in redline

## Slide 44: Summary: Five core design components
Trigger conditions: Indicate when gas availability may be low, and system conditions tight
Maximum duration: Caps the total inventoried energy that is compensated
Forward settlement rate: Per MWh payment rate for inventoried energy sold forward for entire winter season
Spot settlement rate: Per MWh payment rate for inventoried energy maintained during each trigger condition
Two settlement structure: Standard settlement pays/charges participants for deviations between their forward and spot positions at the spot settlement rate

## Slide 45: Next Steps

## Slide 46: Stakeholder schedule
Stakeholder Committee and Date | Scheduled Project Milestone
Markets Committee November | Conceptual approach
Markets Committee December | Detailed proposal
Markets Committee January 2019 | Proposal details; Tariff language; review stakeholder alternatives and amendments
Markets Committee February 2019 | Continued discussion of proposal and stakeholder alternatives and amendments
Markets Committee March 2019 | Vote
Participants Committee March 2019 | Vote

## Slide 47: Conclusion
ISO’s proposed interim treatment introduces a two-settlement structure for inventoried energy
This interim treatment satisfies the project’s four objectives
  Provides similar compensation for similar service
  Reduces the likelihood that (otherwise) economic resources pursue retirement
  Simple and implementable for CCP 14
  Broadly consistent with good market design
This treatment will help the region meet its winter security objectives in the short-term
Serves as a bridge to the ISO’s market-based approach to meeting its winter security objectives in the long-term