## Slide 1
March 6, 2019| Markets committee
Andrew Gillespie
413.540.4088 | agillespie@iso-ne.com
Discussion of a market-based solution to improve energy security in the region
WINTER ENERGY SECURITY IMPROVEMENTS: MARKET-BASED APPROACHES

## Slide 2
Winter Energy Security Improvements
WMPP ID:
125
Proposed Effective Date: see below
In accordance with FERC’s July 2, 218 order in EL18-182-000, the ISO must develop and file improvements to its market design to better address regional fuel security
Today’s discussion
  First we will discuss the problem more granularly;
    What are the core problems, the implications, and root causes
    How are the core problems interrelated
  With a clearer picture of these specific problems, we then share our current thinking on design concepts to address these interrelated problems ahead of a draft discussion paper scheduled for next month
The ISO is targeting a filing to FERC for November 15, 2019, consistent with the ISO’s extension request filed on January 18, 2019, in EL18-182
  Extension request currently pending at FERC

## Slide 3: Problem Statement
At the October 2018 Markets Committee meeting, the ISO provided a high-level summary of the issue
  There may be insufficient energy available to the New England power system during extended cold winter weather conditions to satisfy electricity demand, given the system’s evolving resource mix and fuel delivery infrastructure
  While there has been no loss of load to date on the bulk power system attributable to these conditions, the ISO is concerned this emerging issue will worsen over time due to observed industry trends
More granularity will be provided today, beyond the contributing causes previously discussed, to guide solutions

## Slide 4: Three Conceptual Components
New Ancillary Services in the M-DAM
  In December 2018 we discussed the Energy Inventory Reserve Constraint (“EIRC”)
  Since then, this element/concept has been modified
  The concept of a constraint remains, however, the new ancillary services concepts/products have been modified, and will be discussed today
Multi-Day Ahead Market (M-DAM)
  In November 2018, we discussed the M-DAM
  While not the focus of today’s design concept discussion, the role of the M-DAM in some form remains an important part of the comprehensive design
Seasonal Forward Procurement
  The M-DAM and new ancillary services are core to the design
  As noted previously, the ISO will evaluate the seasonal forward procurement aspect following the development of the core components, and discuss ideas later this year

## Slide 5: Problem Discussion

## Slide 6: Deeper Focus: Three Problems
Problem 1. Incentives and Compensation Inefficiently low market incentives for resources that face production uncertainty to make advance fuel/energy supply arrangements
Problem 2. Operational Uncertainty There may be insufficient energy available to withstand an unexpected, extended (multi-hour to multi-day) large generation/supply loss during cold conditions, particularly if that energy supply loss in non-gas generation
Problem 3. Inefficient Schedules Premature (inefficient) depletion of energy inventories for electric generation, absent a mechanism to coordinate and reward efficient preservation of limited-energy supplies

## Slide 7: Context and Implications
These are inter-related problems. Fundamentally, Problem 1 is the contributing (and arguable the primary) cause of both Problem 2 and Problem 3
Uncertainty. Problems 1 and 2 apply to resources that do not routinely clear in the day-ahead market, but that the ISO may need to call upon to operate above any day-ahead market award
  Such resources face uncertainty over when/how often they may operate
  Empirically, we have not observed problems with resources that routinely clear in the day-ahead market failing to procure sufficient fuel/energy to meet their day-ahead award
The Alignment Problem. The ISO’s single day-ahead market (“SDAM”) is not well aligned with the multi-day horizon over which the ISO is forecasting and operating an increasingly energy-limited system

## Slide 8: Problem 1. Incentives and Compensation
It is financially prudent for generators to incur up-front costs of unit-specific fuel/energy supply procurement and replenishment arrangements based on their expected energy output
  For example, the up-front cost to arrange trucking for a prompt oil replenishment, or up-front fees for an intra-day notice gas contract with an LNG terminal, or other fixed costs associated with arranging fuel/inputs in advance relevant to a generator’s technology
The Problem
A generator that faces uncertainty over whether or how often it will operate may not incur such fixed costs for any unexpected energy output
Otherwise, these fixed costs become a loss if the generator does not operate

## Slide 9: Problem 1. Incentives and Compensation Adverse Consequences
Reliability risks. In extreme cases, this can result in extended reserve and energy shortages
Not cost-effective. Inefficiently low procurement incentives may produce higher than necessary total costs compared to efficient procurement outcomes
Bottom line: Robust procurement and replenishment arrangements may not be in a generator’s commercial interest under the current market design, even when such arrangements would be beneficial and cost-effective for the system

## Slide 10: Problem 1. Incentives and Compensation Root Causes
Uncertainty over whether or not the unit will be in demand
Fixed Costs of generator-specific procurement and replenishment arrangements, which will be a financial loss to the generator if it does not operate
The decision to make fuel arrangements matters (i.e., impacts reliability and market outcomes)
  In the past, if a unit wasn’t able to operate (for fuel or any other reason), there were sufficient energy stocks to dispatch up another generator in its place
  This assumption may not be valid in an increasingly energy-limited system, especially during cold winter conditions
  These decisions could dramatically impact the energy price, especially if demand turns out to be high (or cause a deficiency)

## Slide 11: Problem 2. Operational Uncertainty
Imagine a situation when, after the day-ahead market clears, we unexpectedly lose a large (non-gas) generator for an extended duration
  The energy needed to replace the lost generator must come from a generator that did not clear in the day-ahead market
The Problem
As a consequence of Problem 1, it is not certain that a replacement generator will have adequate fuel/energy supply arrangements (especially if the replacement generator does not routinely clear in the day-ahead market)
Conceptually, this implies the need for an ‘energy margin’ to address uncertainty

## Slide 12: Problem 2. Operational Uncertainty What Supply Does the ISO Rely On Above Day-Ahead Market Awards
Three operational categories:
Replacement Energy. Energy needed if a day-ahead cleared resource is unable to perform for an extended (multi-hour or multi-day) duration
Operating Reserves for Fast-Start/Fast-Ramping Generation Contingency Response. Energy from resources that the ISO relies upon for real-time operating reserves in the day-ahead current operating plan, including both off-line generation and ‘upper blocks’ of on-line (spinning) generation
Load-Balance Reserves. Energy to supply the difference when forecast load exceeds day-ahead cleared physical supply

## Slide 13: Problem 2. Operational Uncertainty Implications
Quantity. Depending on the day, there may be up to approximately 4-6 GW of resources in categories A, B, and C, for which Problem 1 is a concern
Not a fixed set of resources. The most cost-effective set of resources to meet these needs can and does vary daily
The ‘Margin’ for Uncertainty. In prior stakeholder discussions, the ISO has stressed at a high-level the need for a ‘margin’ to address operational uncertainties in an increasingly energy-limited system

## Slide 14: Problem 2. Operational Uncertainty Adverse Consequences
Reliability risks. Absent a ‘margin’ for uncertainty, with stronger incentives for advance fuel/energy supply arrangements, this can in extreme cases result in extended reserve and energy shortages
Not cost-effective. Inefficiently low procurement incentives may produce higher than necessary total costs compared to efficient procurement outcomes
Timing problems. The system may not be well positioned for generators to start-up/ramp-up in a cost-effective way when real-time reserves must be converted back from energy to reserve status after a contingency

## Slide 15: Problem 2. Operational Uncertainty Root Causes
Limited energy. There is an implicit assumption that there will be sufficient additional energy to cover demand after an unexpected, extended (multi-hour to multi-day) large generation/supply loss
  The assumption that there will be sufficient energy from on-line unloaded gen and off-line resources to supplementally commit, post-contingency may not be valid in an increasingly energy-limited system, especially during cold winter conditions
Unpriced value of flexibility. The optimal ‘mix’ of resources to cover the ‘margin for uncertainty’ isn’t simply those units that do not clear day-ahead based on offer prices alone
  This ignores lead-times and resources’ flexibility

## Slide 16: Problem 3. Inefficient Schedules
The single day-ahead market may “use up” limited stored energy inefficiently
The Problem
The current construct does not efficiently coordinate the use of limited stored energy resources to meet the demand for energy tomorrow and the demand for energy for day(s) after tomorrow
This can also result in (preventable) shortages
  There may be enough stored energy to meet total energy demands over the next few days if it is used efficiently, but there may not be enough if it is used inefficiently (prematurely)

## Slide 17: Problem 3. Inefficient Schedules Adverse Consequences
Reliability risks. In extreme cases, this can result in extended reserve and energy shortages
Not cost-effective. In general, the status quo produces higher than necessary total costs by using limited stored energy resources prematurely (inefficiently)
Out-of-market posturing. Neither efficient/cost-effective, nor transparently signals costs of actions taken

## Slide 18: Problem 3. Inefficient Schedules Root Causes
Market horizon is not aligned with the system’s operating horizon. ISO-administered single day-ahead market has no forward price signal to convey value of preserving limited energy for future days, instead of using it today
No external market can aggregate the relevant internal information about system-wide inventory limitations For example, OTC forward power markets:
  Do not have access to the system-level supply information
  Do not have the ability or means to price the value of preserving energy for future days
  Do not have the ability or means to coordinate suppliers’ production over multiple days in an efficient way

## Slide 19: Why Are These Issues ‘Problems’ Now?
New England’s power system is evolving into an ever-more energy-limited system
  Pipeline constraints, retiring generators with ample fuel storage, and growing ‘just-in-time’ generation from renewable technologies
The decision to make (or not make) advance fuel/energy supply arrangements matters more in an increasingly energy-limited power system
  In the past, if a unit wasn’t able to operate (for fuel or any other reason), there was sufficient energy to dispatch up another resource in its place
  The presumption that there will be sufficient energy may not be valid in an increasingly energy-limited system
  If too many generators cannot operate the system may face:
    Operating a much more expensive generator further up the supply stack, or
    Scarcity prices, if there is a real-time deficiency in the system’s energy plus reserves requirement

## Slide 20: Conceptual Design elements

## Slide 21: High-Level Design Objectives
Risk Reduction. Minimize the heightened risk of unserved electricity demand during New England’s cold winter conditions by solving Problems 1, 2, and 3
Cost Effectiveness. Efficiently use the region’s existing assets and infrastructure to achieve this risk reduction in the most cost-effective way possible
Innovation. Provide clear incentives for all resources, including new resources and technologies that can reduce this risk effectively over the long term
Revised from September 2018 Presentation

## Slide 22: Design Principles for a Market-Based Solution
Product definitions should be specific, simple, and uniform. The same well-defined product or service should be rewarded, regardless of the technology used to deliver it
Transparently price the desired service. A resource providing an essential reliability service should be compensated at a transparent price for that service
Reward outputs, not inputs. Paying for obligations to deliver the output that a reliable system requires creates a level playing field for competitors that deliver energy reliably through cold-weather conditions
Sound forward markets require sound spot markets. Forward-market procurements work well when they settle against a transparent spot price for delivering the same service
Compensate all resources that provide the desired service similarly.
Revised from September 2018 Presentation

## Slide 23: Overall Design Concept
A comprehensive set of energy ancillary service products that ensure the system is well positioned and has sufficient energy to handle a variety of situations:
  Reliability (consistent with existing NERC/NPCC criteria)
  Done cost effectively
  Reduce the likelihood of out-of-market supplemental commitments or posturing for:
    Unavailability of gas to gas-only generation
    De-rates or underperformance of day-ahead cleared generation
    Premature depletion of stored energy resources
    Under-procurement of day-ahead cleared demand (i.e., load balancing)

## Slide 24: Design Concepts to Address Problems
Problem 1. Incentives and Compensation Design Concept: Create several new, voluntary ancillary services in the day-ahead markets with stronger, financial-binding, obligations and settlements
Problem 2. Operational Uncertainty Design Concept: Procure new ancillary services of such types and quantities to assure system reliability and procured cost effectively
Problem 3. Inefficient Schedules Design Concept: Award energy and new ancillary service obligations through a multiple-day ahead market

## Slide 25: Multiple-Day Ahead Market Latest Thinking
The M-DAM alone addresses Problem 3, however:
We have heard a number of questions and concerns about the length of the market horizon, primarily how this may not align with participants’ hedging strategies conducted outside ISO-administered markets
In practice it may not be necessary to procure new ancillary service products for the entire multiple-day market horizon
  To be effective, the new ancillary service products should be acquired in/for the first two days of an M-DAM
  This will allow the system to be positioned to handle any major contingency (i.e., the deployment of RER resources) should an extended (multi-day) large energy loss occur shortly after the daily close of the M-DAM
The ISO is still assessing the duration of the M-DAM

## Slide 26: Three Categories of New Ancillary Services (Procured in Day-Ahead Markets)
A multiple-day ahead market for energy, co-optimized with three new ancillary service products:
Replacement Energy Reserves (RER) – New product in the day-ahead markets, not in real-time
  A ‘call on energy’ product from on-line or off-line gen
  1+ hour ramp-up/start-up capability
Generation Contingency Reserves (GCR) – Forward form of existing TMSR, TMNSR, and TMOR products
Energy Imbalance Reserves (EIR) – New product in day-ahead markets
  A ‘call on energy’ product to cover the load forecast in excess of day-ahead cleared load (net virtual bids/offers)
Combined, these provide the ‘margin for uncertainty’ in an increasingly energy-limited system

## Slide 27: New Ancillary Services Current Thinking
Participation
Resources (or portions thereof) that do not sell energy day-ahead may acquire a new day-ahead ancillary service obligation, and receive day-ahead compensation for that position
  Similar to day-ahead energy, the new day-ahead ancillary services are financially settled in real-time
This creates a financial incentive for awarded resources to be capable of delivering energy above any day-ahead scheduled amount – i.e., actually provide energy ‘on call’ during the operating day, if and when the resource is needed
Energy Sustainability
Achieved through the clearing process for the aggregate capability of all obligated ‘on-call’ resource as a whole, not through required energy sustainability limits on individual resources

## Slide 28: Purpose of New Ancillary Services
The new day-ahead ancillary service products address Problems 1 and 2
  Problem 1 is addressed using products with a formal ‘call on energy’ option obligation that mirrors how this problem’s root causes are normally solved in markets (i.e., a real option on energy)
  Problem 2 is addressed via the product definition and quantities procured for each of the new day-ahead ancillary service products
  These mirror the capabilities (above day-ahead awards) the system relies upon for uncertainty today (Slide 12)
The M-DAM alone addresses Problem 3
These new ancillary services will be procured cost-effectively in a co-optimized multiple day-ahead market
Prices will transparently signal the costs of a more reliable energy-limited system

## Slide 29: Procuring New Ancillary Services
Why is it necessary to also procure new day-ahead ancillary services for Operating Reserves and to cover forecast load?
The ‘cannibalization’ problem. If, for example, only Replacement Energy Reserves (RER) are procured day-ahead:
  Many of the system’s fast-start resources may clear as RER instead of Generation Contingency Reserve, GCR
  During the operating day, the real-time reserve markets’ co-optimization will ‘cannibalize’ that fast-start capability (designate it as operating reserves)
  This will leave the system without the Replacement Energy Reserve capability we sought to acquire in the first place
Cost-effectiveness. We need all these ancillary service capabilities to have a reliable operating plan each day
  If they are not procured in a co-optimized process, we will not obtain the least-cost portfolio of resource capabilities going into each operating day

## Slide 30: Conceptual Design Elements Summary

## Slide 31: Next steps

## Slide 32: Target Schedule of ISO Deliverables
This project will continue to be addressed in three broad agenda categories:
  ISO’s Multi-Day Ahead Market (M-DAM) and new ancillary service design
  Stakeholder Proposals
  ISO’s Impact Analysis
The target delivery schedule for the ISO’s major deliverables are shown below
  While chart indicates initial releases, the items will continued to be developed and discussed throughout the extended stakeholder schedule
Target Delivery Date | ISO Deliverable
April 1, 2019 | ISO discussion paper (updated and re-posted as needed)
July 1, 2019 | ISO initial impact analysis presentation (updated and re-posted as needed)
August 7, 2019 | Draft ISO Tariff language and draft ISO impact analysis report
October 9, 2019 | Final ISO discussion paper, final ISO draft impact analysis report, and final ISO Tariff language
Revised from January 2019 Presentation

## Slide 33: Stakeholder Schedule (with Filing Extension)
Stakeholder Committee and Date | Scheduled Project Milestone
Markets Committee March 2019 | Update on ISO conceptual design considerations, stakeholder proposals
Markets Committee April 9-10, 2019 | Initial review of discussion paper
Markets Committee May - June, 2019 | Continued discussion of ISO and stakeholder proposals; updates of discussion paper as warranted
Markets Committee July 9-10, 2019 | Initial review of impact analysis
Markets Committee August 13-15, 2019 | Draft ISO Tariff language and draft ISO impact analysis report
Markets Committee September 18-19, 2019 | Final review of proposed Tariff language (ISO proposal and any stakeholder proposal(s))
Markets Committee October 16-17, 2019 | Vote
Participants Committee November 1, 2019 | Vote