## Slide 1
April 9-10, 2018 | Markets committee
Christopher Parent
413.540.4599 | Cparent@iso-ne.com
Framework for assessing the impacts of the proposed market improvements
Winter Energy Security Improvements: Impact Assessment Approach

## Slide 2: ISO plans to perform analysis of both Energy Market and Capacity Market
Objective of analysis is to inform stakeholders on how the design performs under different scenarios
Quantitatively analyze energy and ancillary service market (EAS) impacts in the context of the day-ahead market(s) using a production cost model (PCM) under particular market conditions
  Impacts measured by comparing market outcomes with and without the proposed energy security improvements
Develop a qualitative framework for understanding the impacts of the proposed market improvements in the capacity market

## Slide 3: Proposed Impact Analysis Schedule
May-2019. Provide a more detailed explanation of the PCM structure and scenarios which the ISO plans to simulate
June-2019. Respond to feedback from stakeholders and discuss any modifications to proposed scenarios
July-2019. Provide initial results (limited scenarios) and discuss how to understand analysis/results
August-2019. Review full results of the analysis
September-2019. Provide a final report on the impact analysis

## Slide 4: Prior Material
Presented at December-2018 Markets Committee (red edits reflect changes)

## Slide 5: Impact Analysis
ISO is planning to provide analysis focused on the energy security improvements design
  Initial overview of approach in December
  Additional discussion of scenarios in May-2019 and June-2019
  Share results in July-2019 to September-2019 timeframe
Objective of analysis is to inform stakeholders on how the design performs under different scenarios
While analysis will include review of historical periods, focus will be on future scenarios
  ISO seeks input on what scenarios should be considered
  ISO will work to run requested scenarios, but may need to consolidate various scenarios due to time constraints
ISO will include qualitative analysis of implications to the Forward Capacity Market (FCM)

## Slide 6: introduction
Objectives for analysis of impacts

## Slide 7: Impact assessment is focused on providing a better understanding of the proposed design
Analysis will evaluate and present multiple scenarios, but not propose a “reference case”
Plan to evaluate the impacts under particular scenarios in terms of economic outcomes (e.g., production costs, overall consumer costs, prices) and operational changes (e.g., energy inventories)
Illustrate how proposed market enhancements will perform and the effect on market outcomes

## Slide 8: Analysis of energy market impacts
Modeling Conceptual Approach

## Slide 9: Analysis of Energy Market Impacts: Objectives and Approach
Quantitatively analyze energy and ancillary service market (EAS) impacts in the context of the day-ahead market(s)
Market simulation using a production cost model (PCM) under particular market conditions
Impacts measured by comparing market outcomes with and without the proposed energy security improvements
  Can inform impact of input design parameters (e.g., new ancillary service requirement)
  Model not intended to forecast all proposal impacts (e.g., not modelling investment or equilibrium market response)
Scenario analysis will demonstrate the impacts under a range of assumptions – for example, resource mixes, gas prices, load, and winter conditions

## Slide 10: Production Cost Model: Framework
A PCM will use standard logic, minimizing production costs subject to system and resource constraints
Solution logic will capture the proposed market enhancements
  MDAM: the model will minimize costs over an N-day ahead time period, subject to selected market requirements (e.g., operating reserves)
  New A/S requirements: the model will include the three new ancillary service (A/S) requirements in the day-ahead market
Model will not have all “real-life” energy market constraints – for example:
  Likely to model no (or few) transmission constraints
  May use of simplified commitment logic to handle unit “lumpiness”

## Slide 11: Key Model Assumptions
Key model assumptions are in four areas:
  Time period of analysis
  Supply
  Demand
  Other market factors (e.g., fuel input prices)
Analysis will focus on future time period
  December-to-February, mid-next decade (e.g., 2025/26)
  The model will be benchmarked to recent winter outcomes
  ISO is reviewing how to approach analysis of impacts outside of winter periods

## Slide 12: Production Cost Model: Supply
Resource mix
  Most recent set of resources based upon capacity market qualification with adjustments as appropriate to model specific scenarios (resource mixes)
  Scenarios will consider alternative assumptions, such as renewable additions (given state energy policies) and retirement of at-risk resources
Energy inventories and refueling rates
  Based on historical experience, adjusted for changing market economics and market design impacts

## Slide 13: Production Cost Model: Demand & Other Inputs
Demand
  Hourly load profiles based on historical winters, adjusted for changes in future demand
  Loads will be net of (non-wholesale) solar and (passive) demand response (more/less solar or EE may be addressed as scenarios)
Natural gas prices
  Model will incorporate daily price volatility
  Utilize historical volatility patterns or simulate using statistical model
  Potential adjustments for changing market conditions (e.g., changing natural gas demand, retirement of non-gas resources)
Other prices (fuel oil, emission allowances)
  Fixed across each winter scenario, reflecting current forward markets/forecasts
Unit-level emissions rates

## Slide 14: Production Cost Model: Outputs
Total production costs
Prices (energy, operating reserves, energy inventory)
Total payments (revenues to supply, costs to load)
Changes in energy production and storage, with/without the proposed design changes
  Energy, operating reserve and other reserve shortages
  Total “economically postured” energy
  Energy inventory profiles over winter
Air emissions impacts
Technology-type revenues and output (but not unit-level results, due to Information Policy limitations)

## Slide 15: Production Cost Model: Sensitivity Analysis
Analysis will consider multiple scenarios, to show impacts under different potential future market conditions
No plans to propose a “reference case”
  PCM provides no basis to measure likelihood of any particular scenario
Scenarios to focus on key assumptions/conditions:
  Future retirements and additions (e.g., renewable resources, at-risk resources)
  Natural gas price volatility
  Load / winter weather severity
  Market responses to natural gas prices
  New ancillary service requirement level and/or penalty factors

## Slide 16: Impact on forward capacity market
A brief introduction to the approach for assessing the impact of the proposed energy security improvements on the FCM

## Slide 17: Forward Capacity Market Framework
Current time constraints and modeling approach precludes a full quantitative assessment of how the proposed market improvements will impact the capacity market
  ISO is planning to perform additional, quantitate analysis in context of revisions to Net CONE and ORTP for FCA16
Plan is to develop a qualitative framework for understanding the impacts of the proposed market improvements in the capacity market
  Assess qualitatively factors that could affect FCM outcomes, particularly changes in net CONE and changes in net EAS revenues for proxy resource types
If time permits, may be able to complete (limited) quantitative analysis of (some) FCM scenarios