## Slide 1: ISO-NE Long Term Market Reforms Fuel Security
Michelle Gardner, Markets Committee
June 11, 2019

## Slide 2: Introduction
Per FERC directive, ISO-NE to file long-term market reforms to address energy security in October 2019
  Stated objective for these long-term reforms is to replace short-term measures, such as ISO-NE’s interim compensation scheme, and avoid the need to do fuel security RMRs (or any other “out-of-market” or other emergency action)
NEER commends ISO-NE for its work to date and for the number of improvements already completed to the design
NEER, however, remains concerned that the ISO-NE proposal does not go far enough to put the right price signals in place
  Without any real-time demand for energy security reserves (Replacement Energy Reserves, RER), the ISO-NE proposal is unlikely to incent in-market solutions to winter energy security much more effectively than the current design that led to the RMR
Addressing regional energy security needs begins with proper price signals and incentives in the energy and reserve markets
NEER is proposing physical RER and GCR in the DA market

## Slide 3: Two Key Examples to Measure Any Design
EXAMPLE ONE: During a stressed winter period, the regional markets should enable optimized use and the right pricing across all fuels, not just stored fuels
  Operator stress and concern with depleting regional inventories should be reflected in real-time prices such that all units with fuel available, including CC plants with available pipeline gas, can be picked up in-merit
  The “Combined Cycle with Expensive Maine Pipeline Gas” example
EXAMPLE TWO: If there are extraordinary actions that a generator can take that are valued by the operators, those actions should be offered and priced in the market
  The “We can arrange a special delivery but it is expensive” example
  These actions are fluid – they could be done hours before or several days before – suggesting a more flexible multi-day ahead market
Any final market design should be measured against its ability to optimize the resources already in the region and to provide real incentives
The region needs tools to properly value any final market design

## Slide 4: ISO-NE Proposal is Challenging
We think the main idea is that resources that sell the call options would have incentives for next-day fuel arrangements, however, the extra incentives are weak at best
  They depend on assumptions about lumpy offers and risk aversion
  One simply cannot expect a strong response absent a fundamental change to real-time demand (expectations for which work backwards to incent preparedness)
Open proposal questions:
  How ISO-NE will set the strike price for the new products
  How ISO-NE/IMM will mitigate offers, particularly if they are voluntary
Questions on whether the proposal will ultimately depress real-time prices and/or what incentives will be given to those long-lead time resources with stored fuel
ISO-NE’s design does not incent a strong real-time demand and appears to stray far from our original objectives
ISO-NE reliability requirements for GCR/EIR/RER are not based on depleted inventories or energy security concerns

## Slide 5: NEER Alternative to Strengthen the RER
“Replacement Energy Reserves” to be purchased by ISO-NE
  RER is a physical reserve product, not a financial call option
RER is set aside both in the DAM and RTM, and as such it can increase RT energy prices when fuel reserves are low
RER would be deployed only under fuel scarcity conditions, at high prices incorporating reserve constraint penalty factors
  Fuel scarcity conditions to be defined
  This alternative proposal aims to reflect fuel scarcity conditions in RT energy prices consistent with reliability objectives
  Expectations for scarcity would translate to forward prices and influence fuel procurement and investment/retention of energy-secure resources
No separate EIR product from RER; additional RER can be secured if virtual participation needs to be backed
NEER alternative for a physical RER is the same as what has been previously called Strategic Operating Reserve
RERs must have physical capacity backed by secure fuel

## Slide 6: NEER Alternative to Strengthen the GCR
“Generation Contingency Reserve” purchased by ISO-NE in DA
  GCR are physical reserve products, not a financial call option
  GCR meets the same criteria as the OR products in the RTM
GCR suppliers have the financial obligation to provide the corresponding OR product in the RTM
  GCR suppliers can trade their DA obligations in the RTM
GCR and RER offers and clearing prices are different
  GCR and RER qualification criteria, quantities and offers will differ
ISO-NE would co-optimize energy and reserves in DA
  Existing OR are presently procured in real-time; DA co-optimization has been an open item/action item for many years in New England
NEER alternative for physical GCR makes them consistent with the RT Operating Reserves
GCRs are separate and different products from RER

## Slide 7: RER Product Definition
RER are reserves of a secure-MWh-backed MW that will not be used for energy unless called by ISO-NE to avoid/reduce an anticipated energy or operating reserve shortages
Up to a 12-hour notification time for deployment
  Consistent with winter energy security mostly being a multi-day challenge, not a real-time surprise
Can be deployed DA or up-to 12 hours ahead as part of the RAA process in the day-of, but not in the RT market
NEER RER used by ISO-NE to avoid/reduce energy or reserve shortages
The product purchased by ISO-NE is a physical one and requires secured fuel

## Slide 8: RER Demand Curve in DA and RT
Could be 1-2 GW minimum for each hour of the next day (or multi-days-ahead), subject to an RCPF of $900/MWh, consistent with deploying to avoid shortages of 30-min OR @$1000/MWh
Then sloping down and rightward from there, as a gradual ORDC provides better price formation
  Size and number of participating units is large relative to the need
  The minimum quantity could be sized to cover the largest resource contingency
Could keep demand simple, invariant to current/forecast conditions; if tight and the resource is needed for energy, it will be deployed; if not, the price will be low
NEER RER Demand Curve to set Quantities
Creating a demand curve addresses lumpiness issues and creates a stronger price signal

## Slide 9: Example RER Demand Curve
NEER RER Demand Curve
Creating a demand curve addresses lumpiness issues and creates a stronger price signal
$/MW price
MW quantity
minimum
quantity
RCPF: $900/MW

## Slide 10: RER Supply Requirements
Any resource backed by energy-secure MWh, with startup ≤ 12 hrs (must verify availability)
Potential suppliers (non-exhaustive list):
  Oil-fired units with on-site fuel inventory
  Gas-fired units with secure fuel supply arrangements
  Pondage hydro (depending on their reservoir level)
  Pumped hydro, batteries (depending on their reservoir level/state of charge)
NEER eligibility for RER closely aligns with incentives for resources with stored fuel
Supply requirements are clear and straightforward and open to any resource with energy-secure MWhs

## Slide 11: RER Day-Ahead Clearing
Clearing engine tries to select the full amount of RER at least cost
Cleared resources will be withheld from the DA energy market (while still being available for intra-day deployment, see slide 12)
But if the clearing engine can minimize cost (incl. $900 RCPF for RER) by clearing less RER, it does; the RER price will be $900, and the DA energy and GCR prices will be > $900
Prices for RER include energy and GCR opportunity cost and RER offer price of the RER marginal unit
Day-ahead clearing is similar to the ISO-NE proposal, except that RER and GCR clear separately

## Slide 12: RER Intra-Day Deployment
Resources providing reserves cannot be deployed in RT if they have a 12-hour startup; but they can be called intra-day as part of the RAA process
For example, if a resource with an 12-hour startup is committed to providing reserves at 2 p.m., ISO-NE can deploy before 2 a.m. if needed to avoided reserve shortages
Intra-Day Deployment similar to existing processes
RER deployment would be outside of RT, although the product would be traded in RT (e.g., similar to TMOR)

## Slide 13: RER Real-Time Dispatch & Settlement
The resource will be dispatched in RT based on its incremental energy offers, as part of the co-optimized system dispatch that accounts for the demand for RER (incl. RCPF) and all other resources’ energy offers and ability to provide RER and OR
  Need to carefully define eligibility for the RER in RT to get pricing right
Co-optimization of energy, Operating Reserves (OR) and RER can result in RT RER prices of $0 to $900 RCPF
  Energy and OR prices are always higher (or, no lower) than RER prices
  When taking one more MWh of energy or OR reduces RER clearing, RER prices are set by the demand curve (up to RCPF)
Real-Time Dispatch and Settlement is the same whether committed DA or in the RAA
RT Dispatch and Settlement is the same as today’s except that there is a new reserve product added, RER.

## Slide 14: RER Real-Time Dispatch & Settlement Examples
Streamlined system:
  Load: 700 MW
  No Operating Reserves
  RER requirement: 300 MW
  RER offer price: $0/MWh
Will analyze RT market clearing under three different scenarios:
  No fuel scarcity
  Near fuel scarcity (not all units offer RER)
  Fuel scarcity (unit outage)
NEER proposal creates appropriate incentives for fuel scarcity conditions
Under NEER’s Alternative to the ISO-NE proposal, RT dispatch and prices change as a function of fuel scarcity

## Slide 15: RT Example 1 – Normal Conditions
C
A
RT Energy price: $42/MWh
RT RER price: $0/MWh
NEER proposal creates appropriate incentives for fuel scarcity conditions
Under normal conditions, RER price is very low (at or near $0) and energy prices do not change with respect to today’s design
price $/MW
$10
$60
$50
$40
$30
$20
B
D
E
energy price
cleared for RER
cleared for energy
quantity MW
load
load + RER req

## Slide 16: RT Example 2 – Near Fuel Scarcity
RT Energy price: $60/MWh
RT RER price: $24/MWh
NEER proposal creates appropriate incentives for fuel scarcity conditions
As the fuel margin becomes tight, low-cost secure-energy units are set aside as reserves, increasing RER and energy prices
C
A
price $/MW
quantity MW
load
$10
$60
$50
$40
$30
$20
B
D
E
energy price
cleared for RER
RER price
load + RER req
Unit E not available for RER

## Slide 17: RT Example 3 – Fuel Scarcity
RT Energy price: $942/MWh
RT RER price: $900/MWh
NEER proposal creates appropriate incentives for fuel scarcity conditions
When fuel becomes scarce, the RER price is the RCPF and energy prices are above it, reflecting scarcity conditions
price $/MW
$10
$60
$50
$40
$30
$20
A
C
D
E
quantity MW
load
load + RER req
cleared for RER
RER shortage, price set by RCPF
Unit E not available for RER
Unit B on outage

## Slide 18: RER Penalties for Non-Availability / Performance
The RT clearing price also determines the cost to cover for any resource that has committed to providing reserves but becomes unavailable
NEER to incorporate penalties where a resource cannot cover its obligation
NEER to develop non-availability and performance penalties

## Slide 19: Big Picture / Next Steps
ISO-NE has indicated that post-filing, they will look at a seasonal forward market
  Voluntary, competitive forward auction to provide asset owners with incentives and compensation to invest in supplemental supply arrangements for the coming winter
  If done incorrectly, a seasonal forward market is likely to depress energy market prices and provide the wrong incentives
FCM could be reformed to consider “demand” for winter-energy-secure infrastructure to be procured competitively in FCM
Getting energy markets designed right is a necessary step against any other out-of-market interventions in the future that could be harmful to the market
A physical RER, coupled with the right forward incentives is key