## Slide 1: ISO-NE Long Term Market Reforms Fuel Security: Updates/Clarifications (Significant New/Revised Slides Noted)
Michelle Gardner
August 13-15, 2019

## Slide 2: Introduction
Per FERC directive, ISO-NE to file long-term market reforms to address energy security in October 2019
  Stated objective for these long-term reforms is to replace short-term measures, such as ISO-NE’s interim compensation scheme, and avoid the need to do fuel security RMRs (or any other “out-of-market” or other emergency action)
Since at least 2011, ISO-NE has expressed concern with its reliance on “just-in-time” gas units and pipeline constraints but has been short on market-based proposals
NEER is very concerned that the latest ISO-NE proposal does not meaningfully address operator concerns and does not go far enough to put the right price signals in place
  Do not want to end up back in the same place facing another RMR
Addressing regional energy security needs begins with proper price signals and incentives in the energy and reserve markets that align with objectives
NEER is proposing its own alternative to address fuel security

## Slide 3: ISO-NE Proposal Not About Fuel Security Anymore
ISO-NE proposing a day-ahead call option for three types of reserves:
  One for forecasting error – “Replacement Energy Reserves” or RER
  One to address load imbalances due to virtual transactions – “Energy Imbalance Reserves” or EIR
  Traditional operating reserves that will now be bought day-ahead – “Generation Contingency Reserves” or GCR
ISO-NE’s argument that resources that sell the call options would gain incentives for next-day fuel arrangements is weak
  It depends on assumptions about lumpy offers and supplier risk aversion
Questions remain on the proposal’s impact on real-time prices and/or what incentives will be given to those resources with stored fuel that can meet ISO-NE’s operational needs
ISO-NE’s design does not incent a strong real-time demand and appears to stray far from our original objectives
ISO-NE reliability requirements for GCR/EIR/RER are not based on depleted inventories or energy/fuel security

## Slide 4: NEER Proposal Summary and Differences from ISO-NE
Core: Introduces DA and RT Strategic Operating Reserves (SOR)
  Physical, secure MW + MWh reserves to increase the demand for (and hence the total supply of) winter preparedness
  Replaces ISO-NE’s RER, which is only a call option on RT energy
Introduces DA Operating Reserves (OR) (TMSR/TMNSR/TMOR)
  Forward contracts to provide physical RT OR
  Not designed for winter energy security, but needed to ensure that enough resources are set aside in DA to meet RT OR requirements, in addition to those supplying DA SOR
  Replaces ISO-NE’s GCR, which is a call option on RT energy
Does not address virtual participation in the DAM (i.e., no EIR)
  Not clear at this point that virtuals pose a winter security problem or that the concerns need to be addressed right now as part of this Chapter 3; does not preclude addressing this issue in the future
NEER presents an alternative proposal that would much more effectively align price signals with objectives
NEER’s Alternative relies on physical reserve products in DA and RT, rather than on DA financial call options on RT energy

## Slide 5: NEER “Strategic Operating Reserve” Alternative
Strategic Operating Reserves (SORs) are secure MW+MWh procured and held by ISO-NE as backup to protect against adverse conditions, consistent with ISO-NE reliability objectives
  Ensure that the system can sustain a prolonged contingency that would reduce energy-secure supply during a cold snap.
Holding SORs in both DA and RT maintains market consistency and properly increases the demand for physical energy and reserves to internalize value that might otherwise be met out of market
The resulting prices signal the desired increased preparedness in the operating, procurement, and investment timeframes
  Expectations for scarcity would translate to forward prices and influence fuel procurement and investment/retention of energy-secure resources
“Strategic Operating Reserve” is designed specifically to address stated ISO-NE operator needs for fuel security

## Slide 6: Strategic Operating Reserve Product Definition
SORs are a new type of reserve purchased by ISO-NE specifically because they have secure MWhs
Provided by secure MWh-backed MWs:
  Oil-fired units with on-site fuel inventory
  Gas-fired units with secure fuel supply
  Pondage hydro (depending on their reservoir level)
  Pumped hydro/batteries (depending on their reservoir level/state of charge)
Units can have up to a 12-hour notification time for deployment
  Unlike traditional reserves, these units are valued because of their MWh security, not because they are fast-start units
SORs provide MWh security on the system in the day-ahead market
SORs are oil units, firm fuel, LNG options, storage

## Slide 7: Resource Offers in the DAM: SOR, Energy and OR
Energy offers: 3-part offers, same as today
DA OR offers:
  Separate offer curve (MW and corresponding $/MWh) from energy
SOR units offer to provide SORs and/or energy and DA OR in the Day-Ahead Market (or Multi-Day Ahead Market)
  Offer parameters (could also be developed as curves):
    MW,
    $/MWh,
    Volumes of secure MWh available to (two separate volumes):
      back the MW associated to the SOR offer during the day
      back the MW associated to the energy+SOR offer during the day
Prices for SOR include energy and reserves opportunity cost and SOR offer price of the SOR marginal unit
SORs are purchased day-ahead consistent with winter security being mostly a multi-day challenge, not a real-time surprise

## Slide 8: Day-Ahead Market Clearing with SORs
ISO-NE to co-optimize SOR suppliers with energy and OR
  Clearing engine tries to select the full amount of energy, OR and SOR at least cost
    MWs may be designated as either SOR, OR or energy only – SOR MWs cannot also clear for energy and OR
  DA (and RT) demand for SOR expressed through a “demand curve” allowing sacrifice of SOR for higher-value energy/OR, for a penalty, much like the RCPFs for current ancillary services (see later slides)
  Co-optimization also appropriately rewards all resources that provide energy and OR when inventory becomes tight (when SOR is scarce/costly, energy and OR prices rise even before shortages of energy and OR actually occur).
SORs are then paid a separate SOR clearing price and do not receive the Day-Ahead Market energy clearing price
By virtue of the co-optimization, prices account for opportunity costs and are consistent with the dispatch:
  Units do not have incentives to deviate from market clearing solution
Prices for SOR include energy and reserves opportunity cost and SOR offer price of the SOR marginal unit

## Slide 9: Modeling of SORs in RAA
SOR requirements will be modeled in RAA, consistent with DA, and similar to the way OR is modeled in RAA
Role of RAA: determine the need to start additional units, including those that cleared SOR in DA, to ensure reliable RT operations
  Same as today
  Under fuel scarcity conditions that require SOR deployment (e.g., no other resources are available), if DA SOR suppliers are offline RAA determines which of those suppliers must be started
Resource start during RAA provides advantages
  Takes into account longer lead time resources
  May also provide good timelines for calling on LNG options
Offline DA SOR suppliers may be called to start during the RAA process (NEW SLIDE)
RAA is the same as today’s except that there is a new reserve product added, SOR

## Slide 10: Real-Time Market Clearing with SORs
RT dispatch seeks to minimize the cost of meeting energy + OR + SOR demand curve
Deployment of SOR would only occur when needed to meet higher-value energy and OR
  DA SORs deployed in RT are from online (committed in DA, RAA or self-committed) or fast-start resources – respect operating parameters
  DA SOR deployment creates a shortfall of SORs in the real-time market, which increases the RT SOR prices through the SOR demand curve
When SOR deployment occurs, there will likely be a shortage of SOR, and $0-900 RCPF translates into high prices for SOR, energy, and OR.
  When taking one more MWh of energy or reserves reduces SOR clearing, SOR prices are set by the demand curve (which will be designed up to the RCPF)
Online and fast-start DA SOR suppliers may deployed in RT, to supply energy or OR under fuel scarcity conditions (REVISED SLIDE)

## Slide 11: RT Market Clearing and Settlement with SORs
Resources will be dispatched in RT based on their incremental offers, co-optimizing their energy, SOR and OR positions
  SOR RT offers are limited to the DA MWh offered, for consistency and in recognition that SOR is effectively a DA product.
  SOR clearing is re-optimized in RT to further improve market efficiency:
    RT SOR prices are used to settle changes in SOR positions from DA, both due to non-performance and for deployment (including self-scheduling)
    RT SOR clearing provides updated SOR allocations when it becomes optimal to deviate from DA plans.
DA SOR deployed in RT (dispatched for energy or OR in RT) buys back the SOR position at the RT SOR price and gets paid the energy or OR RT price, making an incremental profit
RT Dispatch and Settlement is the same as today’s except that there is a new reserve product added, SOR (REVISED SLIDE)
RT SOR clearing sends proper price signals into the market, whether holding or deploying SOR as needed

## Slide 12: Real-Time SOR Offers
DA SOR resources can self-schedule for energy in RT
  They would be buying out of their DA SOR position at RT SOR prices
SORs to have the ability to re-offer in RT
Resources qualified to offer SOR in RT are
  Those that cleared for SOR in DA for that interval
  Those that offered but did not clear for SOR in DA in any interval
Resources that cleared SOR in DA for other intervals can offer up-to the MWh volume that was offered but did not clear in DA.
RT SOR eligibility is independent of the online/offline status of the unit, even for units that are not fast start
  RT SOR supply ensures there is secure energy in the system, even though it may not be deployable for a few hours
  Do not respect operating parameters
Suppliers can re-offer SOR in RT, and may self-schedule for energy (REVISED SLIDE)

## Slide 13: Example 1 – 12-hour Start Unit Offline in RT
Unit A is a 100 MW unit with 12-hour start time and qualifies to provide SOR (i.e., it has secure energy back-up)
In DA, unit A clears 100 MW for SOR (it is offline) at $3/MWh
In RAA the system is in similar conditions as in DA, unit A is not needed online to ensure reliable operations, thus it is not started
In RT, unit A clears 100 MW for SOR (i.e., does not change its SOR position) and stays offline
  RT settlement for unit A is $0
  Unit A gets DA SOR payment for 100 MW at $3,000
SOR-capable slow-start units can sell SOR in RT regardless of whether they are online or offline (NEW SLIDE)

## Slide 14: Example 2 – 12-hour Start Unit Committed in RAA
Unit A is a 100 MW unit with 12-hour start time and qualifies to provide SOR (i.e., it has secure energy back-up)
In DA, unit A clears 100 MW for SOR (it is offline) at $10/MWh
In RAA the system is forecasted to be in fuel scarcity conditions in 12 hours, unit A is determined to be needed to maintain reliability and it is started
  Unit A is guaranteed to recover its costs
In RT, unit A clears 50 MW SOR and 50 MW energy, where energy prices are $200/MWh and SOR prices are $100/MWh
  RT settlement for unit A is +$10,000 (energy settlement) - $5,000 (SOR settlement) = $5000
  Unit A gets DA SOR payment for 100 MW at $10,000
SOR-capable slow-start units are committed in DA or RAA to convert their SOR position to energy or OR when needed

## Slide 15: Strategic Operating Reserve Purchase
Amount of Strategic Operating Reserves to be purchased by ISO-NE based on pre-determined planning criteria
  Similar to other reserves, ISO-NE to publish a requirement (expressed in a demand curve) each day of how many MWs of SOR they need to run the system reliably
  The requirement will dictate how much and at what price ISO-NE will buy SORs
SORs are committed specifically for the purpose of providing operator certainty as to energy security
SORs are oil units, firm fuel, LNG options, storage

## Slide 16: SOR Demand Curve in DA and RT
Could be 1-2 GW minimum for each hour of the next day (or multi-days-ahead), subject to an RCPF of $900/MWh, consistent with deploying to avoid shortages of 30-min OR @$1000/MWh
Then sloping down and rightward from there, as a gradual ORDC provides better price formation
  Size and number of participating units is large relative to the need
  Minimum quantity could be the largest resource contingency
  Maximum quantity could be the sum of the two largest contingencies
Could keep demand simple, invariant to current/forecast conditions, which will naturally suit a variety of conditions:
  If tight and the resource is needed for energy, it will be deployed
  If not, the price will be low
A demand curve is proposed by NEER to purchase SOR subject to a cap equal to the RCPF of $900/MWh
Creating a demand curve addresses lumpiness issues and creates a stronger price signal

## Slide 17: Example SOR Demand Curve
NEER SOR Demand Curve
Creating a demand curve addresses lumpiness issues and creates a stronger price signal
$/MW price
MW quantity
Min quantity, e.g., largest resource contingency
RCPF: $900/MW
Max quantity, e.g., sum of two largest contingencies

## Slide 18: SOR Penalties for Non-Availability / Performance
The RT SOR clearing price also determines the “cost to cover” for any resource that has committed to providing reserves but becomes unavailable (e.g., self-reports unavailability to meet SOR obligations)
And if SOR is called to deploy energy but cannot deliver, the penalty could be the sum of the RT SOR and the RT energy price
NEER to incorporate penalties where a resource cannot cover its obligation
NEER to develop non-availability and performance penalties

## Slide 19: DA Operating Reserves (OR)
Purchased by ISO-NE in DA (TMSR, TMNSR and TMOR)
  DA OR are physical reserve products, not financial call options
  DA OR meets the same criteria as the OR products in the RT
DA OR suppliers have the financial obligation to provide the corresponding OR product in the RT
  DA OR suppliers can trade their DA obligations in the RT
DA OR and SOR DA offers and clearing prices are different
  DA OR and SOR qualification criteria, quantities and offers will differ
ISO-NE would co-optimize energy, OR and SOR in DA
  Existing OR are presently procured in real-time; DA co-optimization has been an open item/action item for many years in New England
NEER Alternative can incorporate ISO-NE design elements, including day-ahead optimization of existing reserves
DA OR are separate and different products from SOR

## Slide 20: Forward Incentives: Part Two
ISO-NE has indicated that post-filing, it will look at a seasonal forward market
  Voluntary, competitive forward auction to provide asset owners with incentives and compensation to invest in supplemental supply arrangements for the coming winter
  If done incorrectly, a seasonal forward market is likely to depress energy market prices and provide the wrong incentives
FCM could be reformed to consider “demand” for winter-energy-secure infrastructure to be procured competitively in FCM
  Reforming FCM is not currently proposed by ISO-NE, but perhaps it should be considered if ISO-NE would otherwise consider RMRs based on its own years-ahead assessment of infrastructure adequacy
Getting energy markets designed right is a necessary step against any other out-of-market interventions in the future that could be harmful to the market
A physical SOR, coupled with the right forward incentives is key

## Slide 21: Appendix

## Slide 22: SOR DA & RT Dispatch & Settlement Examples
Simplified, illustrative system:
  Two hours modeled, as if the day were 2 hours (instead of the full 24)
  Load: 700 MW (for both hours)
  SOR requirement: 300 MW, no Operating Reserves
  No energy-limited units, some SOR-limited units
Will analyze market clearing under three different scenarios:
  Example 1: Normal conditions; in this example we illustrate both DA and RT settlements when RT conditions differ from DA
  Example 2: Near fuel scarcity (some units with reduced SOR capability); DA example only
  Example 3: Fuel scarcity (unit outage in addition to Example 2 conditions); DA example only
NEER proposal creates appropriate incentives for fuel scarcity conditions
Under NEER’s Alternative to the ISO-NE proposal, DA and RT dispatch and prices change as a function of fuel scarcity

## Slide 23: DA Example 1 – Normal Conditions
DA Energy price: $42/MWh
DA SOR price: $2/MWh
NEER proposal creates appropriate incentives for fuel scarcity conditions
Under normal conditions, SOR price is low, and energy prices do not change with respect to today’s design
Unit D sets LMP
Unit F sets SOR price
SOR Offer MWh is the max MWh sum over hours 1 and 2
market clearing is the same for both hours

## Slide 24: DA Example 1 – Normal Conditions
DA Energy price: $42/MWh
DA SOR price: $2/MWh
C
A
NEER proposal creates appropriate incentives for fuel scarcity conditions
Under normal conditions, SOR price is low, and energy prices do not change with respect to today’s design
price
$/MWh
$10
$60
$50
$40
$30
$20
B
D
F
energy price
cleared for SOR
cleared for energy
quantity MW
load
load + SOR req
E
Unit D sets LMP
Unit F sets SOR price

## Slide 25: RT Example 1 – RT Load Higher than Anticipated DA
RT load is 850 MW, higher than the 700 MW forecasted in DA
RT Energy price: $60/MWh, RT SOR price: $2/MWh
NEER proposal creates appropriate incentives for fuel scarcity conditions
Under normal conditions, SOR price is low, and energy prices do not change with respect to today’s design
Unit F sets RT LMP
Unit F sets RT SOR price

## Slide 26: DA Example 2 – Near Fuel Scarcity (Posturing)
Prices derived on next slide
NEER proposal creates appropriate incentives for fuel scarcity conditions
As the fuel margin becomes tight, low-cost secure-energy units are set aside as reserves, increasing SOR and energy prices
Units E and F have reduced SOR capability (e.g., dual fuel units with limited oil in storage, non-firm gas supply)
SOR Offer MWh is the max MWh sum over hours 1 and 2
market clearing shown is the same for both hours (not unique)
SOR MWh limits reached for units E and F, unit D clears for SOR, unit E clears for energy

## Slide 27: DA Example 2 – Near Fuel Scarcity (Posturing)
DA Energy price: $60/MWh
DA SOR price: $24/MWh
C
A
NEER proposal creates appropriate incentives for fuel scarcity conditions
As the fuel margin becomes tight, low-cost secure-energy units are set aside as reserves, increasing SOR and energy prices
price
$/MWh
$10
$60
$50
$40
$30
$20
B
D
F
energy price
cleared for energy
quantity MW
load
load + SOR req
E
Unit D sets SOR price at offer plus its energy opportunity cost:
Unit E sets LMP

## Slide 28: DA Example 3 – Fuel Scarcity
Prices derived on next slide
NEER proposal creates appropriate incentives for fuel scarcity conditions
As the fuel margin becomes tight, low-cost secure-energy units are set aside as reserves, increasing SOR and energy prices
Units A is out of service
SOR requirement not met
market clearing shown is the same for both hours (not unique)
SOR Offer MWh is the max MWh sum over hours 1 and 2

## Slide 29: DA Example 3 – Fuel Scarcity
F
DA Energy price: $936/MWh
DA SOR price: $900/MWh
C
NEER proposal creates appropriate incentives for fuel scarcity conditions
When fuel becomes scarce, the SOR price is the RCPF and energy prices are above it, reflecting scarcity conditions
price
$/MWh
$10
$60
$50
$40
$30
$20
B
D
quantity MW
load
load + SOR req
E
SOR price set by RCPF
Unit D sets the energy price at its offer plus its SOR opportunity cost:
SOR shortage, price set by RCPF