## Slide 1
December 11, 2019| Markets committee
Chris Geissler
413.535.4367
cgeissler@iso-ne.com
How the ESI design incents resources’ fuel arrangements in advance of winter
ENERGY SECURITY IMPROVEMENTS: MARKET-BASED APPROACHES

## Slide 2
Winter Energy Security Improvements
WMPP ID:
125
Proposed Effective Date: June 1, 2024
In accordance with FERC’s July 2, 2018 order in EL18-182-000, the ISO must develop and file improvements to its market design to better address regional fuel security, and file by April 15, 2020
Key Projects – Energy-Security Improvements
  Discussion Paper 2019-04-09 and 2019-04-10 MC A00 ISO Discussion Paper on Energy Security Improvements – Version 1

## Slide 3: Key Issue: How ESI incents resource owners to make advance fuel arrangements
This presentation will address:
How ESI creates an incentive to make cost-effective fuel arrangements before the DA market is cleared
How ESI can create this incentive without a forward market component
This presentation will use economic principles and a numerical example
  We extend the observations in the ISO’s December 4th memo to the Markets Committee, Energy Security Improvements: How Market Improvements Address Fuel Security

## Slide 4: Key Takeaway: ESI will increase incentives for cost-effective advance fuel arrangements
ESI introduces new revenue streams by which resource owners can profit from improved fuel supply arrangements
  Revenues from selling DA options, and/or FER revenue associated DA energy supply
ESI increases the incentive for resources to make such arrangements, including instances where they are made months in advance of the delivery period
Therefore, we expect that ESI will improve the region’s winter energy security

## Slide 5: Markets incent investors to incur costs that they expect to yield profits
Many types of costs are incurred well in advance of delivery, before the compensation is known, both in electricity and other commodity markets, including:
  Capital costs of building a power plant or an automobile factory
  Long-term supply chain arrangements or input price hedges
  Many other types of capital costs including planting crops, maintaining inventory, etc.
Participants may incur these costs before they have contracts in place with consumers to buy their output
Markets create incentives for participants to incur these costs when they expect that they will profit from such investments

## Slide 6: Current market rules may not incent all cost-effective advance fuel arrangements by resource owners
Resources are likely to incur costs if they expect to profit via increased revenues from the following:
  DA and RT energy markets
  RT ancillary service markets
  (Increased) PFP revenues
However, the misaligned incentives problem may prevent these markets from currently compensating resources for fuel arrangements commensurate with their social benefits
  See Section 2.2 of ISO’s April discussion paper

## Slide 7: ESI introduces new revenue streams that will help to address the misaligned incentives problem and better incent advance fuel arrangements
ESI introduces new revenues streams that may help to offset the costs associated with procuring additional fuel and address the misaligned incentives problem
  Revenues from sale of DA options
  Additional FER revenue for DA energy
These new revenue streams may increase the likelihood that market participants make advance fuel arrangements
  For some (e.g., highly inframarginal) resources, current market rules may already incent cost-effective advance fuel arrangements

## Slide 8: Numerical example
How ESI improves incentives for socially beneficial advance fuel arrangements

## Slide 9: ESI will generally incent resources to invest in fuel when cost effective to do so
The new revenue streams introduced under ESI will better allow resources to be more fully compensated for the social benefit of their advanced fuel arrangements
As a result, expect that market participants will be more likely to make advance fuel arrangements when doing so increases social surplus
This is true even if the fuel arrangements must be made well in advance of (e.g., months before) the winter day-ahead markets operate
Demonstrate this property with a numerical example (next)

## Slide 10: Example: Setup and assumptions
Consider the fuel arrangement decision of a hypothetical 50 MW peaker generator, which we’ll call “Gen A”
It is making a fuel arrangement decision for an entire winter
  For simplicity, assume winter is 100 hours long
We assume that Gen A does not expect to clear for energy in the DAM, but may sell RT energy during periods it is in demand

## Slide 11: Example: Gen A’s costs to make fuel arrangements
If Gen A makes advance fuel arrangements, it will incur:
  A marginal cost of $40/MWh to produce energy, and
  An additional up-front cost of $35,000 (regardless of whether it runs or not)
  This arrangement can take various forms, such as buying LNG in the summer preceding the winter delivery period
If Gen A does not make advance fuel arrangements, has marginal costs of $300/MWh to produce energy (assuming it can get fuel) and incurs zero up-front fuel arrangement costs

## Slide 12: Example: Winter conditions assumptions
Gen A expects RT prices will ‘spike’ in 10 hours (over the course of the winter)
  Real-time price during spikes if Gen A makes fuel arrangements is $100/MWh (where it is infra-marginal)
  RT price during spikes if Gen A does not make fuel arrangements is $150/MWh (where it is out of the money)
The specific hours in which prices spike during the winter are not known prior to real-time
Gen A therefore does not produce energy if it does not make advance fuel arrangements
RT energy price during ‘non-spike’ hours ≤ $40/MWh
  Gen A does not run during non-spike hours, regardless of its fuel arrangement

## Slide 13: Example: Assumptions Summary
Gen A Assumptions | With Forward Fuel | Without Forward Fuel
Up front cost | $35,000 | $0
Marginal cost | $40/MWh | $300/MWh
RT price during spikes | $100/MWh | $150/MWh
RT price during non-spikes | ≤ $40/MWh | ≤ $40/MWh
Winter Assumptions | 
Total winter hours | 100
Expected number of hours with price spikes | 10

## Slide 14: Without ESI, Gen A earns negative expected net revenues from the advance fuel arrangement
Key point: Current market rules would not incent Gen A to make this fuel arrangement despite the fact that it improves social welfare (see next slide)
Incremental Net Revenues From Advance Fuel Arrangement | 
Up front cost | – $35,000
Energy revenues | $50,000 (50 MW ×10 hr × $100/MWh)
Production costs | – $20,000 (50 MW ×10 hr × -$40/MWh)
Expected net revenues | – $5,000
Return on investment (ROI) | – 14% (-$5,000 / $35,000)

## Slide 15: Society is better off if Gen A makes the advance fuel arrangement
Society is therefore better off if Gen A makes this fuel arrangement, as it can do so at lower cost
Because Gen A would not make such an arrangement, this example illustrates a case where, under current rules, the misaligned incentives problem occurs
Costs of serving the 50 MWh of load during price spikes | 
Gen A’s total cost | $55,000 ($35,000 + 50 MW × 10 hr × 40/MWh)
‘Replacement’ resource | $75,000 (50 MW × 10 hr × $100/MWh)
Social benefit (savings) | $20,000 (or $75K – $55K)

## Slide 16: Example: DA option strike price
Assume that the strike price for all hours is $40/MWh
  Equal to Gen A’s marginal costs if it arranges fuel (just to simplify the calculations ahead; a little higher or lower would also work)
  This means there’s no option closeout cost during non-spike hours, because the strike price is greater than or equal to the (assumed) real-time LMP during non-spike hours
Expected closeout cost across all winter hours, on average, if Gen A arranges fuel is $6/MWh:
  10 percent frequency of price spike in a given hour × $60/MWh closeout cost during price spike ($100/MWh LMP during spikes less the $40/MWh strike price)

## Slide 17: Example: DA option offer prices are informed by two components
As discussed in the ESI Impact Analysis, the price of DA ancillary services is likely to consist of two components
  Resource’s expected option closeout cost ($6/MWh in this example)
  An additional risk component
Risk component will generally be larger for resources that have greater “exposure” to high real-time prices
  I.e., resources that cannot fully hedge risk associated with high RT prices because their marginal costs exceed the strike price
Offers may also include any avoidable costs that are incurred after the DAM award is known and that reduce the risk associated with selling an option

## Slide 18: Example: Gen A’s advance fuel arrangements reduce its risk associated with selling DA options
Expect risk component of Gen A’s option offer price would be low, if it makes forward fuel arrangement
  It is ‘hedged’ because it can produce energy at the strike price, and therefore had no risk of loss from option closeout (in this example)
  Applying the methodology used in the Analysis Group in the production cost model, Gen A’s risk component would be $0/MWh
Assumption: Gen A’s option offer is infra-marginal for DA reserves, where the DA reserve clearing price is $8.50/MWh
  Reflects a $6/MWh expected close-out cost (see slide 14), and
  A $2.50/MWh risk component from the marginal option offer
  Gen A’s return on investment for an advance fuel arrangement increases with the $ value of this (marginal) risk component

## Slide 19: Example: With ESI, Gen A earns positive expected net revenues from advance fuel arrangement
ESI incents Gen A to make this cost-effective forward fuel arrangement, whereas current market rules do not
ESI solves the misaligned incentives problem, even if fuel must be arranged well in advance of the DA markets
Incremental Revenues From Forward Fuel Arrangement | 
Up front costs | -$35,000
Option net revenues | $12,500 (50 MW × 100 hr × ($8.5/MWh - $6/MWh))
Energy revenues | $50,000 (50 MW × 10 hr × $100/MWh)
Production costs | -$20,000 (50 MW × 10 hr × -$40/MWh)
Expected net revenues | $7,500
ROI | 21% ($7,500 / $35,000)

## Slide 20: Gen A invests in (“sunk”) advance fuel arrangements before winter, and appropriately bears risk/return
Gen A is not ‘guaranteed’ $7,500 in net revenues from making its forward fuel arrangements
  Actual prices and net revenues are commensurate with supply and demand conditions during the delivery period
If Gen A does not expect to recover its costs from this fuel arrangement, it should generally expect that another resource can provide the same reliability services at lower cost
If Gen A’s assumptions about its performance during spikes, or those market conditions, turn out to be incorrect, its profits (and ROI) could be higher or lower
  E.g., if the option clearing price exceeds $8.5/MWh, advance fuel arrangements will yield greater profits, and vice versa

## Slide 21: ESI design creates strong incentives to perform in real-time and accurately forecast market conditions
Market participants have a strong incentive to develop accurate forecasts of performance, market conditions, etc.
Inaccurate forecasts may lead a participant to:
  Make fuel arrangements that are not profitable, or
  To forgo making fuel arrangements that are profitable
Accurate forecasts may reduce risks, but they do not entirely eliminate them
  E.g., could end up with more/less than 10 winter price spikes, different energy or option prices, or so forth
Risk-averse market participants may consider this uncertainty, and how it compares to the expected ROI, when determining how to invest in advance fuel arrangements

## Slide 22: Summary: ESI incents suppliers to make cost-effective advance fuel arrangements
Market participants make advance fuel arrangements when they expect higher incremental revenues and sufficient ROI
  This is true even if the fuel investment costs are irreversible
ESI increases the number of revenue streams to cover the costs and the ROI associated with such arrangements
This example shows how ESI can incent a socially efficient forward fuel arrangement in advance of the DA market
ISO continues to assess if a forward ancillary service market could further enhance cost-effective fuel procurements
  Plan to discuss this topic with the committee at future meetings