## Slide 1: Energy Security Improvements Impact Analysis
Todd Schatzki
Principal
January 15, 2020

## Slide 2: Agenda
  Update to Central Case Results
  Winter Case Scenario Analysis
  Non-winter Month Analysis
  Appendices
    Incentives for energy inventory
    Detailed Scenario Analysis Results

## Slide 3: Status and Progress to Date
  We appreciate the feedback provided by stakeholders, as it has helped inform many of the model's assumptions
  We have received many requests for additional results, analysis, and scenarios; we have worked diligently to be as responsive as possible, although time constraints have affected our ability to respond to all requests
  Our work continues, and we hope to respond to requests not addressed in upcoming presentations and in the report
  Today we present results for:
    Winter Month Central Case ‒ updated results
    Winter Scenarios ‒ selected scenarios
    Non-Winter Months ‒ one Case
Several changes in assumptions

## Slide 4: Update to Central Case Results

## Slide 5: Update to Central Case Results
  Results reflect several changes in assumptions relative to those presented at the December MC
    ESI shortage prices
      ESI shortages prices were set at levels above the levels currently proposed by ISO-NE
      Updated results reflect values consistent with ISO-NE proposal
    Adjustment to treatment of variable renewable (solar, wind) participation in the DA market
    Other adjustments to model parameters, including day-ahead demand and fuel oil inventory assumptions
Several changes in assumptions

## Slide 6: Update to Central Case Results
  Qualitative findings remain consistent with results presented previously
    ESI procures new ancillary services day-ahead to improve system reliability, increasing the supply of energy inventory and reducing stress of fuel supply systems
    ESI would cause DA markets to clear energy supply levels closer to the ISO forecast load
    ESI may cause shifts in energy use through more efficient use of energy inventory that can lower production costs
      For example, shifts in energy supply from resources with stored energy inventories to those with just-in-time fuel supply
Summary of Changes in Results

## Slide 7: Update to Central Case Results
  Modeling updates have led to some changes in estimated ESI’s impacts relative to previously reported preliminary results ‒ for example:
    Impact on total customer payments reduced
    Impact on net revenues reduced (less positive), with some categories of resources facing reductions in net revenues, on average
  Below, key result updates are highlighted, with more detailed results provided in the appendix
Summary of Changes in Results

## Slide 8: LNG Contract Structure is Not a Key Determinant in Model’s Estimates
  Model makes simplifying assumptions to estimate ESI’s impact in a timely manner
  Analysis assumes a call-option contract structure ‒ as previously stated:
    Estimated impacts do not meaningfully depend on choice of contract structure
    Model assumes LNG is used during stressed periods, when it is lower cost than pipeline gas
Observations Regarding Repsol’s Letter and Presentation

## Slide 9: Changes in Model’s Available LNG are Unlikely to Significantly Affect Model’s Estimated ESI Impact
  Model’s ‘full supply’ assumption may overstate available LNG in some cases
    However, incentive to hold LNG increases as system conditions become more stressed
  We include a scenario with less available LNG, and ESI’s impact appears similar to Central Cases
Observations Regarding Repsol’s Letter and Presentation

## Slide 10: Update to Central Case Results: Payments and Prices

## Slide 11: Payments and Prices
  ESI’s impact on total customer payments is ambiguous
    Increased payments in 2 of 3 Cases
    Depends on level additional energy inventory incented by ESI
  Level of some impacts have changed, relative to previously reported preliminary results ‒ for example:
    Total customer payments lower across Cases
Key Takeaways

## Slide 12: Total Customer Payments
Central Cases
Total Payments by Case ($ Million)
  Total customer payments increases in some Cases (Frequent, Infrequent) and decreases in others (Extended)
    Payments increase due to FER payments plus net cost of new DA energy options
    These higher payments are partially or more than fully offset by reduced energy (LMP) costs caused, partly, by the incremental energy inventory under ESI

## Slide 13: LMPs
Central Cases
  With ESI, LMPs generally decline compared to current market rules
    Reductions range from $0.21 to $6.09 per MWh, driven by incremental energy supplies and other factors
  DA and RT prices are generally aligned, consistent with arbitrage between DA and RT markets, which will continue to promote efficient pricing in DA markets under ESI
Average Day-Ahead and Real-Time LMPs by Case ($ per MWh)
Note: [1] Prices are the unweighted average across hours.

## Slide 14: Payments to Day-Ahead Energy
  DA energy is compensated with both LMPs and FER payments
    Average FER payment (column [C]) is the weighted average across all DA energy
  Average compensation (per MWh) to DA energy increases under ESI (compared to CMR) in two of three Cases (Frequent and Infrequent)
    In Extended Case, LMPs reductions exceed FER payments, on average
  FER payments for DA energy increases the return to holding energy inventory, all else equal
Weighted Average DA Energy Payments to Generators, CMR vs ESI ($ per MWh)
Central Case
Note: [1] Prices are weighted by hourly quantity of generation.

## Slide 15: Incremental Fuel Oil Incentives Relative to Current Market Rules
  Compared to CMR, net incentives to maintain energy inventory increase for all types of oil-fired resources
  Updated results ‒ with revised categories ‒ are included in the appendix
  As in prior analyses:
    In the Frequent and Extended Cases, new FER payments and DA energy options (for ESI AS products) exceed incremental holding costs
    In the Infrequent Case, plants with dual fuel capabilities continue to receive positive returns for holding incremental energy inventory, while oil-only, incur negative returns, as these units infrequently supply energy and DA energy options
    Incremental energy inventory may not be beneficial under all market conditions, particularly when market conditions (including weather conditions) provide sufficient supplies of energy inventory
Summary of Changes in Results

## Slide 16: Incremental LNG Contract Incentives Relative to Current Market Rules
  Compared to CMR, net incentives to enter into a forward LNG contracts are increased under ESI
  Incremental revenues associated with signing an LNG contract are greater under ESI because of additional revenues from FER payments and award of DA energy options
  Results are similar to those presented in December 2019
Summary of Changes in Results

## Slide 17: Update to Central Case Results: Energy Supply

## Slide 18: Changes in DA Energy With ESI
Difference in Cleared DA Energy by Resource Type, CMR vs ESI, Central Cases
  With ESI, total cleared DA energy increases (compared to CMR)
    Adjustment due to cost savings of substituting DA energy for EIR, which does not incur a cost under CMR
    This substitution leads EIR to be relatively small in most cases
  With ESI, cleared DA energy quantities are more similar to system real-time demand than under current market rules

## Slide 19: Energy Supply
  With ESI, the mix of energy supply shifts
    Under ESI, DA energy supply generally increases for all resource types, with certain exceptions
      Increase in DA energy greatest for dual-fuel and gas-only
      Oil-fired steam supply increases across Cases, as well
    DA energy options supplied largely by pumped storage, GT’s (dual fuel, oil-only and gas-only), hydro and CC’s (dual fuel and gas-only)
    Some substitution from DA energy to DA energy options (particularly, oil-fired GT’s)
  Detailed results in Appendix
DA Energy and Energy Option Mix

## Slide 20: Update to Central Case Results: Net Revenues and Production Costs

## Slide 21: Net Revenues and Production Costs
  Total production costs are reduced in Cases where the incremental fuel ESI incents is used to displace generation from higher cost, less efficient units
    Change in production costs may be understated, as distribution of incremental energy inventory across resources may not reflect optimal allocation
  Changes in net revenues vary across Cases and resource types, on average
    Net revenues reflect multiple factors, including changes to LMPs, new FER payments and ESI awards for DA energy options
    Changes sensitive to amount of incremental energy inventory incented by ESI across all resources
Key Takeaways

## Slide 22: Production Costs
Production Costs, with and without ESI, Central Cases
  Production costs lower in 2 of 3 cases despite increased DA energy market requirements

## Slide 23: Net Revenues
Average Net Revenues by Resource Type, Winter Season, Frequent Stressed Conditions ($ per MW)

## Slide 24: Net Revenues
Average Net Revenues by Resource Type, Winter Season, Extended Stressed Conditions ($ per MW)

## Slide 25: Net Revenues
Average Net Revenues by Resource Type, Winter Season, Infrequent Stressed Conditions ($ per MW)

## Slide 26: Update to Central Case Results: Operational and Reliability Outcomes

## Slide 27: Operational / Reliability Metrics
  Operating reserve shortages. Hours of 10- or 30-minute operating reserve shortage
  Natural gas consumption when natural gas supply is tight. Change in natural gas consumption during periods when NG supply is tight, as reflected by high prices (> $16 / MMBtu), net of NG from forward LNG contracts
  Minimum daily deliverable energy from oil-fired units. Minimum daily quantity of energy (MWh) available from oil-only and dual-fuel resources given actual fuel inventory
  Average daily deliverable energy from oil-fired units. Average daily quantity of energy (MWh) available from oil-only and dual-fuel resources given actual fuel inventory
  Maximum 4-day drop in energy inventory. Largest drop in energy inventory over a 4-day period.
Multiple Metrics to Capture Different Aspects of Energy Security

## Slide 28: Operational / Reliability Metrics
Multiple Metrics to Capture Different Aspects of Energy Security
Change in Reliability Metric with ESI compared to CMR
Central Cases
  Consistent with prior results, ESI generally relaxes energy physical and economic constraints
    Reduced reliance on NG supply when supplies are constrained (prices are high)
    Increased energy inventory
    Reduced draw-down on energy inventory during periods of need

## Slide 29: Scenarios - Reliability
Daily Oil Available for Real Time Generation, Frequent Stressed Case (MWh)
Maximum Daily Potential Generation from Oil-fired Resources, CMR vs ESI, Frequent Stressed

## Slide 30: System Operations and Reliability
  ESI generally expected to improve system operations and reliability
    Increased energy inventory reduces risk of operational events
    Reduced reliance and stress on fixed fuel (natural gas) delivery systems
    Compensation for DA energy option helps to preserve energy inventory, while shifting energy supply to resources with just-in-time fuel supplies (i.e., natural gas)
      Magnitude of this effect will tend to increase as system conditions become more stressed
Key Takeaways

## Slide 31: Preliminary Scenario Analysis Results

## Slide 32: Scenarios Presented
  The Scenarios evaluated seek to be responsive to the set of stakeholder requests we have received to date
  Particular Scenarios being analyzed are described on the following page
    These descriptions list all of the changes in assumptions for each Scenario
    One Scenario ‒ “Strike Hourly” ‒ assumes an hourly-varying strike price that is consistent with ISO-NE’s current design thinking
  Scenarios are organized into two groups:
    Changes to ESI Design
    Changes to Resource or Demand Assumptions
  Results are preliminary, and we continue to evaluate results to develop more insight into expected ESI impacts
Set of Scenarios Presented Today

## Slide 33: Scenarios Presented

## Slide 34: Scenarios - Customer Payment Impacts
  ESI’s impact on consumer costs varies across scenarios and Cases
    Range from reduction of $316 million to increase of $407 million
    Impact is complex, reflecting multiple factors, including:
      Changes in and nature of change in market tightness (e.g., High Load, 1- and 5-day Supply Shocks, More/Less LNG supply)
      Changes in costs (e.g., higher risk premiums)
      ESI design (e.g., higher RER quantity)
Impacts Vary Across Cases and Scenarios

## Slide 35: Scenarios - Prices
  Across cases:
    LMPs decrease due to increased energy inventory incented by ESI and increased DA energy supply (at lower LMPs)
    FER prices range from $1.47 to $20.40 per MWh
    DA energy option prices vary across Cases, but relatively similar across Scenarios within Cases
Impacts Vary Across Cases and Scenarios

## Slide 36: Scenarios - Summary Results
Frequent Stressed Case

## Slide 37: Scenarios - Summary Results
Extended Stressed Case

## Slide 38: Scenarios - Summary Results
Infrequent Stressed Case

## Slide 39: Scenarios – Operational and Reliability Outcomes
  Across scenarios, ESI causes positive operational improvements through incremental fuel supply and substitution of resources with just-in-time energy supply for inventoried energy
    Fewer operating reserve shortages during 5-day supply contingency (“Shock HQ 5 Days”) in Frequent Case
    Use of natural gas when prices are high (i.e., NG supply is tight) decreases under all scenarios, illustrating how ESI reduces stress on fuel systems
    System-wide quantity of fuel oil inventory generally higher under ESI
    Depletion of oil inventory during periods of high demand (i.e., “cold snaps”) reduced under ESI
Impacts Vary Across Cases and Scenarios

## Slide 40: Operational / Reliability Metrics
Multiple Metrics to Capture Different Aspects of Energy Security
Change in Reliability Metric with ESI compared to CMR, Frequent Stressed Conditions

## Slide 41: Operational / Reliability Metrics
Multiple Metrics to Capture Different Aspects of Energy Security
Change in Reliability Metric with ESI compared to CMR, Extended Stressed Conditions

## Slide 42: Operational / Reliability Metrics
Multiple Metrics to Capture Different Aspects of Energy Security
Change in Reliability Metric with ESI compared to CMR, Infrequent Stressed Conditions

## Slide 43: Preliminary Non-Winter Month Analysis

## Slide 44: ESI Impacts in Non-Winter Months
  Framework for analysis of ESI during non-winter months is largely the same as the analysis for winter months
  Analysis considers different levels of stressed conditions in a future non-winter, 2026:
    Moderate Conditions based on 2017 (March through November)
      Moderate or typical non-winter market conditions
  Results are preliminary, but provide reasonable estimates of impacts for the cases evaluated
Fundamentals of Impact Approach

## Slide 45: Preliminary Non-Winter Central Case – Assumptions
  Key assumptions (discussed in November MC, as well):
    Demand escalated in manner consistent with winter approach (reflecting ISO forecasts for 2026)
    Supply
      Variable renewable profiles consistent with historical output, grown to anticipated future renewable supplies
      Available supplies reflect scheduled “shoulder” month maintenance outages
    Fuel supply (natural gas and fuel oil) not materially binding on market outcomes in these Cases
    No market responses to ESI incentives
    DA energy option offer prices adjusted for non-winter market conditions (with limited intra-day fuel price risk)
Data and assumptions generally consistent with winter analysis

## Slide 46: Preliminary Central Case Results – Overview
  Results today will cover the key impacts evaluated in our preliminary analysis, including:
    Changes in total customer payments under ESI
    Price signals, including LMPs and DA AS prices
    Quantities of DA energy and AS procured, and the shifts in DA cleared energy compared to current market rules
    Changes in net revenues to resource owners
    Operational and reliability outcomes
Scope of results to be discussed today

## Slide 47: Non-Winter Results: Payments and Prices

## Slide 48: Payments and Prices
  ESI increases total customer payments in non-winter months for the Case considered
    Consistent with procurement of additional reliability services
    Reflects assumption of no market responses to ESI incentives
  Change in LMPs and total payments to energy is relatively small
    In Moderate Case, total change in payments ‒ accounting for change in LMP and new FER payments ‒ is approximately ~ $0.25 per MWh
Key Takeaways

## Slide 49: Total Customer Payments
Central Case
Total Payments by Case ($ Million)
  Customers payments under ESI increase by $69 million (2.4%) in the Moderate Case
  Increases due to new FER payments and net cost of ESI AS products

## Slide 50: LMPs
Central Case
  With ESI, DA LMPs lower than under current market rules
    Market clears more DA energy
    LMPs “set” at demand offers, which are lower when clearing a greater quantity of supply
  No change in RT LMPs, as energy inventories and fuel use decisions unchanged by ESI given lack of tightness in energy supplies
Average Day-Ahead and Real-Time LMPs by Case ($ per MWh)
Note: [1] Prices are the unweighted average across hours.

## Slide 51: Payments to Day-Ahead Energy
  DA energy is compensated with both LMPs and FER payments
    Average FER payment (column [C]) is the weighted average across all DA energy
  Total compensation to DA energy increases under ESI (compared to CMR) reflecting combined impact to LMPs and new FER payments
    FER payments (more than) offset decrease in LMPs
Weighted Average DA Energy Payments to Generators, CMR vs ESI ($ per MWh)
Central Case
Note: [1] Prices are weighted by hourly quantity of generation.

## Slide 52: Day-Ahead Option Prices
  Weighted average hourly prices for EIR, GCR10, GCR30, and RER are:
    As with winter Cases, RER and GCR average prices are relatively similar, although this masks significant hour-to-hour variation in each
    EIR price is higher because prices are typically highest in hours when EIR quantity is large
Weighted Average DA Energy Option Clearing Prices ($ per MWh)
Note: [1] Prices are weighted by hourly quantity of each ESI product.
Central Case

## Slide 53: Non-Winter Results: Energy Supply

## Slide 54: Energy Supply
  ESI increases cleared DA energy, with cleared amount closer to the ISO forecast
  Under ESI, DA energy supply generally increases for all resource types, with certain exceptions
    Largest increases for CC units (dual fuel and gas-only)
    DA energy options supplied largely by pumped storage, GT’s (dual fuel, oil-only and gas-only), hydro and CC’s (dual fuel and gas-only)
Key Takeaways

## Slide 55: Changes in DA Energy With ESI
Difference in Cleared DA Energy by Resource Type, CMR vs ESI, Central Cases
  With ESI, total cleared DA energy increases (compared to CMR) due to cost savings of substituting DA energy for EIR
    EIR is small, as energy is substituted for EIR

## Slide 56: Total Non-Winter Generation Mix
Energy and DA Options by Resource Type, CMR vs ESI, Moderate Summer Conditions

## Slide 57: Non-Winter Results: Net Revenues

## Slide 58: Net Revenues and Production Costs
  Given assumption that there is no change in fuel availability or other response to ESI, total production costs are unchanged between CMR and ESI cases
  Net revenues generally increase by resource type, on average
    Net revenues reflect multiple factors, including changes to LMPs, new FER payments and ESI awards for DA energy options
Key Takeaways

## Slide 59: Net Revenues
Average Net Revenues by Resource Type, Non-Winter Season, Moderate Summer Conditions
($ per MW)

## Slide 60: Net Revenues
Average Net Revenues, Selected Resources, Non-Winter Season, Moderate Summer Conditions

## Slide 61: Next Steps
  January
    Additional Winter Scenarios
    Additional Non-Winter Central Case
  February
    Draft Report
Current plan for providing stakeholders with findings

## Slide 62: Appendix

## Slide 63: Central Case Detailed Results and Fuel Oil Assumptions

## Slide 64: Assumptions Regarding Fuel Oil Inventory and Replenishment
  Under CMR, initial inventory set to December 2017 storage
  Under ESI, initial inventory set relative to storage in December 2014-17
    Assumed values adjusted from historical values based on analysis of the benefits of additional fuel storage, relative to CMR levels
    Analysis reflects multiple factors, including unit’s marginal cost, volume stored under CMR (large for some units), and relative size of historical storage in 2017/18 compared to 2014-17
Initial Inventory Under ESI
Initial ESI Inventory Relative to 2014-17 Average December Storage

## Slide 65: Assumptions Regarding Fuel Oil Inventory and Replenishment
  The Table above provides assumptions for fuel oil inventories and replenishment at oil-only and dual fuel plants
    Assumptions vary based on tank size (days of fuel) and means for delivery (truck of barge)
    Refill threshold determines the trigger for replenishing fuel, (measured as a percent of maximum storage); for example, a plant with a tank with 4 days of fuel would replenish when the unit has 1.2 days of fuel remaining (4 days x 30%)
    When the trigger is hit, the plant receives a shipment, of quantity equal to the Rate of Fuel Delivery, after waiting the Order Lead Time
Fuel Oil Replenishment Assumptions

## Slide 66: Day-Ahead Option Prices
  Weighted average hourly prices for EIR, GCR10, GCR30, and RER vary across cases, but relatively within Cases, similar to prior results
    The weighted average price paid for EIR is generally higher because prices are typically highest in hours when EIR quantity is large
  EIR quantity zero in large fraction of hours, as market clearing substitutes energy for EIR to lower costs
Weighted Average DA Energy Option Clearing Prices ($ per MWh)
Note: [1] Prices are weighted by hourly quantity of each ESI product.

## Slide 67: Incremental Fuel Oil Incentives Relative to Current Market Rules
Cost Effectiveness of Additional Fuel – Central Case, Frequent Stressed Conditions
  Compared to CMR, net incentives to maintain energy inventory increase for all types of oil-fired resources
  In the Frequent Case, new FER payments and DA energy options (for ESI AS products) exceed incremental holding costs

## Slide 68: Incremental Fuel Oil Incentives Relative to Current Market Rules
Cost Effectiveness of Additional Fuel – Central Case, Extended Stressed Conditions
  Results are similar for the Extended Case as the Frequent Case

## Slide 69: Incremental Fuel Oil Incentives Relative to Current Market Rules
Cost Effectiveness of Additional Fuel – Central Case, Infrequent Stressed Conditions
  In the Infrequent Case, plants with dual fuel capabilities continue to receive positive returns for holding incremental energy inventory
    For oil-only plants, additional holding costs of the assumed level of incremental fuel inventory exceeds the total FER and ESI DA AS payments; under infrequent stressed conditions, these units infrequently supply energy and DA energy options
  Incremental energy inventory may not always be beneficial, particularly when market conditions provide sufficient supplies of energy inventory

## Slide 70: Total Winter Generation Mix
Energy and DA Options by Resource Type, CMR vs ESI, Frequent Stressed Conditions

## Slide 71: Total Winter Generation Mix
Energy and DA Options by Resource Type, CMR vs ESI, Extended Stressed Conditions

## Slide 72: Total Winter Generation Mix
Energy and DA Options by Resource Type, CMR vs ESI, Infrequent Stressed Conditions

## Slide 73: Net Revenues
Frequent Stressed Conditions Case
Average Net Revenues, Selected Resources, Winter Season, Frequent Stressed Conditions

## Slide 74: Net Revenues
Extended Stressed Conditions Case
Average Net Revenues, Selected Resources, Winter Season, Extended Stressed Conditions

## Slide 75: Net Revenues
Infrequent Stressed Conditions Case
Average Net Revenues, Selected Resources, Winter Season, Infrequent Stressed Conditions

## Slide 76: Contact
Todd Schatzki Principal 617-425-8250 Todd.Schatzki@analysisgroup.com