## Slide 1: 2020 Economic Study Request
MC/RC Joint Meeting
  July 1, 2020

## Slide 2: Motivation
Drivers
    States are increasingly procuring and assigning value to clean resource production
    NESCOE 2019 Offshore Wind study showed high levels of renewable spillage
    MIT’s “Deep Decarbonization of the Northeastern U.S. and the Role of Canadian Hydropower” 2020 study demonstrated bi-directional transmission with Quebec complements high intermittent resource mixes in New England
Purpose
    Identify a potential pathway, leveraging transmission and battery storage, to meet state clean energy goals
    Evaluate use of large scale, dispatchable reservoir hydro in fully integrating large penetrations of intermittent renewables cost-effectively
      Scale of storage needs at high intermittent penetration likely to be met by a diversity of resources
      Seasonal and resource diversity between New England and Quebec may be leveraged to the more effective achievement of state policy goals and benefit of customers

## Slide 3: Study Overview
High-level Assumptions
    2035 Study Year
      Demand extrapolated from 2020 CELT
      Heating load of ~9,500 GWh
      EV load of ~7,000 GWh
      2015 weather year for wind and PV profiles
Scenarios
    Incremental resources: beginning with “base case”, varies offshore wind, solar and thermal retirements
    Bi-directional: varies use of existing ties and additional ties to explore potentially up to 3,600MW of export capability to Quebec
    Battery Storage: varies the amount of in-region battery storage with the lowest at 2,000MW as used in the NESCOE study
Deliverables
    Economic: Production cost, marginal prices, load-serving entity energy expenses, congestion, spillage, emissions, exchange with Quebec
    Ancillary Services: load following/ramping, operating reserves, regulation

## Slide 4: Status and Next Steps
Previous PAC presentations by National Grid and ISO-NE
    April 23, 2020 – National Grid request
    May 21, 2020 – ISO-NE Assumptions Part I
    June 17, 2020 – ISO-NE Assumptions Part II
Study will continue to progress at the PAC
    July 22, 2020 – ISO-NE Assumptions Part III
    Q3 2020 – draft results expected and sensitivities identified
    Q4 2020 – sensitivity results and draft ancillary services results expected
    Q1 2021 – draft and final reports expected

## Slide 5: Supporting the Future Grid Initiative
Carbon compliant resource mix
    “Base Case” meets 2035 legislated targets for the New England states, interpolating midpoints for target dates beyond 2035
Pathway with a focus on storage
    Provides a pathway emphasizing role of exchange with Quebec
      Previous studies indicate Quebec may be utilized as a balancing resource, complementing intermittent renewables
      Important to include this pathway option when analyzing operational issues as part of the Future Grid Initiative
    Includes various levels of in-region battery storage for short-term storage
      In combination with the long-term storage option provided by bi-directional exchange with Quebec, spillage may reduce, more effectively using renewables at all hours