## Slide 1
JuLY 14-15, 2020 | MC TELECONFERENCE
Deborah Cooke
413.540.4488 | dcooke@iso-ne.com
Energy and Ancillary Service Revenue Adjustments for Level of Excess Supply and Energy Security Improvements
Cost of New Entry and
Offer Review Trigger Prices

## Slide 2
Cost of New Entry and Offer Review Trigger Prices
WMPP ID: 139
Proposed Effective Date: June 1, 2025 (CCP 16)
The recalculation of the Cost of New Entry (CONE), Net CONE, and Offer Review Trigger Prices (ORTPs) is being performed for the 2025-2026 Capacity Commitment Period (CCP)
Net CONE and ORTPs include energy and ancillary services (E&AS) revenue offsets
E&AS revenue offsets will include two adjustments
  Net CONE: Level of Excess adjustment to the energy prices, to reflect a system at the equilibrium (i.e., at ICR)
  Net CONE and ORTPs: Estimated revenues associated with the proposed Energy Security Improvements (ESI)

## Slide 3: E&AS revenue offsets will account for (future) market conditions in CCP16
The Level of Excess (LOE) reflects the system at criteria
  In accordance with the underlying design principles of the Forward Capacity Market and its MRI demand curve
  Further discussion following
E&AS revenues will be provided both with and without ESI revenue adjustments
  To account for the expected impact of these future market changes, which will be in effect for the CCP16
E&AS revenues will also be provided both with and without Forward Reserve Market revenues
  To account for the proposed elimination of the Forward Reserve Market
  Previously discussed at the June meeting

## Slide 4: Level of Excess ADJUSTMENT TO ENERGY PRICES
Adjustment Factor Logic and Results

## Slide 5: Net CONE calculations and the MRI-based FCM demand curves are based on a system at equilibrium
In New England, the FCA is intended to clear at the net Installed Capacity Requirement (ICR) in equilibrium
  ICR is determined based on the “1-day-in-10” Loss of Load Expectation resource adequacy objective
In principle: The FCA should induce new entry (at a price of Net CONE) if capacity is less than net ICR, and not if otherwise
To do so, the MRI-based demand curves are designed to pass through the point of Net CONE at the net Installed Capacity Requirement
  MRI Scaling Factor “shall be set at the value such that, at the quantity specified by the System-Wide Capacity Demand Curve at a price of Net CONE, the Loss of Load Expectation is 0.1 days per year”

## Slide 6: Recently, the system has been “long” on capacity
Capacity Commitment Period | Net ICR ARA3 (MW) | ARA3 Capacity Supply Obligation (MW) | Difference: CSO - Net ICR (MW)
2016-17 | 33,152 | 33,492 | 340
2017-18 | 33,138 | 33,693 | 555
2018-19 | 33,247 | 35,002 | 1,755
2019-20 | 33,390 | 35,396 | 2,006
Excess capacity supply (the “level of excess” or LOE) can lead to lower average prices in the energy and ancillary services markets
Using those “excess supply condition” energy prices for Net CONE would underestimate the E&AS revenue offsets at criteria

## Slide 7: A four-step method for Level of Excess Adjustment
Construct a “base case” energy market supply curve, specific for each hour of the operating day
  Intersect energy offer supply curves with day-ahead load forecast to determine locational marginal prices (LMPs)
  Uses last three calendar years of hourly energy market data (~26,304 hours in total)
Reconstruct “LOE-adjusted” energy market supply curves, removing energy supply offers in amounts equal to the level of excess MW (“LOE-adjusted case”)
  Based on resources pending retirement
  Intersect the LOE-adjusted energy supply curves with the (same) day-ahead load forecast to determine LOE-adjusted LMPs

## Slide 8: Methodology for Level of Excess Adjustment (cont.)
Calculate average LMPs for the base case and the LOE-adjusted case for three periods:
  On-peak hours: HE 08 through HE 23, non-holiday weekdays
  High on-peak hours: subset of on-peak hours, coincident with summer and winter intermittent reliability hours and all summer hours with a system-wide capacity scarcity condition
  Off-peak hours: all non-on-peak hours
Level of excess adjustment factor (“LOE AF”) is calculated specific to each hourly period in every month (36 LOE AF per year; 108 overall) as
Results on next slide

## Slide 9: Level of Excess Adjustment Factors - Results
Hourly prices will be adjusted by dividing historical prices by the prospective ‘at criteria’ adjustment factor
Examples on next slide
Hour Category | Jan 17 | Feb 17 | Mar 17 | Apr 17 | May 17 | Jun 17 | Jul 17 | Aug 17 | Sep 17 | Oct 17 | Nov 17 | Dec 17
High On-Peak | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00
On-Peak | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00
Off Peak | 0.98 | 0.99 | 0.99 | 0.99 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 0.99
Hour Category | Jan 18 | Feb 18 | Mar 18 | Apr 18 | May 18 | Jun 18 | Jul 18 | Aug 18 | Sep 18 | Oct 18 | Nov 18 | Dec 18
High On-Peak | 0.98 | 1.00 | 1.00 | 1.00 | 1.00 | 0.94 | 0.87 | 0.82 | 0.88 | 0.94 | 0.93 | 0.92
On-Peak | 0.98 | 1.00 | 1.00 | 1.00 | 1.00 | 0.95 | 0.90 | 0.88 | 0.95 | 0.96 | 0.95 | 0.95
Off Peak | 0.98 | 1.00 | 1.00 | 1.00 | 1.00 | 0.98 | 0.97 | 0.97 | 0.99 | 0.99 | 0.96 | 0.97
Hour Category | Jan 19 | Feb 19 | Mar 19 | Apr 19 | May 19 | Jun 19 | Jul 19 | Aug 19 | Sep 19 | Oct 19 | Nov 19 | Dec 19
High On-Peak | 0.94 | 0.93 | 0.94 | 0.96 | 1.00 | 0.97 | 0.93 | 0.96 | 0.99 | 0.99 | 0.97 | 0.96
On-Peak | 0.94 | 0.96 | 0.96 | 0.97 | 1.00 | 0.98 | 0.96 | 0.98 | 0.99 | 0.99 | 0.98 | 0.96
Off Peak | 0.95 | 0.97 | 0.97 | 0.99 | 1.00 | 0.99 | 0.96 | 1.00 | 1.00 | 1.00 | 0.98 | 0.98

## Slide 10: Applying the Level of Excess Adjustment
Historical energy prices from the previous three calendar years are the basis for determining prices in the E&AS dispatch models
  As described by Concentric Energy Advisors in June
The appropriate LOE AF – based on year and category – will be applied to each hourly historical energy price
  Day-Ahead LMP, Real-Time LMP, and real-time reserve prices (as adjusted for scarcity)
For example:
  An observed high-on peak LMP of $50 in the month of July 2018 would be adjusted to ($50 ÷ 0.90) = $55.56/MWh
  An observed on-peak real-time ten-minute spinning reserve price of $8 in the month of January 2017 would be adjusted to ($8 ÷ 0.99) = $8.08
  An observed off-peak LMP of $35 /MWh in the month of October 2019 would be adjusted to ($35 ÷ 1.00) = $35/MWh

## Slide 11: Energy Security Improvements
Estimated Revenue Impacts for Net CONE and ORTPs

## Slide 12: Approach to estimating ESI revenue offsets
Estimated incremental revenues from the proposed Energy Security Improvements designs will be included in the revenue offsets for Net CONE and ORTPs
  Both the ISO-proposed and NEPOOL-proposed designs are estimated
Calculated technology-specific revenue changes using similar methodology as the ESI Impact Analysis models
  Net CONE: Winter and non-winter Central Cases recalculated for Combined Cycle and Combustion Turbine new entrants
    Modeled on select, recent new entrants
  ORTPs: Results of winter and non-winter ESI Central Case for all technologies except storage
    Analysis Group estimated revenues separately for storage based on highest priced hours of each calendar day

## Slide 13: Approach to estimating ESI revenue offsets (cont.)
Winter and non-winter case scenarios weighted based on estimated frequency
  Based on weather data from the past 20 winter and non-winter periods (Details included in the Appendix)
Methodology used is generally the same as that summarized in the Internal Market Monitor “FCA15 Energy Security Estimate for FCM Offers” document
Tables with weighted final values for each technology included in the Appendix

## Slide 14: ESI revenue offsets example Incremental revenues for Combustion Turbine
Season | Incremental Payments to Generation | Incremental Payments to Capacity
Winter (3 months) | $/MWh | $/MW, 3-months
Frequent (15%) | $7.79 | $7,694
Extended (10%) | ($29.56) | $3,567
Infrequent (75%) | $0.00 | $1,625
Weighted Final Value | ($1.79) | $2,730
Non-Winter (9 months) | $/MWh | $/MW, 9-months
Severe (15%) | $9.21 | $5,116
Moderate (85%) | ($11.35) | $4,218
Weighted Final Value | ($8.27) | $4,353
Incremental Payments to Generation = revenue from LMP and FER
Incremental Payments to Capacity = net option revenue minus holding costs
Values based on ESI proposal filed by ISO
Next – using these values to estimate ESI revenue offsets

## Slide 15: ESI revenue offsets example Incremental revenues for Combustion Turbine (cont.)
In this example, the final adjustment for ESI revenues for this technology is $0.507/kW-month
  Sum of incremental payments to generation and incremental payments to capacity
Season | Winter (3-months) | Summer (9-months) | Combined $, 12-month | Combined $/kW-mo.
Incr. Payments to Generation |  |  |  | 
Weighted Final Value ($/MWh) | ($1.79) | ($8.27) |  | 
Seasonal generation (MWh) | 17,992 | 40,946 |  | 
Weighted Incremental Payments | ($32,166) | ($338,586) | ($370,753) | ($0.083)
Incr. Payments to Capacity |  |  |  | 
Weighted Final Value ($/MW) | $2,730 | $4,353 |  | 
Seasonal Capacity (MW) | 372.20 | 372.20 |  | 
Weighted Incremental Payments | $1,015,997 | $1,620,222 | $2,636,219 | $0.590
Change in Total Payments |  |  | $2,265,467 | $0.507
ISO will post the ESI revenue offsets for all technology types when available

## Slide 16: Conclusion & Next Steps
A Level of Excess adjustment will be applied in the E&AS revenue calculations for Net CONE technologies, to reflect the system at equilibrium
  In accordance with the underlying design principles of the Forward Capacity Market
E&AS revenue offsets will be calculated reflecting both current and proposed (future) market conditions in CCP16, including:
  Revenue impacts from ESI, both as proposed by ISO and as proposed by NEPOOL
  Elimination of the Forward Reserve Market (as discussed in June)
Incremental revenue offsets associated with ESI for the various modeled technologies will be provided when available

## Slide 17: Stakeholder Schedule
Stakeholder Committee and Date | Scheduled Project Milestone
Markets Committee June 10, 2020 | Review initial projections of potential revenue offsets associated with FRM sunset
Markets Committee July 14-16, 2020 | Review initial projections of potential revenue offsets associated with ESI and initial discussion of proposed level of excess adjustment methodology
Markets Committee August 11-12, 2020 | Continued discussion of revenue offsets
Markets Committee September 9-10, 2020 | Continued discussion of revenue offsets
Markets Committee October 6-7, 2020 | Final review and MC vote on FCM parameter updates
Participants Committee November 5, 2020 | PC vote

## Slide 19: Acronyms Used in this Presentation
CCP = Capacity Commitment Period
CONE = Cost of New Entry
E&AS = Energy & Ancillary Services
ESI = Energy Security Improvements
FCA = Forward Capacity Auction
FCM = Forward Capacity Market
ICR = Installed Capacity Requirement
LMP = Locational Marginal Price
LOE = Level of Excess
LOE AF = Level of Excess Adjustment Factor
MRI = Marginal Reliability Impact
ORTP = Offer Review Trigger Price

## Slide 20: Appendix
Analysis to derive Winter and Non-Winter category ratings for Energy Security Improvements revenue offsets
Additional ESI revenue offset examples

## Slide 21: Approach to developing season weightings
An analysis of the temperature profiles of the seasons used in the AG analysis was performed
Based on the temperature profiles, criteria were developed to identify like-seasons (slide 22)
Temperature profiles of the past 20 seasons (winter/non-winter) were evaluated and compared to the category criteria
  For the non-winter periods, the months of June through September were included; temperatures in the shoulder months had no impact on results
The number of the last 20 seasons meeting the criteria were compiled and used to determine the season weights applied for ESI revenue offsets (slides 24 - 25)

## Slide 22: Criteria for season categories
Season | Category | Criteria
Winter | Extended Stressed | A winter period with five or more consecutive days with an average daily temperature of 10°F or less
 | Frequently Stressed | A winter period not classified as Extended, with 15 or more days with a minimum daily temperature of 10°F or less
 | Infrequently Stressed | All winter periods not classified as Extended or Frequent
Non-Winter | Severe | Contains both: two or more three-day events with temperatures at or above 85°F and two or more three-day events with dew points at or above 70; or Contains three or more four-day events with temperatures at or above 85°F and/or dew points at or above 70
 | Moderate | All non-winter periods not classified as Severe

## Slide 23: Summary of season results
Season | Category | Total Seasons Evaluated | Category Seasons | Percent
Winter | Extended Stressed | 20 | 2 | 10%
 | Frequently Stressed | 20 | 3 | 15%
 | Infrequently Stressed | 20 | 15 | 75%
Non-Winter | Severe | 20 | 3 | 15%
 | Moderate | 20 | 17 | 85%

## Slide 24: Winter season analysis results
Season/Year Evaluated | Extended Stressed: 5-Day Event Count Avg Temp <= 10°F | Frequently Stressed: Number of Days, Minimum Temp <= 10°F
WINTER 00-01 | 0 | 4
WINTER 01-02 | 0 | 0
WINTER 02-03 | 4 | 19
WINTER 03-04 | 5 | 14
WINTER 04-05 | 4 | 13
WINTER 05-06 | 0 | 7
WINTER 06-07 | 0 | 8
WINTER 07-08 | 0 | 5
WINTER 08-09 | 1 | 11
WINTER 09-10 | 0 | 6
WINTER 10-11 | 0 | 8
WINTER 11-12 | 0 | 4
WINTER 12-13 | 1 | 6
WINTER 13-14 | 1 | 16
WINTER 14-15 * | 1 | 23
WINTER 15-16 | 1 | 5
WINTER 16-17 | 0 | 5
WINTER 17-18 * | 6 | 14
WINTER 18-19 | 0 | 7
WINTER 19-20 | 0 | 1
* Seasons modeled in the Impact Analysis
Legend:
BLUE – Frequently stressed winter periods
RED – Extended stressed winter periods

## Slide 25: Non-Winter season analysis results
Season/Year Evaluated | 3-Day Event Count Temp >=85°F | 3-day Event Count Dew Point >=70 | 4-Day Event Count Temp >=85°F | 4-Day Event Count Dew Point >=70
SUMMER 00 |  |  |  | 
SUMMER 01 | 2 |  | 1 | 
SUMMER 02 | 3 |  | 1 | 
SUMMER 03 | 1 | 1 |  | 1
SUMMER 04 |  | 1 |  | 
SUMMER 05 | 1 | 1 |  | 1
SUMMER 06 | 1 |  |  | 
SUMMER 07 |  |  |  | 
SUMMER 08 | 1 |  |  | 
SUMMER 09 | 1 | 1 | 1 | 
SUMMER 10 | 2 | 1 | 2 | 1
SUMMER 11 | 1 |  | 1 | 
SUMMER 12 | 2 | 1 | 1 | 
SUMMER 13 | 2 | 2 | 2 | 1
SUMMER 14 | 1 | 1 |  | 
SUMMER 15 | 2 |  | 2 | 
SUMMER 16 | 1 | 1 | 1 | 1
SUMMER 17 |  |  |  | 
SUMMER 18 * | 3 | 5 | 1 | 2
SUMMER 19 | 2 | 1 |  | 1
* Season modeled in the Impact Analysis
Legend:
RED - Severe non-winter period

## Slide 26: ESI revenue offsets - Example 2 Incremental revenues for Combustion Turbine NEPOOL proposal
In this example, the final adjustment for ESI revenues for this technology is $0.292/kW-month
  Sum of incremental payments to generation and incremental payments to capacity
Season | Winter (3-months) | Summer (9-months) | Combined $, 12-month | Combined $/kW-mo.
Incr. Payments to Generation |  |  |  | 
Weighted Final Value ($/MWh) | ($1.91) | $4.67 |  | 
Seasonal generation (MWh) | 17,992 | 40,946 |  | 
Weighted Incremental Payments | ($34,337) | $191,314 | $156,977 | $0.035
Incr. Payments to Capacity |  |  |  | 
Weighted Final Value ($/MW) | $2,366 | $718 |  | 
Seasonal Capacity (MW) | 372.20 | 372.20 |  | 
Weighted Incremental Payments | $880,481 | $267,244 | $1,147,725 | $0.257
Change in Total Payments |  |  | $1,304,702 | $0.292

## Slide 27: ESI revenue offsets – Example 3 Incremental revenues for Combined Cycle
In this example, the final adjustment for ESI revenues for this technology is $0.180/kW-month
  Sum of incremental payments to generation and incremental payments to capacity
Season | Winter (3-months) | Summer (9-months) | Combined $, 12-month | Combined $/kW-mo.
Incr. Payments to Generation |  |  |  | 
Weighted Final Value ($/MWh) | $0.58 | $0.52 |  | 
Seasonal generation (MWh) | 614,456 | 1,629,510 |  | 
Weighted Incremental Payments | $359,454 | $849,627 | $1,209,081 | $0.179
Incr. Payments to Capacity |  |  |  | 
Weighted Final Value ($/MW) | $0 | $8 |  | 
Seasonal Capacity (MW) | 563.3 | 563.3 |  | 
Weighted Incremental Payments | $0 | $4,466 | $4,466 | $0.001
Change in Total Payments |  |  | $1,213,547 | $0.180

## Slide 28: ESI revenue offsets - Example 4 Incremental revenues for Combined Cycle NEPOOL proposal
In this example, the final adjustment for ESI revenues for this technology is $0.124/kW-month
  Sum of incremental payments to generation and incremental payments to capacity
Season | Winter (3-months) | Summer (9-months) | Combined $, 12-month | Combined $/kW-mo.
Incr. Payments to Generation |  |  |  | 
Weighted Final Value ($/MWh) | $0.48 | $0.33 |  | 
Seasonal generation (MWh) | 614,456 | 1,629,510 |  | 
Weighted Incremental Payments | $294,819 | $544,299 | $839,118 | $0.124
Incr. Payments to Capacity |  |  |  | 
Weighted Final Value ($/MW) | $0 | $2 |  | 
Seasonal Capacity (MW) | 563.3 | 563.3 |  | 
Weighted Incremental Payments | $0 | $1,007 | $1,007 | $0.000
Change in Total Payments |  |  | $840,125 | $0.124