## Slide 1: Future Grid: Review of Past/Ongoing and Proposed Studies September 1, 2020 NEPOOL Markets and Reliability Committee Meeting

## Slide 2: Introduction
MC/RC requested review of certain past/ongoing studies for potential to inform future grid study to be developed (“Future Grid Study”). Request was to identify objectives/questions asked in each study and potential for analysis and model to be used in Future Grid Study. To advance discussions, we also looked at the Future Grid Study request proposals.
Observations on studies and proposals are from NEPOOL counsel; final word on them is for those who conducted, commissioned, or proposed the studies.
Six past/ongoing studies were identified for examination: (1) 2016 NEPOOL Economic Study; (2) 2019 NESCOE Economic Study; (3) Massachusetts 2050 Roadmap Effort; (4) Eversource “Grid of the Future” Study; (5) E3/EFI “Electric Reliability under Deep Decarbonization” Study; and (6) 2019 Brattle Group “Achieving 80% GHG Reduction in New England by 2050” Study.

## Slide 3: Overview of Analysis
The slides below look at:
  Scope of Future Grid Study effort, based on the “Bubble” Chart* that was presented at the March 5, 2020 NPC meeting
  The objectives, overall purpose, subordinate questions asked, scenarios and modeling used for each past/ongoing study; specific observations
  General observations regarding the past and ongoing studies
  Observations regarding the proposals for the Future Grid Study
  Final comments
* The “Bubble” Chart is Agenda Item 5 from the March NPC Meeting. To access, please click here.

## Slide 4: Scope of Study Effort (from “Bubble” Chart)
Objective: Assess and discuss future state of the regional power system in light of current state energy and environmental policies.
Study Process to Define and Assess Future State of Regional Power System: 1. Identify Resource Mix in [Year]; 2. Identify Resource & Operational/Reliability Needs
*Assumptions, future scenarios, etc. to be developed within stakeholder process.
Gap Analysis: As part of study process, conduct a gap analysis to determine whether, in the future state envisioned, the markets (current design plus ESI) provide resources/ISO-NE what they need to continue to reliably operate the system? If not, what market deficits need to be addressed to assure reliability?
Discuss Potential Market Approach(es) to Address Gap(s): Based on study results/gap analysis, explore potential market approaches to address any future gaps identified in the prior step, including evaluation of the pros/cons of different approaches and discussion of how any such market approach contemplates state energy and environmental laws.
{Note: Identification and discussion of potential future pathways/market frameworks is currently on a separate track at the NPC.}

## Slide 5: 2016 NEPOOL Economic Study, Phase I
Objective and Overall Purpose | Study potential economic effects (in 2025 and 2030) on ISO-NE’s wholesale energy markets when implementing public policies in the New England states; evaluate physical quantities of ramping, reserves, and regulation that could be needed to meet environmental policy goals Examine resource-expansion scenarios of the regional power system and the potential effects of these different future changes on resource adequacy, operating and capital costs, and options for meeting environmental policy goals
Subordinate Questions | Projected wholesale energy market revenues and the contribution of these revenues to the fixed costs for generic new generation Total wholesale electricity cost of supplying load and operating the system and total regional emissions under alternative scenarios

## Slide 6: 2016 NEPOOL Economic Study, Phase I
Scenarios | Scenario 1: RPSs + Gas Scenario 2: ISO Queue Scenario 3: Renewables Plus Scenario 4: No Retirements beyond FCA #10 Scenario 5: ACPs + Gas Scenario 6: RPSs + Geodiverse Renewables All six scenarios were used in both Phase I and Phase II Note: Of the six scenarios, Scenarios 3 and 6 are the most relevant and the other four scenarios did not seem especially relevant to the Future Grid Study.
Modeling | ABB’s GridView program, a common simulation tool vetted before stakeholders, calculates least-cost transmission-security-constrained unit commitment and economic dispatch under differing sets of assumptions and minimizes production costs for a given set of unit characteristics
Note | In 2017, the Conservation Law Foundation requested an Economic Study of NEPOOL Scenario 3 to make it an emissions-compliant scenario. Also requested three other scenarios: “EE + Offshore”, “Onshore Less EE/PV”, and “Wind Less Nuclear”. The final report on this study, published on October 29, 2018, can be found by searching “2017 Economic Study” in the ISO-NE website.

## Slide 7: 2016 NEPOOL Economic Study, Phase II
Overall Purpose | Evaluate physical quantities of ramping, reserves, and regulation that could be needed to meet environmental policy goals
Modeling | ElectricPower Enterprise Control System (EPECS) simulator was developed to address the multi-time scale nature of renewable energy integration. It consists of four simulation layers: Day-Ahead Resource Scheduling as a Security Constrained Unit Commitment (SCUC) Layer Real-Time Resource Scheduling as a Real-Time Unit Commitment (RTUC) Layer Real-Time Balancing as a Security Constrained Economic Dispatch (SCED) Layer Real-Time Physical Power Flow w/ Integrated Regulation Service Layer EPECS assessed: Simulated Operating Reserves: Load Following, Ramping, and Curtailment Performance Simulated Interface & Tie-line Performance Simulation Regulation Performance Simulated Balancing Performance
Note | Phase II also examined FCA clearing prices and natural gas system deliverability issues but these items were not the focus of Phase II

## Slide 8: Observations on NEPOOL Study
Study completed
Looked at both economic and operational consequences of future grid scenarios
Looked at two year snapshots in relatively near horizon: 2025 and 2030; would need to be extended
Not intended to backcast from future grid to how we get there
Economic modeling done by ISO-NE using Gridview tool available to the ISO; operational modeling (regulation, ramping and reserves) done by outside consultant using Electric Power Enterprise Control System (EPECS) simulation tool; FCM and gas constraint modeling done by outside consultants
Of the six scenarios, Scenarios 3 and 6 seem more consistent with and in the scope of the intended Future Grid Study; would need to be updated/supplemented in significant ways (e.g., did not look at electrification of building and transportation sectors; did not consider all current emissions compliance requirements). Could supplement with 2017 CLF Economic Study.

## Slide 9: 2019 NESCOE Economic Study
Objective and Overall Purpose | Study the interconnection of as much as 8,000 MW (nameplate) of new offshore wind resources off the coast of southern New England by 2030
Subordinate Questions | Provide information on several transmission configurations available to integrate various levels of additional offshore wind resources, at different points of interconnection into southeastern New England, and to estimate transmission upgrade costs associated with these conceptual configurations Considered wholesale market impacts and power sector air emissions for each scenario studied
Scenarios (Offshore Wind Additions (Nameplate) with 1,000 MW of RFP-committed) | 
Modeling | The economic analysis was conducted using ABB’s GridView economic-dispatch program. The system was modeled at the zonal level, and New England was modeled as a constrained single area for unit commitment. The 2030 transfer capabilities for internal and external transmission interfaces were based on the values established for 2025 for FCM and regional planning studies. The interconnection analysis was conducted using Siemens’ PSS/E power flow simulator. The interconnection analysis was performed at the feasibility level with a handful of solution concepts explored in the highest penetration cases. The ancillary services analysis was conduced using Dartmouth’s EPECS economic-dispatch program. The ancillary services analysis re-examined system operating requirements associated with the 2016 Economic Study.

## Slide 10: Observations on NESCOE Study
Study completed, but no transmission cost estimates were provided; the ancillary services analysis used the NEPOOL study scenarios
Focused on interconnection of offshore wind additions only
Geographically limited to southern New England offshore wind
Included both an economic analysis and a conceptual level transmission analysis, both done by ISO using available tools
  Provides analysis of system emissions estimates associated with increasing levels of off-shore wind
Also included some operational effects analysis (regulation, ramping and reserves capability) using same outside consultant and modeling tool and scenarios as for the NEPOOL operational study
  Directionally indicative due to scenario assumptions
Time frame limited to 2030
Not fully consistent with scope of Future Grid Study because of limited focus, but possibly could be used as a component of a larger Future Grid Study to examine the offshore wind piece

## Slide 11: Massachusetts 2050 Roadmap Effort
Overall Purpose | Identify the strategies, policies, and implementation pathways for MA to achieve “net zero” GHG emissions by 2050 (at least 85% of 1990 level GHG reductions + sequestration), and the priorities to achieve an interim goal by 2030
Subordinate Questions | Describe optionality and requirements across all energy supply and demand necessary to achieve deep, permanent GHG emissions. Identify key “no regrets” and “must do” near term policies and actions required in the 2020s to enable continued achievement of emissions reduction requirements 2030–2050.
Scenarios | Eight cross-sector, all-economy scenarios (2020 – 2050) each capable of achieving at least an 85% reduction below 1990 levels. To test robustness of resource availability across sectors, scenarios assume the entire Northeast (NY, New England, Maritimes) is moving together towards IPPC-compliant emissions targets. Scenarios test widespread deployment of DERs, availability of decarbonized pipeline gas product, various levels regional coordination and OSW deployment, availability of thermal electricity generation, fully-renewable primary energy supply.
Modeling (Evolved Energy Research) | EnergyPATHWAYS: Scenario analysis tool that is used to develop economy-wide energy demand scenarios (additional information here). RIO: Optimization tool to develop portfolios of low-carbon technology deployment for electricity generation and balancing, alternative fuel production, and direct air capture (additional information here).

## Slide 12: Observations on MA Study
Draft study report release expected mid- to late-Sept. (published in final in Dec.)
Includes granular data for all commercialized energy supply technologies, and 363 demand-side technologies in 5-year time-steps based on 8,760 integrated dispatch modeling for entire Northeast.
Approach is to start with the goal (net zero by 2050) and develop a range of cost-effective technical supply and demand portfolios capable of achieving it
Method – Bottom up backcasting to explore wide range of compliant scenarios:
  1. Underlying drivers of energy demand advanced to 2050 levels;
  2. Design system to reliably meet 2050 energy demand at required emissions level across the economy—all sectors, all fuels;
  3. Work back to 2020 with attention to stock rollover timing to minimize stranded asset costs;
  4. Pathway scenarios are designed to test the system and gain insight into low-carbon system dynamics and cross-sector inter-dependencies across more than a half-dozen Global Warming Solutions Act-compliant futures; and
  5. Produce very granular data (hourly dispatch; 5-year capacity time-step) data to enable decision-making re: implementation
Modeling tools: EnergyPATHWAYS is open-source but RIO is not
Some of the data/analysis/assumptions could be useful to the Future Grid Study, including to help establish assumptions and identify gaps; seems to focus on how to achieve an end state goal; not completed; uses a proprietary modeling tool ISO would need to obtain or hire third party

## Slide 13: Eversource’s “Grid of the Future” Study
Overall Purpose | Analyze the impact of decarbonization policy on the electric grid out to 2050; quantify electric system changes needed to meet regional carbon emission reduction targets
Subordinate Questions | How will carbon policies impact electric system dynamics in New England Understand potential range of changes to all sectors of the economy Specifically understand impact on the grid and system operations
Scenarios | 2030/2040/2050 Balanced Portfolio, Solar Focus and Offshore Wind Focus. All three scenarios assume achievement of 80% economy-wide GHG reduction below 1990 levels by 2050 2030/2040 Aggressive Decarbonization scenario which assumes 95% economy-wide GHG reduction below 1990 levels by 2050
Modeling | Comprehensive industry research and hourly economic simulations for the next three decades; hourly simulations run by London Economics using POOLMOD, a proprietary modeling tool
Preliminary Results | Significant changes to supply and demand between 2030 and 2040 including changing of the timing of peak load, resource adequacy needs for dispatchable resources, etc. Net demand (TWh) continues to increase, significant increase in EE and BTM PV resulting in a need for focus on Grid operations and planning to ensure reliability and cost effectiveness A balanced portfolio of supply, demand and grid technologies results in cost-effectively meeting reliability while staying on the path of achieving the region’s clean energy goals

## Slide 14: Observations on Eversource Study
Study is ongoing
Looks at how decarbonization efforts across the economy will impact energy system dynamics in New England
Focus is on supply mix, demand changes, hourly supply and demand dynamics, total cost of supply, clearing prices, and total cost to load.
Looks out to 2050 but scenarios focus on 2030 and 2040
Deliverables include multiple scenarios with detailed information on supply, demand, storage, and transmission that successfully achieve regional decarbonization targets
Uses POOLMOD as a modeling tool, a proprietary model that simulates security constrained dispatch in ISO-NE
Seems consistent with scope of intended Future Grid Study; scenarios might need to be extended to 2050; modeling tool might not be available to ISO- ISO would need to obtain or hire third party

## Slide 15: E3/EFI “Electric Reliability under Deep Decarbonization”
Overall Purpose | Analyze whether New England can provide affordable, reliable power under future scenarios that achieve net zero economy-wide GHG emissions by 2050
Subordinate (Corollary) Questions | What decarbonization technologies and strategies are most likely to be successful in New England, given weather, policy, economics, etc.? How much must electricity sector emissions be reduced by 2050? How much new electric load will materialize due to electrification of end-uses in other sectors by 2050? What is the optimal electricity resource mix to meet’s NE energy and resource adequacy needs through 2050 while achieving economy-wide GHG goals? What roles do various supply resources play in achieving resource adequacy? How much firm capacity is needed in the medium to long-term, and how substitutable renewable generation is for firm dispatchable capacity
Scenarios and Modeling | High Electrification/High Fuels Step 1 PATHWAYS Model: Used to identify economy-wide GHG scenarios designed to meet 2050 economy-wide decarbonization goals Step 2 RESOLVE Model: Electricity capacity expansion model develops least-cost resource portfolios to meet GHG targets Step 3 RECAP Model: Tests the resource adequacy of the portfolios

## Slide 16: Observations on E3/EFI Study
This study is not yet finalized
Study looks out to 2050
Includes a first step that seems to focus on how to achieve 2050 goals
Uses a RESOLVE model to develop least-cost resource portfolios to meet GHG targets
Uses a New England RECAP model to tests the resource adequacy of the supply resource portfolios
Includes some conceptual transmission constraints/cost analysis
Some of the data/analysis/assumptions could be useful to the Future Grid Study, including to help establish assumptions and identify gaps; seems to focus partly on how to achieve an end state goal; not completed; uses a proprietary modeling tool ISO would need to obtain or hire third party

## Slide 17: 2019 Brattle Group “Achieving 80% GHG Reduction in New England by 2050” Study
Overall Purpose | Estimate whether and how much clean energy resource additions in New England need to accelerate to achieve the 2050 decarbonization goals
Subordinate Questions | What is the necessary infrastructure (e.g., storage, transmission) to maintain a reliable power? How much does New England need to electrify the largest remaining sources of GHG emissions (transportation, residential heating, and commercial heating)? What emerging technologies will require the necessary electrification? What energy resource portfolios could supply the 2050 New England electric system?
Scenarios | Efficiency Focused Electrification Focused Electrification and Renewable Fuels
Modeling | Decarbonized Energy Economy (DEEP) Model is an economy-wide energy and emissions model designed to investigate the implications of decarbonization policies. DEEP includes a bottom-up analysis of electrification and other approaches, such as energy efficiency, to achieve decarbonization mandates and simulates how these changes impact hourly electric load. DEEP then identifies investments in clean resources (e.g., renewables) and dispatchable resources (e.g., combustion turbines or battery storage) to reliably balance and operate the system. It is designed for rapid investigation of many scenarios and sensitivities.

## Slide 18: Observations on Brattle Study
Study is completed
Looks out to 2050
Asks what supply resource changes need to occur to achieve a specific goal: 80% GHG reduction by 2050 relative to a 1990 baseline
Includes some analysis of reliability resource needs but not an in depth analysis of reliability gaps or transmission
Uses a model proprietary to the Brattle Group; ISO-NE would need to obtain or hire third party
  DEEP (“An economy-wide energy and emissions model designed to investigate the implications of decarbonization policies. DEEP includes a bottom-up analysis of electrification and other approaches, such as energy efficiency, to achieve decarbonization mandates and simulates how these changes impact hourly electric load.”)
Although this study seems to focus on how to achieve an end state, some of its data/analysis could be useful

## Slide 19: General Observations on Past Studies
The past/ongoing studies that seem most consistent with the scope of the intended Future Grid Study are the:
  NEPOOL Economic Study (would need updating and supplementing, perhaps with 2017 CLF Economic Study)
  Eversource’s “Grid of the Future” Study
  E3/EFI “Electric Reliability under Deep Decarbonization” Study
Some of the data/analysis/assumptions from the Massachusetts 2050 Roadmap Effort study and the Brattle Group study could be useful to the Future Grid Study, including to help establish assumptions and identify gaps; seem to focus on how to achieve an end state goal; MA study not completed; each uses modeling tools that ISO does not have
The NESCOE study is more limited in scope and would provide only a part of the analysis/information being sought in the Future Grid Study.

## Slide 20: Observations on Proposed Studies
The following slides provide initial, high-level observations on the nine proposed studies* that were considered at the August 4, 2020 MC/RC meeting.
The observations are from NEPOOL counsel only and are intended to facilitate further discussion of the proposals and how they might fit into the intended Future Grid Study.
* To view the proposed study requests, please click here.

## Slide 21: Observations on Proposed Studies
The National Grid proposal seems generally consistent with the scope but has a transmission/storage focus (using bi-directional, controllable transmission for purposes of leveraging energy storage between New England and Quebec). Mentions 2035 values; not sure it extends to 2050. Unclear whether it would identify reliability gaps. Would use modeling tools that include Gridview, steady-state power flow and a tool for forecasting FCA clearing prices. Proposal to consider impact of bi-directional, controllable transmission to external regions could probably be included as a scenario in various other studies.
The Eversource proposal seems like a complete economic and reliability study and consistent with the intended scope of the Future Grid Study. The modeling tools associated with it (Gridview and GE MARS) are used by the ISO.

## Slide 22: Observations on Proposed Studies
Some of the proposals seem to have a more limited focus that could be worked into a larger study, or potentially could be used as change cases/scenarios/sensitivities, but are not necessarily proposals for a full Future Grid Study on their own, including:
  EMA: Focuses on two interconnection cases (capacity interconnection and minimum interconnection) and how these impact markets/operations
  FirstLight: Focuses on certain considerations for storage in the assumptions and modeling
  Multi-Sector Group A: Focuses on the impact on needs for ramping, regulation and load-following resources of a 2050 decarbonized future grid; does not include an economic analysis. Would build upon NEPOOL Phase 2.
  Multi-Sector Group B: Focuses on a transmission system assessment of a 2050 decarbonized future grid
  NextEra/Dominion: Focuses on loss of Seabrook and Millstone nuclear

## Slide 23: Observations on Proposed Studies
NESCOE submitted a “pathway” scenario that would look at the years 2035 and 2040 under certain electrification assumptions. Seems like it could work into a larger study as a scenario to be considered.
The Anbaric proposal seems outside the scope of the intended Future Grid Study because it identifies a goal and then studies how to achieve it. Possibly could be used for assumptions that go into the study, identification of reliability gaps, or sensitivities to the study, rather than the focus of the study.

## Slide 24: Final Comments
Project administrator, working with NEPOOL, NESCOE and the ISO, can facilitate further stakeholder consideration of:
  What can and should be used from past/ongoing studies
  What needs to be updated/supplemented from those studies
  Consolidation of proposed studies into an integrated proposal consistent with the intended scope of the Future Grid Study
  What modeling tools/services should be used and their availability
  Perhaps next step should be to develop a straw proposal for a study using the input from study proponents and from past/ongoing studies, consistent with the intended scope of the Future Grid Study