## Slide 1
September 8 - 10, 2020 | MC TELECONFERENCE
REVISION 1
Deborah Cooke
413.540.4488 | dcooke@iso-ne.com
Estimated revenue offsets associated with Energy Security Improvements
Stakeholder questions
Tariff language revisions
Cost of New Entry and
Offer Review Trigger Prices

## Slide 2
Cost of New Entry and Offer Review Trigger Prices
WMPP ID: 139
Proposed Effective Date: June 1, 2025 (CCP 16)
The recalculation of the Cost of New Entry (CONE), Net CONE, and Offer Review Trigger Prices (ORTPs) is being performed for the 2025-2026 Capacity Commitment Period (CCP)
Net CONE and ORTPs include energy and ancillary services (E&AS) revenue offsets
This presentation will:
  Provide the estimated revenue offsets associated with Energy Security Improvements
  Respond to several stakeholder questions from the July MC meeting
  Provide a summary of Tariff revisions

## Slide 3: E&AS revenue offsets will account for (future) market conditions in CCP16
The Level of Excess (LOE) reflects the system at criterion
  In accordance with the underlying design principles of the Forward Capacity Market and its MRI demand curve
E&AS revenues are provided both with and without ESI revenue adjustments
  ESI revenue adjustments reflect the most recent Concentric Energy Advisors (CEA) dispatch models
E&AS revenues are provided both with and without Forward Reserve Market revenues
  To account for the proposed sunset of the Forward Reserve Market beginning in CCP 16
From August presentation

## Slide 4: Energy Security Improvements
Incremental revenue offsets for the Net CONE and ORTP modeled technologies
ISO proposal
NEPOOL proposal

## Slide 5: ESI revenues are estimated and incorporated in the Net CONE and ORTP calculations
As discussed in the July 2020 Markets Committee meeting, ESI revenue offsets will be estimated under both the ISO and NEPOOL filed proposals
  Both scenarios assume the sunset of the Forward Reserve Market
Revenues will be estimated using results of the Energy Security Improvements Impact Analysis
The following slides provide revenue offsets for each modeled Net CONE and ORTP technology

## Slide 6: Summary of estimated ESI revenue offsets Net CONE Technologies – ISO Proposal
Technology Type | Incr. Payments to Generation ($/kW-mo.) | Incr. Payments to Capacity ($/kW-mo.) | Total 2020$ ($/kW-mo.) | Total 2025$ ($/kW-mo.)
Combustion Turbine | $-0.140 $0.184 | $0.589 | $0.450 $0.405 | $0.497 $0.447
Combined Cycle | $0.237 $0.273 | $0.001 | $0.238 $0.273 | $0.263 $0.301
Aeroderivative | $-0.092 $0.129 | $0.587 | $0.495 $0.458 | $0.547 $0.506
Incremental Payments to Generation = revenue from LMPs and Forecast Energy Requirement
Incremental Payments to Capacity = net option revenue minus holding costs
Detailed calculations are in Appendix A
Note: values may reflect rounding
Revised

## Slide 7: Summary of estimated ESI revenue offsets Net CONE Technologies – NEPOOL Proposal
Technology Type | Incr. Payments to Generation ($/kW-mo.) | Incr. Payments to Capacity ($/kW-mo.) | Total 2020$ ($/kW-mo.) | Total 2025$ ($/kW-mo.)
Combustion Turbine | $0.064 $0.076 | $0.265 | $0.328 $0.341 | $0.362 $0.376
Combined Cycle | $0.162 $0.187 | $0.000 | $0.162 $0.187 | $0.179 $0.206
Aeroderivative | $0.042 $0.051 | $0.277 | $0.320 $0.328 | $0.353 $0.362
Incremental Payments to Generation = revenue from LMPs and Forecast Energy Requirement
Incremental Payments to Capacity = net option revenue minus holding costs
Detailed calculations are in Appendix B
Note: values may reflect rounding
Revised

## Slide 8: Summary of estimated ESI revenue offsets ORTP Technologies - ISO proposal
Technology Type | Incr. Payments to Generation ($/kW-mo.) | Incr. Payments to Capacity ($/kW-mo.) | Total 2020$ ($/kW-mo.) | Total 2025$ ($/kW-mo.)
Combustion Turbine | $0.011 $0.016 | $0.310 | $0.321 $0.326 | $0.354 $0.360
Combined Cycle | $0.272 $0.315 | $0.015 | $0.287 $0.330 | $0.317 $0.364
On-Shore Wind | $0.066 | $0.000 | $0.066 | $0.073
Off-Shore Wind | $0.073 | $0.000 | $0.073 | $0.081
Solar | $0.023 | $0.000 | $0.023 | $0.025
Battery | $0.002 | $0.061 | $0.064 | $0.071
Combined Solar/Battery | $0.013 | $0.006 | $0.019 | $0.021
Incremental Payments to Generation = revenue from LMPs and Forecast Energy Requirement
Incremental Payments to Capacity = net option revenue minus holding costs
Detailed calculations are in Appendix A
Note: values may reflect rounding
Revised

## Slide 9: Summary of estimated ESI revenue offsets ORTP Technologies – NEPOOL proposal
Technology Type$0.005 | Incr. Payments to Generation ($/kW-mo.) | Incr. Payments to Capacity ($/kW-mo.) | Total 2020$ ($/kW-mo.) | Total 2020$ ($/kW-mo.)
Combustion Turbine | $0.005 $0.007 | $0.136 | $0.141 $0.143 | $0.156 $0.158
Combined Cycle | $0.155 $0.180 | $0.004 | $0.160 $0.184 | $0.177 $0.203
On-Shore Wind | $0.042 | $0.000 | $0.042 | $0.046
Off-Shore Wind | $0.049 | $0.000 | $0.049 | $0.054
Solar | $0.010 | $0.000 | $0.010 | $0.011
Battery | $0.002 | $0.043 | $0.044 | $0.049
Combined Solar/Battery | $0.008 | $0.014 | $0.022 | $0.024
Incremental Payments to Generation = revenue from LMPs and Forecast Energy Requirement
Incremental Payments to Capacity = net option revenue minus holding costs
Detailed calculations are in Appendix B
Note: values may reflect rounding
Revised

## Slide 10: Stakeholder Questions
Responses to stakeholder questions from the August 11-13, 2020 Markets Committee
Level of excess (LOE) adjustment
Energy Security Improvements

## Slide 11: Won’t the lumpiness of new entry prohibit the system from ever being at criteria, which will also impact E&AS revenues?
The Forward Capacity Market allows for entry of resources even if it will exceed net ICR (“lumpy” resources)
Stakeholder concern: The excess supply depresses E&AS prices, precluding the unit from earning E&AS revenues at criteria
A simple example to illustrate this concern is provided next, where the system is never at or below net ICR
  Each time the system would otherwise have a net ICR deficit, a “lumpy” new resource enters the market
  Example assumes infinite new supply that is willing to enter at Net CONE

## Slide 12: A numerical example was provided to demonstrate the impact of lumpy new entry
When there is a projected deficit in Net ICR before new entry (CCPs 1, 3), new entry is assumed to occur
  New resource size (360 MW) exceeds the net ICR deficit before new entry
In this example, the system is persistently long
  Better than 1-in-10 reliability
However, assuming the E&AS revenue offsets would be lower under a system with excess supply, Net CONE is not high enough to provide the appropriate reliability
CCP | Load Growth MW | Net ICR Excess (Deficit) MW, before new entry | New Entry MW | Excess (Deficit) Supply MW
1 | 0 | -100 | 360 | 260
2 | 150 | 110 | 0 | 110
3 | 150 | -40 | 350 | 310
4 | 150 | 160 | 0 | 160

## Slide 13: The example assumptions do not account for the entirety of revenues
The assumption that Net CONE is sufficient to incent entry requires that the participant expects average E&AS revenues consistent with a system at criterion
  In this example, new entrants would expect average E&AS revenues that are less than those when the system is at criteria
  As a result, the new entrants in this example would not expect to recover Gross CONE, and as a result, we would not expect to see the new entry assumed in this example
To recover Gross CONE, entrants must instead expect that they will receive average capacity revenues of Net CONE over the life of the resource and average energy and ancillary service revenues commensurate with those when the system is at criterion

## Slide 14: There appears to be inconsistency in dual fuel dispatch when determining ESI revenue impacts vs. estimating E&AS offsets. Is an adjustment needed to account for this?
Specifically, the ESI Impact Analysis assumes that fossil units can be run economically on oil, while the Net CONE and ORTP dispatch models do not include any economic dispatch on oil.
The ESI Impact Analysis model does contain scenarios where dual-fuel units were dispatched on oil
  Dispatch on oil occurred in winter scenarios under both ESI and current market rules, at almost the same frequency
Therefore, dispatch on oil vs. gas isn’t a significant factor in determining the unit’s incremental revenues from ESI, relative to under current market rules
  No adjustment is considered necessary

## Slide 15: Proposed Tariff Revisions

## Slide 16: Three sets of Tariff redlines have been provided
As discussed previously, E&AS revenue offsets and the Performance Payment Rate have been calculated for three scenarios:
  ESI market changes filed by ISO and the sunset of FRM
  ESI market changes filed by NEPOOL and the sunset of FRM
  Without ESI and with the continuation of FRM
Excerpts of the Tariff red-lines are replicated in Appendix C
  Tariff redlines are identical other than the Net CONE, ORTP, and PPR numerical values

## Slide 17: The Tariff definition for Net CONE will be clarified to reflect actual calculations
Current definition does not clearly reflect that E&AS revenues are calculated reflecting the system at long-term equilibrium
The definition does not capture the methodology used to calculate Net CONE
  Discounted cash flow over the investment time frame
  Updated language more accurately describes the Net CONE calculation
Net CONE is an estimate of the Cost of New Entry, net of the first-year non-capacity market revenues, for a reference technology resource type and is intended to equal the amount of capacity revenue the reference technology resource would require, in its first year of operation, to be economically viable given reasonable expectations of the first year energy and ancillary services revenues, and projected revenue for subsequent years under long-term equilibrium conditions.

## Slide 18: A new defined term – Offer Review Trigger Prices – will be added
Used extensively throughout section III.13 and III.A as a defined term
Conforming change
Offer Review Trigger Prices are the prices specified in Section III.A.21.1 of Market Rule 1 associated with the submission of New Capacity Offers in the Forward Capacity Auction.

## Slide 19: Minor revisions are being made to the interim update process
Net CONE and ORTP values are updated in between major recalculations to reflect changes in various indices
Tariff revisions reflect recommended changes in the indices and approach
  Generally minor
Details and support for the modifications will be addressed by Concentric Energy Advisors

## Slide 20: Summary of Proposed Tariff Changes Definitions
Tariff Section | Description of Change
I.2.2 – Net CONE | Update existing definition to more clearly reflect calculation of Net CONE
I.2.2 – Offer Review Trigger Prices | New defined term

## Slide 21: Summary of Proposed Tariff Changes CONE and Net CONE
Tariff Section | Description of Change
III.13.2.4 Forward Capacity Auction Starting Price and the Cost of New Entry | Update CONE and Net CONE values for the Capacity Commitment Period beginning June 1, 2025 Note the next CONE and Net CONE recalculation will be for the Capacity Commitment Period beginning June 1, 2028

## Slide 22: Summary of Proposed Tariff Changes ORTPs
Tariff Section | Description of Change
III.A.21.1.1 Offer Review Trigger Prices for the Forward Capacity Auction | Update ORTP values for the Capacity Commitment Period beginning June 1, 2025 Add Battery as a new technology for Generating Capacity Resources Add On-Peak Solar and Solar + Battery as new technologies for Demand Capacity Resources Remove the Load Management ORTP categories for Demand Capacity Resources – Residential Combine the Demand Capacity Resources - Commercial and Industrial and Demand Capacity Resources – Residential into one Demand Capacity Resources category

## Slide 23: Summary of Proposed Tariff Changes ORTPs
Tariff Section | Description of Change
III.A.21.2 (e)(1) | Note that capital costs will be updated based on changes in the Bureau of Labor Statistics Producer Price Index for Machinery and Equipment: General Purpose Machinery and Equipment index Remove the table of indices used to update individual line items for capital costs in the capital budgeting model
III.A.21.2 (e)(2) | Remove the table of indices used to update individual line items for fixed operating and maintenance costs in the capital budgeting model Modify the description to reflect the single index to be used to update capital costs
III.A.21.2 (e)(3) | Include ESI revenue offsets in the E&AS revenues update Change the dates of the indices from the CCP beginning June 1, 2021, to the months of the commitment period to which the values will apply

## Slide 24: Summary of Proposed Tariff Changes ORTPs
Tariff Section | Description of Change
III.A.21.2 (e)(4) | Revise to indicate the average of the MA Class 1 REC prices for the most recent five-year vintages will be used
III.A.21.2 (e)(5) | New section noting that bonus tax depreciation will be reduced each year by 20% starting with the Capacity Commitment Period beginning on June 1, 2026

## Slide 25: Conclusion
E&AS revenue offsets will be calculated to reflect both current and proposed (future) market conditions in CCP16, including:
  Revenue impacts from ESI, both as proposed by ISO and as proposed by NEPOOL
  With and without estimated Forward Reserve Market revenue due to the proposed sunset of the Forward Reserve Market
The definition for Net CONE will be modified to more clearly reflect the calculation, and a new defined term for Offer Review Trigger Prices will be added
Tariff revisions will:
  Support the new values for CONE, Net CONE , and ORTPs
  Reflect changes in the methodology for updating Net CONE and ORTP values in periods between major recalculations

## Slide 26: Stakeholder Schedule
Stakeholder Committee and Date | Scheduled Project Milestone
Markets Committee June 10, 2020 | Review initial projections of potential revenue offsets associated with FRM sunset
Markets Committee July 14-16, 2020 | Review initial projections of potential revenue offsets associated with ESI and initial discussion of proposed level of excess adjustment methodology
Markets Committee August 11-13, 2020 | Review modeling the system at equilibrium for the Net Cost of New Entry Continued discussion of revenue offsets
Markets Committee September 8-10, 2020 | Updated values for Energy Security Improvement revenue impacts Proposed Tariff revisions
Markets Committee October 6-7, 2020 | Final review and MC vote on FCM parameter updates
Participants Committee November 5, 2020 | PC vote
December 2020 | FERC Filing

## Slide 28: Acronyms Used in this Presentation
CCP = Capacity Commitment Period
CPP = Capacity Performance Payment
CONE = Cost of New Entry
E&AS = Energy & Ancillary Services
ESI = Energy Security Improvements
FCM = Forward Capacity Market
FRM = Forward Reserve Market
ICR = Installed Capacity Requirement
LMP = Locational Marginal Price
LOE = Level of Excess
MRI = Marginal Reliability Impact
NICR = Net Installed Capacity Requirement
ORTP = Offer Review Trigger Price
PPR = Performance Payment Rate

## Slide 29: Appendix A
Incremental Energy Security Improvements revenue offsets for the Net CONE and ORTP modeled technologies
ISO proposal

## Slide 30: Incremental ESI revenue offsets Net CONE Technologies – ISO Proposal
Description | Combustion Turbine | Combined Cycle | Aeroderivative
Nameplate Capacity (MW) | 376.0 | 557.0 | 98.0
Winter Dispatch Capacity (MW) | 394.1 | 584.6 | 110.7
Summer Dispatch Capacity (MW) | 363.8 | 539.4 | 89.1
Incremental Payments for Energy |  |  | 
Winter: Weighted Final Value ($/MWh) | -$1.79 | $0.58 | -$1.79
Day-Ahead Generation (MWh) | 23,255 42,831 | 641,420 800,109 | 3,874 8,967
Weighted Incremental Payments ($, 3-Month) | -$41,576 -$76,574 | $375,227 $468,060 | -$6,926 -$16,031
Non-Winter: Weighted Final Value ($/MWh) | -$8.27 | $0.52 | -$8.27
Day-Ahead Generation (MWh) | 71,141 91,181 | 2,323,855 2,596,066 | 12,262 16,436
Weighted Incremental Payments ($, 9-Month) | -$588,272 -$753,985 | $1,211,659 $1,353,590 | -$101,396 -$135,911
Combined Weighted Incremental Payments for Energy ($, 12-Month) | -629,848 -$830,559 | $1,586,887 $1,821,650 | -$108,322 -$151,942
Combined Weighted Incremental Payments for Energy ($/kW-mo.) | -$0.140 -$0.184 | $0.237 $0.273 | -$0.092 -$0.129
Incremental Payments for Options |  |  | 
Winter: Weighted Payments ($/MW, 3-Month) | $2,730 | $0 | $2,730
Weighted Incremental Payments ($, 3-Month) | $1,075,778 | $0 | $302,179
Non-Winter: Weighted Payments ($/MW, 9-Month) | $4,353 | $8 | $4,353
Weighted Incremental Payments ($, 9-Month) | $1,583,656 | $4,277 | $387,861
Combined Weighted Payments for Options ($, 12-Month) | $2,659,434 | $4,277 | $690,039
Combined Weighted Payments for Options ($/kW-mo.) | $0.589 | $0.001 | $0.587
Change In Total Payments ($, 12-Month) | $2,029,586 $1,828,875 | $1,591,163 $1,825,926 | $581,718 $538,097
Change In Total Payments ($/kW-mo.) | $0.450 $0.405 | $0.238 $0.273 | $0.495 $0.458
Revised

## Slide 31: Incremental ESI revenue offsets ORTPs Technologies – ISO Proposal
Description | Combustion Turbine | Combined Cycle | On-Shore Wind | Offshore Wind
Nominal Capacity (MW) | 376.0 | 557.0 | 82.5 | 800.0
Winter Dispatch Capacity (MW) | 394.1 | 584.6 | 82.5 | 800.0
Summer Dispatch Capacity (MW) | 363.8 | 539.4 | 82.5 | 800.0
Incremental Payments to Generation |  |  |  | 
Winter: Weighted Final Value ($/MWh) | $0.27 | $0.42 | $0.22 | $0.34
Day-Ahead Generation (MWh) | 17,080 34,028 | 595,581 711,558 | 52,419 | 498,922
Weighted Incremental Payments ($, 3-Month) | $4,574 $9,112 | $252,745 $301,962 | $11,334 | $167,846
Non-Winter: Weighted Final Value ($/MWh) | $0.87 | $0.71 | $0.48 | $0.42
Day-Ahead Generation (MWh) | 51,801 70,499 | 2,203,254 2,533,853 | 112,658 | 1,246,771
Weighted Incremental Payments ($, 9-Month) | $45,007 $61,252 | $1,567,952 $1,803,224 | $54,403 | $528,211
Combined Weighted Incremental Payments ($, 12-Month) | $49,581 $70,365 | $1,820,698 $2,105,186 | $65,737 | $696,057
Combined Weighted Incremental Payments to Generation ($/kW-mo.) | $0.011 $0.016 | $0.272 $0.315 | $0.066 | $0.073
Incremental Payments to Capacity |  |  |  | 
Winter: Weighted Payments ($/MW, 3-Month) | $1,178 | $0 | $0 | $0
Weighted Incremental Payments ($, 3-Month) | $464,316 | $0 | $0 | $0
Non-Winter: Weighted Payments ($/MW, 9-Month) | $2,571 | $184 | $0 | $0
Weighted Incremental Payments ($, 9-Month) | $935,432 | $99,499 | $0 | $0
Combined Weighted Payments to Capacity ($, 12-Month) | $1,399,748 | $99,499 | $0 | $0
Combined Weighted Payments to Capacity ($/kW-mo.) | $0.310 | $0.015 | $0.000 | $0.000
Change In Total Payments ($, 12-Month) | $1,449,328 $1,470,112 | $1,920,196 $2,204,685 | $65,737 | $696,057
Change In Total Payments ($/kW-mo.) | $0.321 $0.326 | $0.287 $0.330 | $0.066 | $0.073
Revised

## Slide 32: Incremental ESI revenue offsets ORTPs Technologies – ISO Proposal (cont.)
Description | Solar | Battery | Combined Solar/Battery
Nominal Capacity (MW) | 20.0 | 150.0 | 10.0
Winter Dispatch Capacity (MW) | 20.0 | 150.0 | 10.0
Summer Dispatch Capacity (MW) | 20.0 | 150.0 | 10.0
Incremental Payments to Generation |  |  | 
Winter: Weighted Final Value ($/MWh) | $0.05 | $0.27 | $0.16
Day-Ahead Generation (MWh) | 2,336 | 7,014 | 518
Weighted Incremental Payments ($, 3-Month) | $123 | $1,864 | $83
Non-Winter: Weighted Final Value ($/MWh) | $0.41 | $0.54 | $0.47
Day-Ahead Generation (MWh) | 13,603 | 4,270 | 3,197
Weighted Incremental Payments ($, 9-Month) | $5,510 | $2,298 | $1,508
Combined Weighted Incremental Payments to Generation ($, 12-Month) | $5,633 | $4,162 | $1,590
Combined Weighted Incremental Payments to Generation ($/kW-mo.) | $0.023 | $0.002 | $0.013
Incremental Payments to Capacity |  |  | 
Winter: Weighted Payments ($/MW, 3-Month) | $0 | $278 | $28
Weighted Incremental Payments ($, 3-Month) | $0 | $41,714 | $278
Non-Winter: Weighted Payments ($/MW, 9-Month) | $0 | $460 | $46
Weighted Incremental Payments ($, 9-Month) | $0 | $68,979 | $460
Combined Weighted Payments to Capacity ($, 12-Month) | $0 | $110,693 | $738
Combined Weighted Payments to Capacity ($/kW-mo.) | $0.000 | $0.061 | $0.006
Change In Total Payments ($, 12-Month) | $5,633 | $114,855 | $2,328
Change In Total Payments ($/kW-mo.) | $0.023 | $0.064 | $0.019

## Slide 33: Appendix B
Incremental Energy Security Improvements revenue offsets for the Net CONE and ORTP modeled technologies
NEPOOL proposal

## Slide 34: Incremental ESI revenue offsets Net CONE Technologies – NEPOOL Proposal
Description | Combustion Turbine | Combined Cycle | Aeroderivative
Nameplate Capacity (MW) | 376.0 | 557.0 | 98.0
Winter Dispatch Capacity (MW) | 394.1 | 584.6 | 110.7
Summer Dispatch Capacity (MW) | 363.8 | 539.4 | 89.1
Incremental Payments to Generation |  |  | 
Winter: Weighted Final Value ($/MWh) | -$1.91 | $0.48 | -$1.91
Day-Ahead Generation (MWh) | 23,255 42,831 | 641,420 800,109 | 3,874 8,967
Weighted Incremental Payments ($, 3-Month) | -$44,381 -$81,742 | $307,756 $383,896 | -$7,393 -$17,113
Non-Winter: Weighted Final Value ($/MWh) | $4.67 | $0.33 | $4.67
Day-Ahead Generation (MWh) | 71,141 91,181 | 2,323,855 2,596,066 | 12,262 16,436
Weighted Incremental Payments ($, 9-Month) | $332,396 $426,030 | $776,228 $867,154 | $57,292 $76,795
Combined Weighted Incremental Payments to Generation ($, 12-Month) | $288,014 $344,288 | $1,083,985 $1,251,050 | $49,899 $59,682
Combined Weighted Incremental Payments to Generation ($/kW-mo.) | $0.064 $0.076 | $0.162 $0.187 | $0.042 $0.051
Incremental Payments to Capacity |  |  | 
Winter: Weighted Payments ($/MW, 3-Month) | $2,366 | $0 | $2,366
Weighted Incremental Payments ($, 3-Month) | $932,288 | $0 | $261,873
Non-Winter: Weighted Payments ($/MW, 9-Month) | $718 | $2 | $718
Weighted Incremental Payments ($, 9-Month) | $261,213 | $964 | $63,975
Combined Weighted Payments to Capacity ($, 12-Month) | $1,193,501 | $964 | $325,848
Combined Weighted Payments to Capacity ($/kW-mo.) | $0.265 | $0.000 | $0.277
Change In Total Payments ($, 12-Month) | $1,481,515 $1,537,789 | $1,084,949 $1,252,014 | $375,747 $385,530
Change In Total Payments ($/kW-mo.) | $0.328 $0.341 | $0.162 $0.187 | $0.320 $0.328
Revised

## Slide 35: Incremental ESI revenue offsets ORTPs Technologies – NEPOOL Proposal
Description | Combustion Turbine | Combined Cycle | On-shore Wind | Offshore Wind
Nominal Capacity (MW) | 376.0 | 557.0 | 82.5 | 800.0
Winter Dispatch Capacity (MW) | 394.1 | 584.6 | 82.5 | 800.0
Summer Dispatch Capacity (MW) | 363.8 | 539.4 | 82.5 | 800.0
Incremental Payments to Generation |  |  |  | 
Winter: Weighted Final Value ($/MWh) | $0.09 | $0.24 | $0.09 | $0.22
Day-Ahead Generation (MWh) | 17,080 34,028 | 595,581 711,558 | 52,419 | 498,922
Weighted Incremental Payments ($, 3-Month) | $1,454 $2,896 | $143,737 $171,726 | $4,871 | $109,580
Non-Winter: Weighted Final Value ($/MWh) | $0.42 | $0.41 | $0.33 | $0.29
Day-Ahead Generation (MWh) | 51,801 70,499 | 2,203,254 2,533,853 | 112,658 | 1,246,771
Weighted Incremental Payments ($, 9-Month) | $21,842 $29,727 | $895,593 $1,029,977 | $36,703 | $359,774
Combined Weighted Incremental Payments to Generation ($, 12-Month) | $23,296 $32,623 | $1,039,329 $1,201,703 | $41,575 | $469,354
Combined Weighted Incremental Payments to Generation ($/kW-mo.) | $0.005 $0.007 | $0.155 $0.180 | $0.042 | $0.049
Incremental Payments to Capacity |  |  |  | 
Winter: Weighted Payments ($/MW, 3-Month) | $984 | $0 | $0 | $0
Weighted Incremental Payments ($, 3-Month) | $387,977 | $0 | $0 | $0
Non-Winter: Weighted Payments ($/MW, 9-Month) | $615 | $53 | $0 | $0
Weighted Incremental Payments ($, 9-Month) | $223,782 | $28,635 | $0 | $0
Combined Weighted Payments to Capacity ($, 12-Month) | $611,759 | $28,635 | $0 | $0
Combined Weighted Payments to Capacity ($/kW-mo.) | $0.136 | $0.004 | $0.000 | $0.000
Change In Total Payments ($, 12-Month) | $635,055 $644,381 | $1,067,965 $1,230,338 | $41,575 | $469,354
Change In Total Payments ($/kW-mo.) | $0.141 $0.143 | $0.160 $0.184 | $0.042 | $0.049

## Slide 36: Incremental ESI revenue offsets ORTPs Technologies – NEPOOL Proposal (cont.)
Description | Solar | Battery | Combined Solar/Battery
Nominal Capacity (MW) | 20.0 | 150.0 | 10.0
Winter Dispatch Capacity (MW) | 20.0 | 150.0 | 10.0
Summer Dispatch Capacity (MW) | 20.0 | 150.0 | 10.0
Incremental Payments to Generation |  |  | 
Winter: Weighted Final Value ($/MWh) | -$0.05 | $0.20 | $0.08
Day-Ahead Generation (MWh) | 2,336 | 7,014 | 518
Weighted Incremental Payments ($, 3-Month) | -$111 | $1,424 | $40
Non-Winter: Weighted Final Value ($/MWh) | $0.18 | $0.38 | $0.28
Day-Ahead Generation (MWh) | 13,603 | 4,270 | 3,197
Weighted Incremental Payments ($, 9-Month) | $2,442 | $1,633 | $898
Combined Weighted Incremental Payments to Generation ($, 12-Month) | $2,332 | $3,057 | $939
Combined Weighted Incremental Payments to Generation ($/kW-mo.) | $0.010 | $0.002 | $0.008
Incremental Payments to Capacity |  |  | 
Winter: Weighted Payments ($/MW, 3-Month) | $0 | $240 | $80
Weighted Incremental Payments ($, 3-Month) | $0 | $36,000 | $800
Non-Winter: Weighted Payments ($/MW, 9-Month) | $0 | $270 | $90
Weighted Incremental Payments ($, 9-Month) | $0 | $40,500 | $900
Combined Weighted Payments to Capacity ($, 12-Month) | $0 | $76,500 | $1,700
Combined Weighted Payments to Capacity ($/kW-mo.) | $0.000 | $0.043 | $0.014
Change In Total Payments ($, 12-Month) | $2,332 | $79,557 | $2,639
Change In Total Payments ($/kW-mo.) | $0.010 | $0.044 | $0.022