## Slide 1
September 8 - 10, 2020 | MC TELECONFERENCE
Deborah Cooke
413.540.4488 | dcooke@iso-ne.com
Stakeholder questions
Parameter input assumptions and updated values
Tariff language revisions
Cost of New Entry,
Offer Review Trigger Prices, and
Performance Payment Rate

## Slide 2
Cost of New Entry, Offer Review Trigger Prices,
And Performance Payment Rate
Proposed Effective Date: June 1, 2025 (CCP 16)
The recalculation of the Cost of New Entry (CONE), Net CONE, and Offer Review Trigger Prices (ORTPs) is being performed for the 2025-2026 Capacity Commitment Period (CCP 16)
The Performance Payment Rate (PPR) is being updated concurrently for CCP 16
  This rate depends upon the values used to derive the Net CONE
This presentation:
  Responds to stakeholder questions from the September MC meeting
  Provides updated revenue offsets associated with Energy Security Improvements (ESI)
  Provides the updated Performance Payment Rate
  Provides a summary of Tariff revisions since the September MC meeting
WMPP IDs: 139 & 144

## Slide 3: E&AS revenue offsets, Net CONE values, ORTPs, and PPR values are provided for several future scenarios
E&AS revenues are provided both with and without ESI revenue adjustments (for ISO’s and NEPOOL’s ESI alternatives)
  ESI revenue adjustments reflect the most recent Concentric Energy Advisors (CEA) dispatch models
E&AS revenues are provided both with and without Forward Reserve Market revenues (accounting for ESI)
  To account for the proposed sunset of the Forward Reserve Market beginning in CCP 16, contingent on ESI
This results in three sets of potential Net CONE, ORTP, and PPR values and Tariff redlines (see slide 22)

## Slide 4: Stakeholder Questions
Responses to stakeholder questions from September 8-10, 2020 Markets Committee meeting

## Slide 5: Why are the ESI incremental payments for options similar for the Simple Cycle and Aeroderivative units?
Stakeholder concern: Shouldn’t these revenue offsets differ as the Aero has a much lower start cost in the CEA dispatch model than the Simple Cycle?
Response:
Total payments to energy differ based on different day-ahead energy dispatch awards but net payments from options are essentially the same on a $/MW (of seasonal capability) basis
  Startup costs do not (directly) affect energy option awards under ESI
In the AGI’s ESI Impact Analysis model, start-up costs are included as part of a day-ahead energy option risk premium that accounts for, among other things, “operational and intertemporal factors that prevent physical energy inventory from perfectly hedging financial risks”1
  The risks are based on general resource category (e.g., Combustion Turbine) and fuel type (e.g., Dual Fuel)
  This indirect role of startup costs leads to similar ESI incremental option revenue for the SC and Aero units
1 Energy Security Impact Assessment, Appendix C, Day-Ahead Energy Options Offers, page 126

## Slide 6: Are the ESI incremental payments for options for the dual-fuel unit too high?
Stakeholder concern: The “incremental payments to options” revenues reflect the ability of the dual-fuel unit to offer ancillary services more frequently than a gas-only unit. Yet the unit is not dispatched economically on oil in the CEA model. Should the estimated ESI revenues be adjusted?
Response:
CEA dispatch models assumed that air emissions constraints preclude a unit’s economic dispatch on oil under the modeled dispatch conditions
  Air permits issued in Connecticut generally limit dispatch on oil to Energy Emergency conditions declared by ISO-NE; certain interruptions in natural gas supply; and performance and maintenance testing
The underlying assumption is that a resource that clears day-ahead ESI options will run on gas unless one of those air permit operating conditions existed
  The dual-fuel capability reduces the risk of writing options
  ESI participation will not modify the frequency with which the unit physically operates on gas vs. oil in real-time

## Slide 7: When calculating the level of excess adjustment, was the entry of the Net CONE resource included?
Stakeholder concern: Entry of the “lumpy” new resource will depress energy prices going forward, which should be reflected in the E&AS revenues.
Response:
As noted at the August MC, Net CONE is designed to incent new entry when the system is at criterion
And as discussed at the September MC, E&AS revenues must be consistent with a system at criterion
  Lower E&AS revenues offsets associated with a system with excess supply are not high enough to incent new entry
Energy prices used in the dispatch models were based on calendar years 2017, 2018, and 2019 – when the system had excess capacity
Therefore, to calculate the level of excess adjustment resources were removed from the supply stack to bring the system to equilibrium

## Slide 8: Can the ISO consider applying a different index to FRM revenues in the interim update process?
Stakeholder concern: The power-gas forward price indices used to update the E&AS revenue offsets do not correlate well with FRM market prices.
Response:
Indices used to update the E&AS revenues are the Henry Hub natural gas futures, Algonquin Citygates Basis natural gas futures, and Massachusetts Hub On-Peak electricity prices
In general, FRM revenues should reflect the opportunity costs of missed energy profits (from offering above the FRM Threshold Price) and real-time reserve payments
These opportunity costs are correlated with gas and electricity prices
Therefore, it is reasonable for these revenues to be updated consistent with other E&AS revenue offsets

## Slide 9: Was the original Performance Payment Rate based on inputs from an ORTP value?
Stakeholder Concern: Is it appropriate to use the Net CONE reference technology in the current update of the PPR?
Response:
Yes. The current PPR was set in 2013 based on the ORTP value for a Combined Cycle.
  In 2013, that ORTP value was used only because it was the most current at that time (Net CONE and ORTP were not updated concurrently then)
The ISO explained (in detail) in its 2014 PFP filings* that the PPR is appropriately based on estimated Gross CONE less E&AS Offsets for a new entrant, which are the estimates applied in this PPR update
* See ER14-1050-001, Performance Incentives Changes, January 17, 2014; and ER14-2419-0000, Compliance Filing Docket ER14-1050-000, dated July 14, 2014

## Slide 10: What is the source of the reference technology performance factor used in the Performance Payment Rate?
Stakeholder Concern: Does/should this value reflect past performance issues?
Response:
The reference unit is a GE 7HA.02 simple cycle turbine
The 0.98 performance factor is sourced from General Electric, and is based on performance of this technology over the past 12 months
  This is expected to be indicative of 7HA.02 performance going forward
  Issues occurred with the turbines when they were new but have since been addressed by GE and are not expected to reoccur

## Slide 11: Performance Payment Rate
Updated values reflecting latest CEA Net CONE value

## Slide 12: Changes to the Simple Cycle technology dispatch required updates to the Performance Payment Rate
Intraday gas premiums were applied in the offer data used for the dispatch of the simple cycle technology
  As noted in the CEA memo dated September 29, 2020
The resulting change impacted energy and ancillary services revenue offsets (including ESI revenue offsets), requiring a change to the PPR

## Slide 13: Inputs to the PPR formula reflect the proposed Net CONE unit (Combustion Turbine)
The PPR formula* is:
* Details for deriving the PPR formula can be found in the FCM Performance Incentives – Performance Payment Rate memo dated September 3, 2013
Input Description | Value | Description and source of data
Gross CONE | $ /kW-mo. | Estimated cost of new entry for the combustion turbine
E&AS Revenues | $ /kW-mo. | Energy and ancillary services revenues (excluding Capacity Performance Payments) for the combustion turbine
Hours | 15.3 | Expected annual scarcity hours (‘at criteria’) from the ISO scarcity hours review
Actual Performance | 0.98 | Average performance for the GE 7HA.02 combustion turbine
From September presentation

## Slide 14: PPR values reflecting latest updated inputs to the Net CONE discounted cash flow model
Notes: Values are in 2025$ and are based on qualified capacity. See Appendix C for installed capacity values
Intermediate values may reflect rounding
 | Scenario |  | 
Input | ESI (ISO), no FRM | ESI (NEPOOL) no FRM | FRM (no ESI)
Gross CONE ($/kW-mo. of Qualified Capacity) | $11.77 | $11.77 | $11.77
E&AS Revenues: |  |  | 
Energy & Reserves ($/kW-mo. of QC) | $1.67 | $1.67 | $2.86
Scarcity ($/kW-mo. of QC) | $1.08 | $1.08 | $1.08
ESI Revenues ($/kW-mo. of QC) | $0.56 | $0.37 | $0.00
Total E&AS Revenue ($/kW-mo. of QC) | $3.31 | $3.12 | $3.94
Gross CONE – E&AS ($/kW-mo. of QC) | $8.46 | $8.65 | $7.83
Hours (per year) | 15.3 | 15.3 | 15.3
Actual Performance (per MW) | 0.98 | 0.98 | 0.98
PPR ($/MWh) | $6,773 | $6,927 | $6,266

## Slide 15: Energy Security Improvements
Incremental revenue offsets for the Net CONE and ORTP modeled technologies
ISO proposal
NEPOOL proposal

## Slide 16: ESI revenues are estimated and incorporated in the Net CONE and ORTP calculations
As discussed in past Markets Committee meetings, ESI revenue offsets are estimated under both the ISO and NEPOOL filed proposals
  Both scenarios assume the sunset of the Forward Reserve Market
Modifications to the dispatch models for the simple cycle, aeroderivative, and battery technologies resulted in updates to the ESI revenue offsets
  Simple cycle and aeroderivative technologies: to reflect intraday gas premiums
  Battery technology: updated available energy amounts at point of interconnection
From September presentation

## Slide 17: Updated Summary of estimated ESI revenue offsets Net CONE Technologies – ISO Proposal
Technology Type | Incr. Payments to Energy ($/kW-mo.) | Incr. Payments to Options ($/kW-mo.) | Total 2020$ ($/kW-mo.) | Total 2025$ ($/kW-mo.)
Combustion Turbine | $-0.104 | $0.589 | $0.486 | $0.537
Aeroderivative | $-0.072 | $0.587 | $0.514 | $0.567
Incremental Payments to Energy = revenue from LMPs and Forecast Energy Requirement
Incremental Payments to Options = net option revenue minus holding costs
Detailed calculations for all Net CONE technologies are in Appendix B
Note: values may reflect rounding
Revised from September presentation

## Slide 18: Updated Summary of estimated ESI revenue offsets Net CONE Technologies – NEPOOL Proposal
Technology Type | Incr. Payments to Energy ($/kW-mo.) | Incr. Payments to Options ($/kW-mo.) | Total 2020$ ($/kW-mo.) | Total 2025$ ($/kW-mo.)
Combustion Turbine | $0.055 | $0.265 | $0.319 | $0.352
Aeroderivative | $0.039 | $0.277 | $0.316 | $0.349
Incremental Payments to Energy = revenue from LMPs and Forecast Energy Requirement
Incremental Payments to Options = net option revenue minus holding costs Detailed calculations for all Net CONE technologies are in Appendix C
Note: values may reflect rounding
Revised from September presentation

## Slide 19: Updated Summary of estimated ESI revenue offsets ORTP Technologies - ISO proposal
Technology Type | Incr. Payments to Energy ($/kW-mo.) | Incr. Payments to Options ($/kW-mo.) | Total 2020$ ($/kW-mo.) | Total 2025$ ($/kW-mo.)
Combustion Turbine | $0.008 | $0.310 | $0.318 | $0.351
Battery | $0.002 | $0.061 | $0.064 | $0.071
Incremental Payments to Energy = revenue from LMPs and Forecast Energy Requirement
Incremental Payments to Options = net option revenue minus holding costs Detailed calculations for all ORTP technologies are in Appendix B
Note: values may reflect rounding
Revised from September presentation

## Slide 20: Updated Summary of estimated ESI revenue offsets ORTP Technologies – NEPOOL proposal
Technology Type | Incr. Payments to Energy ($/kW-mo.) | Incr. Payments to Options ($/kW-mo.) | Total 2020$ ($/kW-mo.) | Total 2025$ ($/kW-mo.)
Combustion Turbine | $0.004 | $0.136 | $0.139 | $0.153
Battery | $0.002 | $0.043 | $0.044 | $0.049
Incremental Payments to Energy = revenue from LMPs and Forecast Energy Requirement
Incremental Payments to Options = net option revenue minus holding costs Detailed calculations for all ORTP technologies are in Appendix C
Note: values may reflect rounding
Revised from September presentation

## Slide 21: Proposed Tariff Revisions
Review of Tariff revisions since the September 8-10 MC Meeting

## Slide 22: Three sets of Tariff redlines are provided
As discussed previously, E&AS revenue offsets and the Performance Payment Rate have been calculated for three scenarios:
  ESI market changes filed by ISO and the sunset of FRM
  ESI market changes filed by NEPOOL and the sunset of FRM
  Without ESI and with the continuation of FRM
Excerpts of the Tariff red-lines are replicated in Appendix C
  Tariff redlines are identical other than the Net CONE, ORTP, and PPR numerical values
From September presentation

## Slide 23: Revisions to the Net CONE and ORTP calculations from September require Tariff updates
Modifications to the E&AS for the simple cycle technology required a change to the PPR
  Impacted Net CONE and ORTPs values
Changes to the battery dispatch also impacted the ORTP for that technology
Performance payments for intermittent power resource technologies also were adjusted to reflect expected capability during scarcity hours
Index used in the interim update of ORTPs for renewable technologies was revised
Following slides detail Tariff language revisions from September
  Summary of all Tariff revisions included in Appendix D

## Slide 24: Summary of Proposed Tariff Changes Performance Payment Rate
Tariff Section | Reason for Change
III.13.7.2.5 Capacity Performance Payment Rate | Indicate that the Capacity Performance Payment Rate of $5,455/MWh applies to the Capacity Commitment Period beginning on June 1, 2024 and ending on May 31, 2025 Update the Capacity Performance Payment Rate for the Capacity Commitment Periods beginning on or after June 1, 2025 to $6,773/MWh
Note: Three sets of Tariff redlines have been provided reflecting the Performance Payment Rate under the three scenarios. The value above reflects the ESI market changes filed by ISO and the sunset of FRM.
Revised from September presentation

## Slide 25: Summary of Proposed Tariff Changes ORTPs
Tariff Section | Description of Change
III.A.21.1.1 Offer Review Trigger Prices for the Forward Capacity Auction | Update ORTP values for the Capacity Commitment Period beginning June 1, 2025 Add Battery as a new technology for Generating Capacity Resources Add Solar (in the NEPOOL ESI case only) as a new technology for Generating Capacity Resources Add On-Peak Solar and Solar + Battery as new technologies for Demand Capacity Resources Remove the Load Management ORTP categories for Demand Capacity Resources – Residential Combine the Demand Capacity Resources - Commercial and Industrial and Demand Capacity Resources – Residential into one Demand Capacity Resources category
Revised from September presentation

## Slide 26: Summary of Proposed Tariff Changes ORTPs
Tariff Section | Description of Change
III.A.21.2 (e)(1) | Capital costs for non-renewable technologies will be updated based on changes in the Bureau of Labor Statistics Producer Price Index for Machinery and Equipment: General Purpose Machinery and Equipment index Capital costs for renewable technologies will be updated based on changes in the Bureau of Labor Statistics Producer Price Index for Goods Less Foods and Energy – Private Capital Equipment index Remove the table of indices used to update individual line items for capital costs in the capital budgeting model
Revised from September presentation

## Slide 27: Conclusion
E&AS revenue offsets are calculated to reflect both current and proposed (future) market conditions in CCP16, including:
  Revenue impacts from ESI, both as proposed by ISO and as proposed by NEPOOL
  With and without estimated Forward Reserve Market revenue due to the proposed sunset of the Forward Reserve Market
The definition for Net CONE is being modified to more clearly reflect the calculation, and a new defined term for Offer Review Trigger Prices is being added
The updated PPR value will be effective beginning June 1, 2025 (CCP16)
  The value is based upon the Combustion Turbine technology recommended for Net CONE
Tariff revisions will:
  Support the new values for CONE, Net CONE, ORTPs and PPR
  Reflect changes in the methodology for updating Net CONE and ORTP values in periods between major recalculations

## Slide 28: Stakeholder Schedule
Stakeholder Committee and Date | Scheduled Project Milestone
Markets Committee June 10, 2020 | Review initial projections of potential revenue offsets associated with FRM sunset
Markets Committee July 14-16, 2020 | Review initial projections of potential revenue offsets associated with ESI and initial discussion of proposed level of excess adjustment methodology PPR introduction and overview
Markets Committee August 11-13, 2020 | Review modeling the system at equilibrium for the Net Cost of New Entry Continued discussion of revenue offsets Review PPR inputs and calculation Discuss the indicative PPR
Markets Committee September 8-10, 2020 | Updated values for Energy Security Improvement revenue impacts Review the indicative PPR Discuss proposed Tariff revisions
Markets Committee October 6-8, 2020 | Updated values for Energy Security Improvement revenue impacts Review the indicative PPR Discuss proposed Tariff revisions

## Slide 29: Stakeholder Schedule
Stakeholder Committee and Date | Scheduled Project Milestone
Markets Committee November 9-10, 2020 | MC vote on FCM parameter updates and associated amendments
Participants Committee December 3, 2020 | PC vote on FCM parameter updates and associated amendments
December 2020 | FERC Filing

## Slide 31: Acronyms Used in this Presentation
CCP = Capacity Commitment Period
CONE = Cost of New Entry
E&AS = Energy & Ancillary Services
ESI = Energy Security Improvements
FCM = Forward Capacity Market
FRM = Forward Reserve Market
LMP = Locational Marginal Price
LOE = Level of Excess
MRI = Marginal Reliability Impact
NICR = Net Installed Capacity Requirement
ORTP = Offer Review Trigger Price
PPR = Performance Payment Rate
QC = Qualified Capacity

## Slide 32: Appendix A
Installed vs. Qualified Capacity Values for Net CONE technology
Used in PPR calculation

## Slide 33: Installed and Qualified Capacity values of PPR inputs
Notes: Values are in 2025$
Intermediate values may reflect rounding
 | Scenario |  |  |  |  | 
Input | ESI (ISO), no FRM |  | ESI (NEPOOL) no FRM |  | FRM (no ESI) | 
 | Installed | Qualified | Installed | Qualified | Installed | Qualified
Gross CONE ($/kW-mo.) | $11.30 | $11.77 | $11.30 | $11.77 | $11.30 | $11.77
E&AS Revenues: |  |  |  |  |  | 
Energy & Reserves ($/kW-mo.) | $1.60 | $1.67 | $1.60 | $1.67 | $2.75 | $2.86
Scarcity ($/kW-mo.) | $1.04 | $1.08 | $1.04 | $1.08 | $1.04 | $1.08
ESI Revenues ($/kW-mo.) | $0.54 | $0.56 | $0.35 | $0.37 | $0.00 | $0.00
Total E&AS Revenue ($/kW-mo.) | $3.18 | $3.31 | $2.99 | $3.12 | $3.79 | $3.94
Gross CONE – E&AS ($/kW-mo.) | $8.12 | $8.46 | $8.31 | $8.65 | $7.52 | $7.83

## Slide 34: Appendix B
Incremental Energy Security Improvements revenue offsets for the Net CONE and ORTP modeled technologies
ISO proposal

## Slide 35: Incremental ESI revenue offsets Net CONE Technologies – ISO Proposal

## Slide 36: Incremental ESI revenue offsets ORTPs Technologies – ISO Proposal

## Slide 37: Incremental ESI revenue offsets ORTPs Technologies – ISO Proposal (cont.)

## Slide 38: Appendix C
Incremental Energy Security Improvements revenue offsets for the Net CONE and ORTP modeled technologies
NEPOOL proposal

## Slide 39: Incremental ESI revenue offsets Net CONE Technologies – NEPOOL Proposal

## Slide 40: Incremental ESI revenue offsets ORTPs Technologies – NEPOOL Proposal

## Slide 41: Incremental ESI revenue offsets ORTPs Technologies – NEPOOL Proposal (cont.)

## Slide 42: Appendix D
Tariff Revisions for CONE, Net CONE, PPR, and ORTPs

## Slide 43: Summary of Proposed Tariff Changes Definitions
Tariff Section | Description of Change
I.2.2 – Net CONE | Update existing definition to more clearly reflect calculation of Net CONE
I.2.2 – Offer Review Trigger Prices | New defined term
From September presentation

## Slide 44: Summary of Proposed Tariff Changes CONE and Net CONE
Tariff Section | Description of Change
III.13.2.4 Forward Capacity Auction Starting Price and the Cost of New Entry | Update CONE and Net CONE values for the Capacity Commitment Period beginning June 1, 2025 Note the next CONE and Net CONE recalculation will be for the Capacity Commitment Period beginning June 1, 2028
From September presentation

## Slide 45: Summary of Proposed Tariff Changes Performance Payment Rate
Tariff Section | Reason for Change
III.13.7.2.5 Capacity Performance Payment Rate | Indicate that the Capacity Performance Payment Rate of $5,455/MWh applies to the Capacity Commitment Period beginning on June 1, 2024 and ending on May 31, 2025 Update the Capacity Performance Payment Rate for the Capacity Commitment Periods beginning on or after June 1, 2025 to $6,773/MWh
Note: Three sets of Tariff redlines have been provided reflecting the Performance Payment Rate under the three scenarios. The value above reflects the ESI market changes filed by ISO and the sunset of FRM.
Revised from September presentation

## Slide 46: Summary of Proposed Tariff Changes ORTPs
Tariff Section | Description of Change
III.A.21.1.1 Offer Review Trigger Prices for the Forward Capacity Auction | Update ORTP values for the Capacity Commitment Period beginning June 1, 2025 Add Battery as a new technology for Generating Capacity Resources Add Solar (in the NEPOOL ESI case only) as a new technology for Generating Capacity Resources Add On-Peak Solar and Solar + Battery as new technologies for Demand Capacity Resources Remove the Load Management ORTP categories for Demand Capacity Resources – Residential Combine the Demand Capacity Resources - Commercial and Industrial and Demand Capacity Resources – Residential into one Demand Capacity Resources category
Revised from September presentation

## Slide 47: Summary of Proposed Tariff Changes ORTPs
Tariff Section | Description of Change
III.A.21.2 (e)(1) | Capital costs for non-renewable technologies will be updated based on changes in the Bureau of Labor Statistics Producer Price Index for Machinery and Equipment: General Purpose Machinery and Equipment index Capital costs for renewable technologies will be updated based on changes in the Bureau of Labor Statistics Producer Price Index for Goods Less Foods and Energy – Private Capital Equipment index Remove the table of indices used to update individual line items for capital costs in the capital budgeting model
III.A.21.2 (e)(2) | Remove the table of indices used to update individual line items for fixed operating and maintenance costs in the capital budgeting model Modify the description to reflect the single index to be used to update capital costs
III.A.21.2 (e)(3) | Include ESI revenue offsets in the E&AS revenues update Change the dates of the indices from the CCP beginning June 1, 2021, to the months of the commitment period to which the values will apply
Revised from September presentation

## Slide 48: Summary of Proposed Tariff Changes ORTPs
Tariff Section | Description of Change
III.A.21.2 (e)(4) | Revise to indicate the average of the MA Class 1 REC prices for the most recent five-year vintages will be used
III.A.21.2 (e)(5) | New section noting that bonus tax depreciation will be reduced each year by 20% starting with the Capacity Commitment Period beginning on June 1, 2026
From September presentation