## Slide 1
February 24, 2021 | MC TELECONFERENCE
Deborah Cooke
413.540.4488 | dcooke@iso-ne.com
Revisions to address new Federal Investment Tax Credit provisions for certain technologies
Offer Review Trigger Prices

## Slide 2
Offer Review Trigger Prices
Proposed Effective Date: June 1, 2025 (CCP 16)
The recalculation of the Offer Review Trigger Prices (ORTPs) was recently performed for the 2025-2026 Capacity Commitment Period (CCP 16)
  Voted at the December 3, 2020 Participants Committee
On December 27, 2020, the Consolidated Appropriations Act was signed into law, which included significant changes to Investment Tax Credit (ITC) provisions for certain renewable technologies
  These changes impacted certain ORTP values as discussed by Concentric Energy Advisors at the February 9-10, 2021 MC meeting
This presentation provides:
  Responses to stakeholder questions from the February 9-10, 2021 Markets Committee
  Updated modeling assumptions for the ORTP calculation for the co-located resource, in response to stakeholder concerns
  A summary of Tariff revisions relating to the revised ORTPs
WMPP ID: 139

## Slide 3: Background
Under the revised tax provisions, the ITC was revised for off-shore wind and solar technologies
The ORTP values for these technologies were revisited to account for the tax credit changes
  Revised values calculated by Concentric Energy Advisors
Additionally, the Production Tax Credit was extended one year for on-shore wind units
  60% for projects beginning construction by 12/31/2021
  Does not impact the on-shore wind ORTP of $0.000
From February 9-10 presentation

## Slide 4: Stakeholder Questions
Responses to stakeholder questions from the February 9-10, 2021 Markets Committee meeting:
Revenue assumptions in the calculation of the co-located technology ORTP
Impact of jump ball on retirement bids

## Slide 5: Updated revenue modeling for the co-located ORTP to reflect additional ITC considerations
Stakeholder Concern: It is reasonable that the co-located solar and battery will be “decoupled” after 5 years, when the ITC benefit expires. Prior modeling reflected continued coupled operation; this underestimates revenues, and results in a higher ORTP.
Response:
The ITC is applied to installed costs, which are depreciated using the 5-year MACRS schedule, so that after 5 years the installed costs are fully depreciated and no further benefit is available
Therefore, we agree decoupled operation after 5 years is a reasonable assumption, and the revenues for the co-located ORTP have been revised (continued on next slide)

## Slide 6: Stand-alone solar and battery dispatch models were used to estimate revenues for decoupled operation in years 6-20
The market-participation assumptions and calculations for the stand-alone solar and battery were applied
  Adjusted for unit size and locational energy prices
The other detailed assumptions (for years 6-20) are the same as those reviewed with the Markets Committee previously:
  Solar: price-taker (intermittent power), using hourly generation profile of stand-alone solar
  Battery: decoupled asset provides energy, regulation, real-time ten-minute spinning reserves, and participates in Forward Reserve Market
    Energy: 89% of capacity (accounting for regulation)
    Regulation: based on 11% of capacity
    Real-time reserves: 5 MW ten-minute spinning reserves designation
    Forward Reserve Market: 5 MW ten-minute non-spinning reserve

## Slide 7: Stand-alone solar and battery dispatch models were used to estimate revenues for decoupled operation in Years 6-20 (cont.)
Revenues from co-located operation and stand-alone operation used in revised discounted cash flow model
  5 years co-located revenues + 15 years stand-alone revenues
Two additional dispatch models (reflecting Year 6-20 revenues for the solar and battery) have been updated accordingly
  These are provided with the Market Committee materials
Updated discounted cash flow model has also been provided
  Also available with the Markets Committee materials
Revised co-located solar + battery ORTP = $6.964 / kW-mo.

## Slide 8: The co-located solar + battery ORTP is more accurate than a weighted average ORTP
The co-located solar + battery ORTP reflects a “bottom’s up” calculation specific to this configuration
The following important factors contribute to the differences between the co-located solar + battery ORTP and a weighted average of the separate solar ORTP and battery ORTP values
  First five years, the solar output is used first to charge the battery
    Solar generation occurs during the day when prices are higher
    Battery discharges when prices are lower
    Unit does not provide reserves or regulation
  Fixed and installed costs reflect the two different technology types

## Slide 9: Impact on retirement bids from varying ORTP values
Concern: The final ORTP categories and values may impact participation in FCA 16, which in turn will inform retirement and permanent de-list bid submittals. A FERC ruling may not be received prior to retirement and permanent de-list bid window close. Will participants be able to modify bids after the window closes?
Retirement and Permanent De-List Bids window: March 5 – March 12, 2021
Response:
Participants may submit up to three different prices (with supporting documentation) in their Retirement De-List Bids, Permanent De-List Bids, and Test Price submissions, based on the following cases:
  ISO’s proposed ORTP values (IMM base case assumption)
  NEPOOL proposed ORTP values (Alternative case assumption)
  ORTP filing rejected (Rejections assumption)
See “Impact of Offer Review Trigger Price Jump Ball Filing on Retirement Bids” memo from Internal Market Monitor, provided with Markets Committee materials

## Slide 10: Show of Interest ORTP categories for FCA 16 participation will reflect ISO proposed groups
Stakeholder question: New capacity resources indicate an ORTP category when submitting the Show of Interest (SOI). FERC ruling may not be received prior to SOI window close; what categories will appear? What if a technology specific category is not available?
SOI window: April 9 – April 23, 2021
Response:
The ORTP technology categories proposed by the ISO will be reflected in the Forward Capacity Tracking System
If a specific technology category is not available, participants can select “All other technology types”
  ISO will re-categorize the technology category as applicable based upon the FERC ruling on the jump-ball ORTP filing (expected in May, prior to the new capacity submission window)

## Slide 11: Summary of Revisions and Proposed Tariff Revisions

## Slide 12: Summary of updates and revisions to the Tariff
Two new Generating Capacity Resource ORTP categories will be created
  Solar
  Combined Photovoltaic Solar and Energy Storage Device – Lithium Ion Battery
As ORTPs for specific combinations of technology types are specified in the Tariff, a modification is being made to clarify that the weighted average ORTP calculation will only be used for combinations of technology types without a specific ORTP
New language added to specify the ITC values used in the FCA 17 and FCA 18 interim updates
  Reflect scheduled changes of ITC values in recently enacted provisions

## Slide 13: Summary of Proposed Tariff Changes ORTPs
Tariff Section | Description of Change
III.A.21.1.1 Offer Review Trigger Prices for the Forward Capacity Auction | Add ORTP values for the Capacity Commitment Period beginning June 1, 2025 for the following Generating Capacity Resource technologies: Solar: $0.000 Combined Photovoltaic and Lithium Ion Battery: $6.964 Clarify that the weighted average calculation is used only when an ORTP for the combination of technology types is not specified
III.A.21.1.2 (e)(6) | New section detailing the ITC values to be used for solar and combined photovoltaic/lithium-ion battery technologies for the FCA 17 and FCA 18 interim updates
III.A.21.2 (c) | Clarify that the weighted average calculation is used only when an ORTP for the combination of technology types is not specified
Revised from February 9-10 presentation

## Slide 14: Conclusion
Two new ORTP technologies will be included for Generating Capacity Resources, reflecting revised ITC values available due to recent changes in tax law
  Solar
  Co-located solar/lithium-ion battery
Revenues for the co-located ORTP value now reflect decoupled operation after 5 years
Tariff revisions:
  Reflect the amended ORTP values
  Clarify that a weighted average of individual technology ORTPs will be applied when an ORTP is not specified for the combination of technology types
  Address the ITC values that will be used in the interim updates of solar and combined solar/battery technology projects participating in FCAs 17 and 18

## Slide 15: Stakeholder Schedule
Stakeholder Committee and Date | Scheduled Project Milestone
Markets Committee February 9-10, 2021 | Review impacts of revised ITC on ORTP values Discuss proposed Tariff revisions
Markets Committee February 24, 2021 | MC vote on updated ORTP values and Tariff language reflecting impacts of the modified Investment Tax Credit
Participants Committee March 4, 2021 | PC vote on amended ORTP values and Tariff language to reflect impacts of the modified Investment Tax Credit
March 2021 | FERC Filing

## Slide 17: Acronyms Used in this Presentation
CCP = Capacity Commitment Period
FCA = Forward Capacity Auction
ITC = Investment Tax Credit
ORTP = Offer Review Trigger Price
PV = Photovoltaic
SOI = Show of Interest