## Slide 1
Joint Meeting NEPOOL Markets and Reliability Committees July 12, 2022 | Meredith, NH
Feng Zhao
Technical Manager fzhao@iso-ne.com 413-540-4561
MRI-based conceptual design
Resource Capacity Accreditation in the Forward Capacity Market

## Slide 2
WMPP ID:
157
Proposed Effective Date: FCA 19
The Resource Capacity Accreditation (RCA) project proposes improvements to ISO-NE’s accreditation processes in the Forward Capacity Market (FCM) to further support a reliable, clean-energy transition by implementing methodologies that will more appropriately accredit resource contributions to resource adequacy as the resource mix transforms
Resource Capacity Accreditation in the Forward Capacity Market

## Slide 3
WMPP ID:
157
Proposed Effective Date: FCA 19
The ISO has made a commitment to FERC to file proposed improvements in time for FCA 19
This presentation describes the ISO-NE’s conceptual design on capacity accreditation and will be discussed over the next few joint MC/RC meetings
  Graphs and numerical examples do not reflect estimates of the impacts of potential reforms but are merely stylized examples
Resource Capacity Accreditation in the Forward Capacity Market

## Slide 4
WMPP ID:
157
Proposed Effective Date: FCA 19
Today’s discussion will focus on:
Review opportunities for improvements (slides 6-8)
Overview of the RCA improvements (slides 10-14)
The MRI concept (slides 16-22)
Introduce adequacy assessment model enhancements (slides 24-29)
Introduce the MRI-based accreditation and market design (slides 31-50)
Conclusion (slides 52-53)
Stakeholder schedule (slides 55-58)
Resource Capacity Accreditation in the Forward Capacity Market

## Slide 5: Opportunities for improvements to current capacity accreditation process

## Slide 6: Forward Capacity Market Design Objectives
Design Objective 1: To ensure the system has sufficient resources to meet the region’s one-day-in-ten reliability requirement, where “sufficient” is defined as having enough resources that can perform as expected in the right locations
Design Objective 2: To ensure that Design Objective 1 is achieved in a cost-effective manner
Design Objectives 1 and 2 are the current objectives for the FCM, which the RCA reforms must also meet
From June 7-8 presentation

## Slide 7: Clean Energy Transition Objective
The region is moving swiftly toward a decarbonized grid. There are opportunities to implement improvements now to better facilitate reliability and market efficiency in the future
The ISO is proposing improvements to our current resource adequacy assessment and accreditation processes to better ensure that the FCM continues to meet Design Objectives 1 and 2 as well as the objective to actualize our vision for the evolving clean-energy resource mix

## Slide 8: Opportunities for Improvement
Opportunity #1: Current capacity accreditation framework can be improved to reflect different resource contributions toward resource adequacy. These adjustments will better yield accredited capacity that is substitutable between resources, which is beneficial as unique resource types enter the market
Opportunity #2: Current resource adequacy assessment process can be improved to better reflect resources’ expected performance and reliability contributions as the resource mix changes

## Slide 9: Overview of Conceptual design for RCA Improvements

## Slide 10: Our Responses to Improvement Opportunities
RCA Improvement #1: Accredit all resources based on their marginal reliability impact to yield substitutability between resources (Response to Opportunity 1)
RCA Improvement #2: Improve resource adequacy assessment models for more accurate resource MRI and accredited values (Response to Opportunity 2)

## Slide 11: RCA Improvement #1: MRI-based Accreditation
Each resource’s Marginal Reliability Impact (MRI), in hours/year, is evaluated prior to FCA
Each resource’s relative Marginal Reliability Impact (rMRI) to perfect capacity is a ratio (no units): rMRI = MRI/MRIperfect
Each resource’s new accredited capacity, Qualified MRI Capacity (QMRIC), is calculated in MW: QMRIC = QC  rMRI
Qualified Capacity (QC)
Qualified MRIC (QMRIC)
 rMRI

## Slide 12: RCA Improvement #1: MRI-based Accreditation cont.
Two obligations are produced by market clearing
  The new Capacity Supply Obligation (CSO) or cleared MRIC, and
  Effective CSO (ECSO), the physical obligation associated with the CSO
QC
CSO
FCM Clearing
Physical & market obligations
Current:
QMRIC
CSO
 rMRI
 1/rMRI
QC
ECSO
FCM Clearing
Physical obligation
Market obligation
New:

## Slide 13: RCA Improvement #2: Adequacy Assessment Model Improvement
Resource MRI values are calculated using GE-MARS, a resource adequacy assessment tool
  MRIs are affected by the resource adequacy assessment models of load and resources in GE-MARS
Resource adequacy assessment models are enhanced to allow more accurate calculation of resources’ MRI values

## Slide 14: Connection to Previous FCM Improvements
RCA introduces the MRI concept to supply-side of FCM
QC accreditation
MRI-based Demand Curve
MRI-based Resource Accreditation
Zonal Demand Curves

## Slide 15: The MRI concept

## Slide 16: Introduction
As noted in June, the ISO has been finding the marginal approach most compelling
Conceptually marginal ELCC and MRI-based accreditation yield the same results under the same reliability metric
The ISO already implemented the MRI concept in its capacity demand curves (demand-side)
This presentation introduces the MRI concept to resource capacity accreditation (supply-side)

## Slide 17: MRI Concept
The MRI of a resource reflects how a small change to the resource capacity (C) would affect the system reliability in terms of changing Expected Unserved Energy (EUE):
MRI =  EUE / C
The MRI concept has been applied in the ISO’s demand MRI curves, e.g., system demand MRI is calculated as the EUE change with respect to a small change of the system capacity
MW
MWh/year
hours/year

## Slide 18: Choice of EUE in MRI Definition
EUE is selected as the reliability metric in MRI definition since
  it fits in the economic framework of FCM
  it is consistent with capacity demand curve construct
  it supports more accurate calculation of marginal values
Both LOLE and EUE are used by the ISO to achieve a reliable system in a cost-effective manner

## Slide 19: Interpretation of MRI
MRI generally reflects a resource’s expected availability (in hours/year) during reliability hours in the adequacy assessment, e.g., a resource would have
  zero MRI value if it is always unavailable
  MRI value equal to the expected number of reliability hours if it is always available at full capacity like the perfect capacity
Reliability hours are times in adequacy assessments that additional capacity would improve system reliability

## Slide 20: Factors Affecting a Resource’s MRI Value
MRI can be affected by the resource’s own characteristics, e.g., outage rate
MRI can also be affected by the resource mix, e.g., penetration of the resource’s class
  MRI is evaluated for a given resource mix
  Note that ELCC methods also rely on the resource mix assumption

## Slide 21: Resource Mix for MRI Calculation
The calculation of ICR and demand curves assumes the resource mix of the at-criterion ICR base case
We propose to use consistent resource mix assumptions for resource accreditation (supply side), ICR and demand curves (demand side)

## Slide 22: Key Takeaways on MRI Concept
MRI captures a resource’s marginal contribution to the system reliability measured in EUE
MRI generally reflects a resource’s expected availability (in hours/year) when capacity is needed by the system
MRI is affected not only by the resource’s own characteristics, but also by the resource mix
Resource MRIs and demand MRIs are calculated based on consistent resource mix assumptions from the ICR base case

## Slide 23: Enhance adequacy assessment models
For More Accurate MRI Calculation

## Slide 24: MRI Calculation
In the last section, we showed that MRI is the EUE change in response to a small change to the resource’s capacity
In this section, we show how the MRI values can be calculated using the resource adequacy assessment tool and how the accuracy of these values can be improved

## Slide 25: Resource Adequacy Assessment (RAA) for MRI Calculation
Resource Adequacy Assessment (RAA), illustrated in the below figure, plays a critical role in calculating ICR and capacity demand curves
  In RAA, resource parameters such as Qualified Capacities (QCs) are inputs for evaluating the system reliability indices including EUE
MRIs can be calculated by varying (increasing) a resource’s QC and evaluating the EUE change
Probabilistic simulations
Resource parameters (QC, EFORd, etc.)
Reliability metrics (EUE, LOLE, etc.)
RAA models (load and resources)
Adequacy assessment tool (GE-MARS)
Load parameters

## Slide 26: Enhance Load and Resource Models for Capacity Accreditation
The load and resource models used in the adequacy assessment tool (GE-MARS) affect the accuracy of adequacy analysis result and MRI values
We propose to enhance load and resource models for more accurate calculation of resource MRIs, within the limit of technical feasibility, software capability, and project schedule
Details about the model enhancements will be discussed in the coming months and our conceptual direction follows in the next slides

## Slide 27: Potential RAA Model Enhancements
Potential RAA load enhancements
  The current load shape can be enhanced with a composite load shape reflecting representative summer and winter weather conditions for reliability studies
Potential RAA resource model enhancements
  Intermittent resources such as solar and wind currently modeled as perfect capacity can be enhanced with hourly profiles
  Energy storage resources currently modeled as thermal units can be enhanced with energy storage models
  Gas-only resources currently modeled with unlimited gas supply can be enhanced with gas supply constraint

## Slide 28: Calculating MRIs for Each Resource
We propose to directly calculate individual resource MRIs, rather than calculating class values and allocating those class values to individual resources
  This allows more accurate characterization of a resource’s reliability contribution than the class approach
Resources not modeled in resource adequacy assessment can be assigned the corresponding class MRI of similar resources
  Class MRI is the QC-weighted average of all resource MRIs in the class

## Slide 29: Key Takeaways on Adequacy Assessment Model Improvement
MRIs can be calculated by perturbing resource QCs using the resource adequacy assessment tool
Load and resource models in the resource adequacy assessment tool can be improved for more accurate calculation of resource MRI

## Slide 30: The MRI-based capacity accreditation
rMRI and Accredited Capacity

## Slide 31: Using MRI for Capacity Accreditation
The prior sections demonstrated how the MRI is defined and calculated
In this section, we show how the MRI values can be used to translate resource QC into the new accredited value for the resource

## Slide 32: Relative MRI
By comparing each resource’s marginal reliability impact to that of the perfect capacity’s MRIperfect, the resource’s relative Marginal Reliability Impact (rMRI) is represented by
  rMRI of the perfect capacity is 1 (100%)
  rMRI allows each resource’s capacity to be expressed in the same unit of perfect capacity, allowing for substitutability between resources

## Slide 33: Illustrative Example for rMRI
With rMRI, each MW of a resource’s QC can be translated to an equivalent amount of perfect capacity
Suppose resource A has MRIA = 4.5 hrs/yr, resource B has MRIB = 2.5 hrs/yr and MRIperfect = 5 hrs/yr; Then rMRIA = 4.5/5 = 90% and rMRIB = 2.5/5 =50%
  The translation of 1 MW of resource QC to perfect capacity is illustrated below
Resource B
1 MW
Resource A
1 MW
0.9 MW
0.5 MW
1 MW
Perfect Capacity
1 MW
 rMRIA
 rMRIB
 rMRIperfect
QC:
QMRIC:

## Slide 34: Capacity Accreditation with rMRI
Since each 1 MW of a resource’s QC can be translated (in terms of marginal reliability impact) to (1rMRI) MW of perfect capacity, the new accredited capacity for the resource, i.e., Qualified MRI Capacity (QMRIC), is (QCrMRI) in MW
  QMRIC reflects the total marginal reliability impact of the resource
With rMRI, QC of each resource can be translated to the equivalent QMRIC amount of perfect capacity:
QC
QMRIC
 rMRI

## Slide 35: Illustrative example for QMRIC
Suppose that resource A with QCA = 100 MW and rMRIA = 90%, resource B with QCB =100 MW and rMRIB = 50%
Resource QC can be translated to perfect capacity as follows: A
100 MW
100 MW
B
A
A
90 MW
B
50 MW
QMRIC (in perfect capacity)
QC

## Slide 36: Substitutability Under MRI-based Accreditation
Substitutability means that a MW of accredited capacity from different resources has the same reliability impact
Substitutability allows the direct comparison of costs ($/kW-month) of different resources with disparate characteristics, improving market transparency and economic efficiency
Each MW of QMRIC or accredited capacity from different resources has the same reliability impact as a MW of the perfect capacity
MRIC is substitutable under MRI-based accreditation

## Slide 37: MRI-based Accreditation Applies to All Resources
The MRI-based accreditation applies to all resources
  The same accreditation method for all resources facilitates market transparency and fairness
Applying different capacity accreditations for different resources distorts the substitutability between resources and harms economic efficiency

## Slide 38: Key Takeaways on rMRI and QMRIC
rMRI represents the relative MRI of a resource compared to the perfect capacity
With rMRI, resources’ QC can be converted to QMRIC that represents the amount of equivalent perfect capacity
QMRIC allows substitutability between resources
The MRI-based accreditation applies to all resources

## Slide 39: The MRI-based capacity accreditation
Physical and Market Quantities

## Slide 40: Capacity Quantities Under The New Design
In the last section, we reviewed how resources are accredited based on their MRIs
In this section, we discuss the physical and market quantities under the new accreditation

## Slide 41: QC and QMRIC Under the New Accreditation
QMRIC replaces QC as the new market quantity
  QMRIC of a resource reflects the maximum market quantity that the resource can bid into the market
  Resources submit QMRIC-based capacity offers in Descending Clock Auction (DCA)
  QC remains a physical quantity
QMRIC is the QC adjusted by its marginal reliability impact, i.e.,
QC (physical)
QMRIC (market)
 rMRI

## Slide 42: ECSO and CSO Under the New Accreditation
FCM clears the QMRIC-based market offers
  The cleared QMRIC MW is called Capacity Supply Obligation (CSO)
  FCM clearing price is the price for the cleared market quantity, CSO
  The physical quantity corresponding to CSO is named Effective CSO (ECSO)
Relationship between ECSO and CSO: ECSO = CSO  1/rMRI
CSO (market)
ECSO (physical)
 1/rMRI

## Slide 43: Use of Physical and Market Quantities in FCM
QC or ECSO is used for processes that require a physical quantity
QMRIC or CSO is used for processes that require a market quantity
QMRIC
CSO
 rMRI
 1/rMRI
QC
ECSO
FCM Clearing
Physical
Market

## Slide 44: Key Takeaways on Capacity Quantities
The MRI-based accreditation yields new market quantities of QMRIC and CSO
QC and ECSO are used as the physical quantity in certain FCM processes
With rMRI, physical quantities can be translated to market quantities and vice versa

## Slide 45: The MRI-based capacity accreditation
Capacity Requirement and Demand Curves

## Slide 46: Capacity Requirement and Demand Curves
We have covered how the MRI concept is used to drive the proposed resource accreditation
In this section, we explain conceptually how the capacity requirement and demand curves can be formed under the MRI-based accreditation

## Slide 47: Capacity Requirement in MRIC
Net Installed Capacity Requirement (Net ICR) represents the amount of total QC (physical quantity) that the system needs to meet the 1-in-10 criterion, for the resource mix in the ICR base case
With rMRI, Net ICR in QC MW can be translated to the new capacity requirement based upon MRIC (market quantity) as illustrated below
Base case resource mix
Net ICR
MRIC Requirement
Perfect capacity

## Slide 48: Substitutability Between Supply and Demand Capacities in MRIC
With rMRIs translating both resource QCs and Net ICR to the perfect capacity equivalents, a MW of MRIC supplied by each resource satisfies a MW of MRIC requirement from a reliability contribution perspective
Supply and demand capacities under the MRI-based design are substitutable

## Slide 49: Capacity Demand Curves in MRIC
The current capacity demand curves represent the marginal costs of reliability as a function of total system or zonal QC
For any point on a capacity demand curve, the QC MW associated with the point can be translated to the QMRIC MW with the rMRI of the corresponding system or zone
  Capacity demand curves established using QC can be translated to demand curves based upon MRIC

## Slide 50: Key Takeaways on Capacity Requirement and MRIC Demand Curves
The current QC-based Net ICR and demand curves can be translated to MRIC-based capacity requirement and demand curves
By applying the MRI concept and consistent resource mix assumptions to both supply and demand sides of FCM, the supply and demand will align properly

## Slide 51: Conclusion

## Slide 52: Key Takeaways
MRI is a marginal concept with EUE being the reliability metric
The MRI-based capacity accreditation yields resource substitutability
Adequacy assessment model enhancements can improve the accuracy of MRI calculation
More design details will be presented in coming months

## Slide 53: RCA Project in FCM Evolution
QC accreditation
MRI concept applied to both supply and demand of FCM
MRI-based Demand Curve
MRI-based RCA
Zonal Demand Curve

## Slide 54: Stakeholder schedule

## Slide 55: Stakeholder Process - Overview
There are several broad phases laid out for this proposal in the stakeholder process:
  Background, Conceptual Design, & Education: June 2022 – October 2022
  Detailed Design: November 2022 – January 2023
  Finalize Design & Review Tariff Language: February 2023 – April 2023
  Voting: May 2023 (Technical Committees) and June 2023 (Participants Committee)
Through at least the conceptual design phase, the content will primarily be delivered during the MC with the RC jointly invited to discuss the RCA proposal
  As needed, additional joint MC/RC meetings would be held during the regularly scheduled RC to continue discussions of material that were not completed during the regular joint MC/RC meeting
Starting likely with the detailed design phase, the MC and RC will meet separately and discuss distinct content under their committee’s purview
  The MC and RC are each invited to continue to participate in each other’s ongoing discussions and review on the RCA proposal
At the next meeting in August, discussions will continue on:
  Average vs. marginal approaches addressing any additional follow-up questions from July
  Further discussion on ISO’s conceptual design

## Slide 56: Stakeholder Schedule – Conceptual Design Phase
AUGUST 2022 |  |  |  |  |  |  |  | Joint Markets and Reliability Committees MC Meeting Dates: August 9-10, 2022 (with joint RC during RCA components) Posting Materials Beginning: August 3, 2022 Topics: Continue discussion of ISO's conceptual design Stakeholders should submit additional clarifying questions on average and marginal approaches or the conceptual design to the MC Secretary by July 22, 2022 Additional Joint Markets and Reliability Committees RC Meeting Dates: August 16-17, 2022 (with joint MC during RCA components) Posting Materials Beginning: August 10, 2022 Topics: As needed, continue discussion of ISO materials from August 9-10 Joint MC/RC meeting on ISO's conceptual design
S | M | T | W | T | F | S |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 |  | 
7 | 8 | 9 | 10 | 11 | 12 | 13 |  | 
14 | 15 | 16 | 17 | 18 | 19 | 20 |  | 
21 | 22 | 23 | 24 | 25 | 26 | 27 |  | 
28 | 29 | 30 | 31 |  |  |  |  | 
JUNE 2022 |  |  |  |  |  |  |  | Joint Markets and Reliability Committees MC Meeting Dates: June 7-8, 2022 (with joint RC during RCA components)(link to materials) Posting Materials Beginning: June 1, 2022 Topics: Review background and discuss opportunities for adjusting the way resources are accredited in the FCM to support a reliable, clean-energy transition
S | M | T | W | T | F | S |  | 
 |  |  | 1 | 2 | 3 | 4 |  | 
5 | 6 | 7 | 8 | 9 | 10 | 11 |  | 
12 | 13 | 14 | 15 | 16 | 17 | 18 |  | 
19 | 20 | 21 | 22 | 23 | 24 | 25 |  | 
26 | 27 | 28 | 29 | 30 |  |  |  | 
JULY 2022 |  |  |  |  |  |  |  | Joint Markets and Reliability Committees MC Meeting Dates: July 12-14, 2022 (with joint RC during RCA components) Posting Materials Beginning: July 6, 2022 Topics: Discussion of ISO's design objectives and conceptual design Stakeholders should submit additional clarifying questions on average and marginal approaches to the MC Secretary by June 24, 2022
S | M | T | W | T | F | S |  | 
 |  |  |  |  | 1 | 2 |  | 
3 | 4 | 5 | 6 | 7 | 8 | 9 |  | 
10 | 11 | 12 | 13 | 14 | 15 | 16 |  | 
17 | 18 | 19 | 20 | 21 | 22 | 23 |  | 
24 | 25 | 26 | 27 | 28 | 29 | 30 |  | 
31 |  |  |  |  |  |  |  | 

## Slide 57: Stakeholder Schedule – Conceptual Design Phase, cont.
SEPTEMBER 2022 |  |  |  |  |  |  |  | Joint Markets and Reliability Committees MC Meeting Dates: September 13-14, 2022 (with joint RC during RCA components) Posting Materials Beginning: September 7, 2022 Topics: Continue discussion of conceptual design and review proposed impact assessment approach Additional Joint Markets and Reliability Committees RC Meeting Date: September 20, 2022 (with joint MC during RCA components) Posting Materials Beginning: September 14, 2022 Topics: As needed, continue discussion of ISO materials from September 13-14 Joint MC/RC on ISO's conceptual design and proposed impact assessment approach
S | M | T | W | T | F | S |  | 
 |  |  |  | 1 | 2 | 3 |  | 
4 | 5 | 6 | 7 | 8 | 9 | 10 |  | 
11 | 12 | 13 | 14 | 15 | 16 | 17 |  | 
18 | 19 | 20 | 21 | 22 | 23 | 24 |  | 
25 | 26 | 27 | 28 | 29 | 30 |  |  | 
OCTOBER 2022 |  |  |  |  |  |  |  | Joint Markets and Reliability Committees MC Meeting Dates: October 12-13, 2022 (with joint RC during RCA components) Posting Materials Beginning: October 5, 2022 Topics: Continue discussion of conceptual design and proposed impact assessment scope and scenarios Additional Joint Markets and Reliability Committees RC Meeting Date: October 18, 2022 (with joint MC during RCA components) Posting Materials Beginning: October 12, 2022 Topics: As needed, continue discussion of ISO materials from October 12-13 Joint MC/RC on ISO's conceptual design and proposed impact assessment scope and scenarios
S | M | T | W | T | F | S |  | 
 |  |  |  |  |  | 1 |  | 
2 | 3 | 4 | 5 | 6 | 7 | 8 |  | 
9 | 10 | 11 | 12 | 13 | 14 | 15 |  | 
16 | 17 | 18 | 19 | 20 | 21 | 22 |  | 
23 | 24 | 25 | 26 | 27 | 28 | 29 |  | 
30 | 31 |  |  |  |  |  |  | 

## Slide 58: Stakeholder Schedule – Detailed Design Phase
NOVEMBER 2022 |  |  |  |  |  |  |  | Markets Committee MC Meeting Dates: November 8-9, 2022 (RC invited to participate in RCA discussions) Posting Materials Beginning: November 2, 2022 Topic: Review detailed design and finalize impact assessment scenarios Reliability Committee RC Meeting Date: November 16, 2022 (MC invited to participate in RCA discussions) Posting Materials Beginning: November 9, 2022 Topic: Review detailed design
S | M | T | W | T | F | S |  | 
 |  | 1 | 2 | 3 | 4 | 5 |  | 
6 | 7 | 8 | 9 | 10 | 11 | 12 |  | 
13 | 14 | 15 | 16 | 17 | 18 | 19 |  | 
20 | 21 | 22 | 23 | 24 | 25 | 26 |  | 
27 | 28 | 29 | 30 |  |  |  |  | 
DECEMBER 2022 |  |  |  |  |  |  |  | Markets Committee MC Meeting Dates: December 6-8, 2022 (RC invited to participate in RCA discussions) Posting Materials Beginning: November 30, 2022 Topic: Continue review of detailed design Reliability Committee RC Meeting Date: December 14, 2022 (MC invited to participate in RCA discussions) Posting Materials Beginning: December 8, 2022 Topic: Continue review of detailed design
S | M | T | W | T | F | S |  | 
 |  |  |  | 1 | 2 | 3 |  | 
4 | 5 | 6 | 7 | 8 | 9 | 10 |  | 
11 | 12 | 13 | 14 | 15 | 16 | 17 |  | 
18 | 19 | 20 | 21 | 22 | 23 | 24 |  | 
25 | 26 | 27 | 28 | 29 | 30 | 31 |  | 
JANUARY 2023 |  |  |  |  |  |  |  | Markets Committee MC Meeting Dates: January, 2023 (RC invited to participate in RCA discussions) Posting Materials Beginning: January, 2023 Topic: Continue review of detailed design. Review initial Impact Assessment results. Stakeholders interested in proposing conceptual amendments should contact the MC secretary for time on the agenda Reliability Committee RC Meeting Date: January, 2023 (MC invited to participate in RCA discussions) Posting Materials Beginning: January, 2023 Topic: Continue review of detailed design. Stakeholders interested in proposing conceptual amendments should contact the RC secretary for time on the agenda
S | M | T | W | T | F | S |  | 
1 | 2 | 3 | 4 | 5 | 6 | 7 |  | 
8 | 9 | 10 | 11 | 12 | 13 | 14 |  | 
15 | 16 | 17 | 18 | 19 | 20 | 21 |  | 
22 | 23 | 24 | 25 | 26 | 27 | 28 |  | 
29 | 30 | 31 |  |  |  |  |  | 
Note: Detailed information will be shared once the dates for the 2023 NEPOOL calendar are established